# Exterior

- Windshield free of cracks

- Body panel colors match

- Magnet adheres to all steel body panels

- Fresh paint job (if yes, it could be to conceal rust)

- Seams where the trunk and hood close are properly aligned

- Seams where doors and fenders meet are properly aligned

- Free of body scratches

- Free of body dents

- Windshields wipers and blades fully functional

- Headlights and directional lights intact and fully functional

# Tires

- Tires are a reputable brand name (Michelin, Bridgestone, Goodyear)

- Tires are all of the same make

- Tires are of free of any cuts, bubbles or cracks

- Tread worn evenly (uneven wear indicates alignment and suspension problems)

- Spare tire, jack and lug wrench on car and fully functional

- Spare tire inflated

# Engine

- Free of fluid or oil leaks

- Oil filler neck not coated with thick, black deposits

- Battery terminals free of corrosion

- Oil dip stick free of dark, black oil

- Free of odors while engine is running

- Exhaust pipe emissions are neither blue (indicates engine burns oil) or black (indicate excessive oil consumption)

# Suspension

- Vehicle rests levelly

- When bouncing the vehicle's corners, no creaking noises are made

- All corners respond the same when bouncing

# Interior

- Seats unworn and free of cracks

- All doors open and close freely

- Trunk opens and closes freely

- Lacks a heavy scent of air freshener (may indicate something is being concealed)

- All gauges work

- No dashboard warning lights remain illuminated

- Stereo works

- Heater works

- Air conditioner works

- Windshield wipers work

- Windshield wiper fluid dispenses properly

- All seats equipped with functional seat belts

- All seats adjust properly

- Power windows operate properly

- Sunroof opens and closes properly (if applicable)

- Car alarm works (if applicable)

- Trunk and driver-side door lock and unlock with key

- Hazard lights function properly

- Headlights, including brights, work properly

# Frame

- Chassis is neither bent nor cracked

- No signs of crumpling or straightening inside the trunk

- Frame holes just inside outer edge clean and free of scratches

# Automatic Transmission

- Transmission fluid looks clean, not dirty or gritty (no indicates possible internal transmission problem)

- Transmission neither slips nor delays when driving

# Manual or Standard Transmission

- Each gear shifts smoothly

- No grinding noises when in reverse

# Brakes

- Vehicle steers straight and does not pull to one side when applying brakes

- Parking brake engages and disengages freely

- No grinding noises when applying

- Wheels do not lock when applying antilock brakes (if applicable)

# Steering

- Vehicle does not drift to one side without prodding

- Vehicle is stable; no shaking or vibrating

- No resistance in the steering wheel when turning

- No clicking or clunking when turning

# Miscellaneous

- Car manual located in the glove compartment

- Instructions included for any accessories

- Service and repair records available

- Owner has title

# Other Insights

- Walk away if the seller objects to your inspection

- Don't feel rushed while inspecting

- Try to get a mechanic to assess checklist results

- Use any flaws against the asking price