|  |  |  |  |  | WI #: | Rev: |  | TYPE: |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | WI-SQC | C |  | QA |
|  |  |  |  |  |  | Work Instruction |
|  | Owner: |  | Title: |  |  |  |  |  |  |
|  | Director of Quality | Supplier Quality Requirements |  |  |  |  |
|  | References: |  |  |  |  |  |  |  |
|  | None |  |  |  |  |  |  |  |  |
|  | Purpose: |  |  |  |  |  |  |  |  |
|  | This document defines specific supplier quality requirements identified on Mason purchase orders. |  |  |
|  | Scope: |  |  |  |  |  |  |  |  |
|  | This document supports QMS, Suppliers, Purchasing, and Supply Chain by establishing quality requirement |
|  | definitions not necessarily established by design engineering drawings. |  |  |  |  |
|  | Definitions: |  |  |  |  |  |  |  |
|  | None |  |  |  |  |  |  |  |  |
|  | Change Record |  |  |  |  |  |  |  |
|  | Revision | Date | Originator | Description of Change |  |  |  |  |
|  | Rev. NC | 07/27/2016 | L. Cioaba | Issued |  |  |  |  |
|  | Rev A | 02/06/2017 | L. Cioaba | Re-identified as WI-SQC |  |  |
|  | Rev B | 01/12/2018 | R. Rickard | Revised content extensively for clarity of intent |
|  |  |  |  | General grammatical revision. Added MRB inclusion to |
|  |  |  |  | QC 2 and inserted clarification, clarified scope in QC 8 & |
|  |  |  |  | QC10, added scope to QC19, referenced QC 8 in QC 25. |
|  |  |  |  | Removed Esterline from text body. Added package |
|  |  |  |  | labeling to QC9. Added designated and approved |
|  | Rev C | 09/24/2019 | R. Rickard | sources to QC25. Added COTS definition to QC3, QC7, |
|  |  |  |  | QC16 and QC19. QC9 removed “Basic” added |
|  |  |  |  | “General”, inserted “Mason Controls”. QC7 added |
|  |  |  |  | “Mason Controls” to clarify PO traceability. QC17: |
|  |  |  |  | removed performance target of 90%, inserted |
|  |  |  |  | performance target as 98%. QC25 updated CFR |
|  |  |  |  | citations. QC3 added FAIR for some COTS items. |

This document contains specific quality requirements for Mason suppliers. All suppliers of items used in the production of deliverable product are required to meet the supplier quality requirements as defined by purchase orders or similar procurement documents. In addition, suppliers to Mason must meet the terms and conditions outlined in Document SOP-060.6. The Head of quality shall maintain this document for the benefit of Mason, Mason Customers, Purchasing, and suppliers.

| Form WI-020-2.3 Rev G | 1 of 15 |
| --- | --- |

Printed copies of this document are not controlled

WI #:	Rev:	TYPE:

WI-SQC	C	QA

Work Instruction

SUPPLIER QUALITY REQUIREMENTS

Table of Contents

Contents

QC 2. NONCONFORMANCE to PO requirements	3

QC 3. FIRST ARTICLE INSPECTION:	5

QC 4. RAW MATERIAL IDENTIFICATION PHYSICAL AND CHEMICAL ANALYSIS	5

QC 5. FUNCTIONAL/ACCEPTANCE TEST REPORTS	5

QC6. PRINTED CIRCUIT BOARDS	6

QC 7. IDENTIFICATION, SERIALIZATION AND TRACEABILITY	6

QC 8. CERTIFICATION OF CONFORMANCE	6

QC 9. PRESERVATION AND PACKAGING - General	7

QC 10. SURVEILLANCE BY MASON AND RIGHT OF ENTRY	8

QC 11. ACCEPTANCE AND SOURCE INSPECTIONS	8

QC 13. SHELF LIFE MATERIALS	9

QC 14. DOCK-TO-STOCK CERTIFICATION PROGRAM	9

QC 15. PARTS OBSOLESCENCE	9

QC 16. TRACEABILITY –MULTI LEVEL	10

QC 17. SUPPLIER PERFORMANCE EVALUATION	11

QC 18. PRESERVATION AND PACKAGING FOR ELECTRONICS	11

QC 19. FLOW DOWN OF MASON SUPPLIER QUALITY REQUIREMENTS	12

QC 20. FLOWDOWN OF ELECTRONICS COMPONENT MGMT. PLAN REQUIREMENT.	12

QC 21. COUNTERFEIT POLICY	12

QC 22. MASON- FURNISHED MATERIALS/EQUIPMENT	13

QC 23. FOREIGN OBJECT DEBRIS or DAMAGE (FOD)	14

QC 24. FACILITY / PROCESS CHANGE	14

QC 25. SPECIAL PROCESS SOURCES REQUIRED	14

QC 26. SPECIALTY METALS SOURCE OF SUPPLY	14

QC 27. DOMESTIC SOURCE OF SUPPLY	15

QC 28. FAA FORM 8130-3	15

QC 29. RECORDS RETENTION	15

| Form WI-020-2.3 Rev G | 2 of 15 |
| --- | --- |

Printed copies of this document are not controlled

| WI #: | Rev: | TYPE: |
| --- | --- | --- |
| WI-SQC | C | QA |

Work Instruction

QC 1. QUALITY SYSTEM REQUIREMENTS

In supplying goods and services Mason Controls acknowledges its obligation to operate ethically and assure compliance with all specified requirements. Suppliers to Mason shall operate ethically and assure compliance with all requirements, while accepting full responsibility for the quality of the goods or services provided. Supplier shall communicate in writing, within 2 working days of discovery of changes to its quality management system, product processes, products, status of any certification, registration, accreditation, management change, or contractual commitment(s).

Quality and Continuous Improvement can be managed effectively only when the company and external providers share a partnership grounded on common objectives and open effective communication. It is required internally and externally that suppliers and Mason foster the communication necessary to build strong partnerships within the supply corps. The primary point of communication for a supplier is the assigned Mason Buyer.

Supplier shall ensure that all persons involved in fulfilling P.O. requirements are aware of their contribution to product or service conformity and safety of product, and the importance of ethical conduct.

Supplier shall maintain a Quality Management System [QMS] verified by an Industry Controlled Other Party (ICOP) accredited registrar to Aerospace Standard SAE AS9100, AS9120, International Standard ISO9001 or equivalent and appropriate standard like ISO/IEC 17025.

Suppliers not certified by an ICOP shall maintain a Quality Management System [QMS] or Quality Inspection System [QIS] approved by Mason. The supplier quality system shall provide a high degree of confidence that all material and services provided conform to all purchase order requirements and Mason quality expectations.

Suppliers, including sub-tier suppliers, providing special processes shall be NADCAP accredited and authorized for each process at the time work is performed.

QC 2. NONCONFORMANCE to PO requirements

Drawing, Documents, Specifications

Applicable drawings and specifications shall be at the latest revision level with the issuing source, unless stated otherwise on PO or current drawings. The supplier must ensure that the latest engineering drawings and specifications are available at the manufacturing, test or inspection location, including applicable previous revisions if Mason’s PO language requires other than the most recent revision(s). Aesthetic acceptance shall be in accord with Mason document WI-100-3, unless otherwise defined on Mason’s purchase order, design drawing, or within a required specification. (WI-100-3 is supplemental to drawing requirements).

MATERIAL REVIEW BOARD AUTHORITY

MRB (Material Review Board) disposition authority, unless otherwise authorized by Mason Supplier Quality Engineering and documented by approval of a Supplier Deviation Request, is not authorized. Suppliers shall consult with Mason Supplier Quality Engineering prior to authorizing sources or processes not defined by the design engineering drawing or purchase order, and document the consultation and authorization by use of the Supplier Deviation Request form.

| Form WI-020-2.3 Rev G | 3 of 15 |
| --- | --- |

Printed copies of this document are not controlled

| WI #: | Rev: | TYPE: |
| --- | --- | --- |
| WI-SQC | C | QA |

Work Instruction

Note: Prime and lower tier subcontractors cannot perform MRB functions on deliverable Mason designed hardware unless given written and specific delegation from Mason. Suppliers of proprietary designed articles and their sub-tier contractors cannot conduct MRB on a discrepancy that results in a departure from the requirements of the controlling Mason drawing or specification.

REPORT OF DISCREPANCY/DEVIATION

The supplier quality system shall ensure effective control of nonconforming material to drawings, specifications or other purchase order requirements. Nonconforming product or materials shall be withheld from shipment unless authorized by the MASON Purchasing Department with an approved Supplier Deviation Request (SDR) or specific purchase order change. The SDR shall describe the nonconformance in detail, the quantity, the cause and corrective action to preclude a recurrence. Acceptance of the SDR by Mason will not affect the supplier’s quality rating for an authorized deviation.

NOTIFICATION OF ESCAPE

At any time a nonconformance affecting delivered product quality or reliability is discovered, Supplier must submit a disclosure report / Notice of Escape to Mason within 24 hours of discovery. A disclosure report, also known as Notice of Escape (NOE) shall include the following information:

- Description of the nonconformance

- Part Number and Traceability information (serial number, lot/batch, date code etc.).

- Delivered quantity

- Containment actions and immediate corrective action proposal.

In addition, the Supplier shall execute and provide a valid root cause and corrective action report as soon as possible or within mutually agreed time frame.

CORRECTIVE ACTION

Non-conforming materials, products, documents, records, or services resulting in a request for corrective action require timely response by the supplier. If Government source inspection is explicitly required by purchase order for any materials, products, or services, the supplier shall promptly notify the Government representative who normally services your facility so that appropriate coordination of corrective action for the Government and Mason can be accomplished by the supplier.

Supplier’s failure to submit acceptable corrective action (CAR) within the time period established on the Corrective Action Request will result in consequences up to and including removal from the Mason Approved Supplier List and subsequent loss of Mason’s future business.

Initial response: Supplier shall respond within 10 business days to a CAR from the date of transmission of the notification. The 10 days is the accumulation of all days used by the supplier for all cycles of the corrective action with the assigned Buyer or Quality Engineer. If more time is required for a thorough investigation, extension on the due date may be requested and submitted to the Supplier Quality Engineer. It is recommended that the supplier submit an initial Corrective Action (C/A) as early as possible to the originator to allow for additional cycle of responses.

Non-responsiveness: If the total days accumulated by the supplier to respond exceeds 25 business days, Mason may put all future PO’s on hold as agreed by assigned Buyer and/or Quality Engineer until satisfactory progress to completion of the CAR becomes clear.

| Form WI-020-2.3 Rev G | 4 of 15 |
| --- | --- |

Printed copies of this document are not controlled

| WI #: | Rev: | TYPE: |
| --- | --- | --- |
| WI-SQC | C | QA |

Work Instruction

Mason’s Buyer, Quality Engineer, or delegate, will notify and return unsatisfactory C/A to the supplier for an additional cycle of corrective action. Supplier may be suspended when the supplier fails to provide adequate corrective action within four cycles (initial submittal plus three additional cycles).

Failure to submit acceptable corrective actions (non-responsive or multiple cycles of corrective actions) is cause for suspension of supplier and may result in a notification of finding against the Suppliers quality management system (QMS) certificate. Mason shall notify the Supplier’s certification body to provide awareness and description of corrective action taken when QMS is accredited to AS/EN/JISQAS9100.

QC 3. FIRST ARTICLE INSPECTION:

Except for items classed as commercial off the shelf items (COTS), the supplier shall perform a First Article Inspection and provide documentation in accordance with specification SAE AS9102 when one of the following applies:

- A first time supply to Mason Controls;

- New product representative of the first production run

- A change in design;

- A change in location, process, inspection method, material, or tooling;

- A lapse in production provided to Mason exceeding two years.

First Article Inspection Report [FAIR] must include all engineering document (blueprint) notes, dimensions, and title block relevant data. The supplier shall use FAIR forms compliant with the current revision of specification SAE AS9102 and include a corresponding itemized (bubbled) drawing. The complete FAIR must accompany the first shipment of part(s). Parts requiring FAIR and received without FAIR compliance are categorized as non-conforming subject to all available remedies including return at supplier’s expense.

Note: (“Commercial off-the-shelf (COTS) item”— Means a commercial item sold in the commercial marketplace; and offered to Mason Controls under a purchase order, contract or subcontract at any tier, without modification in the same form in which it is sold in the commercial marketplace. Certain Mason customers may require FAIR for specific COTS items. Mason will flow down the requirement on purchase order as an additional requirement when applicable.)

QC 4. RAW MATERIAL IDENTIFICATION PHYSICAL AND CHEMICAL ANALYSIS

Chemical and Physical Test Reports are required, signed and dated by manufacturer stating the batch, melt, heat, or lot number, the specification(s) the material was produced under, and traceable to the raw material source. Complete chain of control documentation from the producing source, mill or foundry to Mason shall be included as part of the material certification.

QC 5. FUNCTIONAL/ACCEPTANCE TEST REPORTS

Include with each shipment a legible and reproducible copy of the actual test results identifiable with test parameters of the lot or item acceptance tests required by the applicable specification requirements. Test report shall contain the signature and title of authorized representative for the agency performing the test and must conform to specific requirements.

| Form WI-020-2.3 Rev G | 5 of 15 |
| --- | --- |

Printed copies of this document are not controlled

| WI #: | Rev: | TYPE: |
| --- | --- | --- |
| WI-SQC | C | QA |

Work Instruction

QC6. PRINTED CIRCUIT BOARDS

A potted micro-section reflecting complete manufacturing processes performed must be retained as record for each lot of new date coded boards.

QC 7. IDENTIFICATION, SERIALIZATION AND TRACEABILITY

Except for commercial off the shelf items (COTS) with traceability via manufacturer certificate of conformance or lot code: all items are subject to traceability of the history, application, use and location of the item through the systematic assignment recording and correlation of control identification numbers assigned by MASON.

Supplier shall maintain traceability records of product during all production processes from Supplier raw material receipt to MASON’s delivery. Supplier’s records shall include the material certs from their sub-tiers.

Category I items, traceability by serial number. Each item and associated documentation (test reports, certifications, etc.) shall be identified with the traceability serial number as directed by purchase order. Category II items, traceability by lot number. All items within the lot and all associated documentation (test reports, certifications, etc.) shall be identified with the lot traceability number. Unless otherwise specified, the Mason purchase order number shall be the lot traceability number.

Category III items, castings shall be identified by a permanent part number, configuration, foundry identification, melt number, or by a traceable chemical, physical analysis and heat treat marking. The identification shall remain legible after machining or surface processing.

Note: (“Commercial off-the-shelf (COTS) item”— Means a commercial item sold in the commercial marketplace; and offered to Mason Controls under a purchase order, contract or subcontract at any tier, without modification in the same form in which it is sold in the commercial marketplace.)

QC 8. CERTIFICATION OF CONFORMANCE

Each shipment shall be accompanied by a dated certification, signed or otherwise accepted by a responsible representative of the supplier, stating that the items were produced and conform to the purchase order and each applicable specification. A printed statement like “This certification electronically generated and remains valid without signature” is acceptable if on unsigned certification documents of known origin. Each supplier and supplier sub-tier certification shall clearly and at minimum show:

- Name and address of the Supplier

- Mason’s Purchase Order Number

- Part number, and revision

- Lot number and/or serial numbers

- Quantity Delivered

- Date of Manufacture or Date Code

- Original Component Manufacturer ( as applicable )

- QPL Vendor ID for MIL Spec Parts ( as applicable )

- List of the specifications, including the revision or date.

- Objective evidence of conformance to the purchase order and applicable specifications (Include, at minimum, original materials and special processing certifications)

- Country of Origin shall be specified on the C of C for all parts, assemblies, raw materials used and

processes performed. Country of Origin must be stated as “Country of Origin: Country Name”,

| Form WI-020-2.3 Rev G | 6 of 15 |
| --- | --- |

Printed copies of this document are not controlled

| WI #: | Rev: | TYPE: |
| --- | --- | --- |
| WI-SQC | C | QA |

Work Instruction

“COO: Country Name”, “Processed in: Country Name”, “Made in: Country Name”, or

“Manufactured in: Country Name”.

- Shelf life ending date of items or articles subject to deterioration by time or environment.

MATERIALS FURNISHED by MASON.

The certificate of conformance shall list the MASON material code number assigned to the furnished material.

MILITARY SPEC PARTS require traceability to a QPL/QPD listed vendor.

CALIBRATION SERVICE SUPPLIERS

Calibration suppliers certifies the following: Quality Management Systems conform to ISO/IEC 17025, and methods in accord with ANSI/ NCSL Z540-1, or Z540-3. Calibration standards used shall be traceable to NIST, or obtained from independent reproducible standards derived from acceptable values of natural physical constraints, or derived from the ratio type of self-calibration techniques. Calibration Certificate of Conformance shall record the following minimum for each asset calibrated:

- Asset number: Unique number identifying the individual equipment.

- Date calibration was performed.

- Calibration interval in calendar weeks.

- Date T&ME item will be due for calibration.

- List of standards used to perform calibration.

- Temperature at which calibration was performed.

- Percent humidity at which calibration was performed.

- Calibration facility/source performing calibration.

- Unique number identifying the calibration certificate.

- Calibration technician's identity.

- Total time required to complete calibration process.

- Date and serial number of out-of-tolerance report, if required.

- OUT OF TOLERANCE NOTES/CALIBRATION NOTES: Comments relative to the calibration performed including actual measured value for out of tolerance condition.

- If applicable, the condition of tamper seals when received for calibration.

- Identification and revision of calibration procedure used.

QC 9. PRESERVATION AND PACKAGING - General

Supplier is responsible for assuring that all items are delivered without damage or deterioration and are efficiently and economically packed for the method of transportation and type of handling involved. Buyer may charge Supplier or adjust the price of the goods downwards for any goods damaged or which deteriorate due to improper packing. No charge shall be made for preparation, packing, crating, cartage or shortage unless specifically stated in the purchase order. Each shipping container must be marked to show the Mason purchase order number, Mason part number, and quantity of goods contained therein. Additionally each package of components shall be labeled with part number, quantity, and Mason purchase order and line item.

| Form WI-020-2.3 Rev G | 7 of 15 |
| --- | --- |

Printed copies of this document are not controlled

| WI #: | Rev: | TYPE: |
| --- | --- | --- |
| WI-SQC | C | QA |

Work Instruction

Packaging must be identified with an appropriate Electro Static Discharge sensitive warning marking when appropriate for the contents.

QC 10. SURVEILLANCE BY MASON AND RIGHT OF ENTRY

All items covered by purchase order are subject to surveillance by MASON Supplier Quality, Government and / or Customer Representative(s). Government Representative may be Defense Contract Management Agency [DCMA], Military, or other contracting agency. Mason reserves the right to enter the supplier or sub-tier facility, at any level of the supply chain, at any time during manufacture of product contracted by purchase order with the right also granted to U.S. Government or Mason’s customer representative(s). Surveillance includes review of products and supplier’s systems, procedures and facilities. The supplier shall furnish, at no cost, necessary facilities and equipment, supply data, and perform tests as required by applicable drawings, specifications, and relevant instructions under surveillance of MASON’s Supplier Quality Representative(s).

QC 11. ACCEPTANCE AND SOURCE INSPECTIONS

LOT ACCEPTANCE INSPECTION

When supplier employs sampling inspection, the sampling plan shall preclude acceptance of material, component, part, or assembly lots with samples having known nonconformities by use of a statistically proven sampling inspection plan with number of attribute and variable non-conformances (C) equal to zero (0) for acceptance of each lot of materials, components, parts or assemblies, and 100% lot acceptance inspection for all discrepant characteristics applied to materials, components, parts, assembly, or sub-assembly. Sampling inspections alone are incapable of demonstrating conformance to purchase order requirements and related technical specifications. Suppliers are encouraged to reduce risks by use of efficient processes with appropriate process controls.

Records of all inspection shall be retained per QC 29.

SOURCE INSPECTION

If Purchase Order requires any type of source inspection, acceptance does not relieve supplier of responsibility to provide conforming product to fulfill P.O., specification, and regulatory requirements. The supplier shall furnish, at no cost, acceptable facilities and equipment for the inspection. Evidence of the completed source inspection shall accompany each shipment. Evidence may be by the Inspector stamping and / or signing the supplier’s shipping document.

SOURCE INSPECTION BY MASON - PRIOR TO SHIPMENT

If Purchase Order explicitly requires inspection at the supplier’s facility by Mason prior to shipment notify Mason’s buyer at least forty-eight hours prior to need for source inspection.

SOURCE INSPECTION BY GOVERNMENT- PRIOR TO SHIPMENT

When Purchase Order explicitly requires inspection at the supplier’s facility by Government prior to shipment, promptly furnish a copy of the purchase order to the Government office or representative who normally services your plant so that appropriate planning for Government inspection can be accomplished. All communications with the Government representative shall be copied to the Mason buyer and Mason reserves the right to be present for any source acceptance inspection. Evidence of such inspections shall be indicated on the packing sheet and certifications accompanying each shipment. In

| Form WI-020-2.3 Rev G | 8 of 15 |
| --- | --- |

Printed copies of this document are not controlled

| WI #: | Rev: | TYPE: |
| --- | --- | --- |
| WI-SQC | C | QA |

Work Instruction

the event the government representative or office cannot be located, notify the Mason buyer immediately for assistance.

SOURCE INSPECTION BY MASON’S CUSTOMER - PRIOR TO SHIPMENT

When Purchase Order explicitly requires inspection at the supplier’s facility by Mason’s customer: All supplier communications intended for Mason’s customer shall be concluded by Mason. Mason reserves the right to be present for any source acceptance inspection. Evidence of inspection shall be indicated on the certifications accompanying each shipment. Notify Mason’s buyer at least forty-eight hours prior to need for source inspection.

IN-PROCESS SOURCE INSPECTION

When explicitly required by Purchase Order, supplier’s materials and services are subject to inspection throughout all or portions of the manufacturing and/or testing operations. Mason shall establish mandatory inspection points with supplier. Evidence of completed inspection shall

be indicated on the work instruction for each operation inspected.

QC 12.  SOFTWARE CONTROL.

Except for distributors of commercial off the shelf software items (COTS), suppliers of materials and services utilizing deliverable computer aided design, computer aided manufacturing/processing or computer aided test equipment shall comply with the requirements of DOD-STD-2168 and SAE AS9115. On request, the supplier shall make available for review and approval the quality control procedures for software controls.

QC 13. SHELF LIFE MATERIALS

The material provided must be submitted with at least 75% shelf life remaining or as specified in the body of the PO. A product submitted out of this requirement is non-conforming and cause for rejection.

Material and articles subject to deterioration by time or the environment, shall be identified on the certification. Certification shall show the initiation date and include exceptional conditions under which the material can be stored. Materials should be packaged and labeled in accordance with best commercial practices like ARP5316 section5 or AMS2817.

A Safety Data Sheet [SDS] or equivalent shall be supplied with each shipment for any hazardous material used for completion of this order.

QC 14. DOCK-TO-STOCK CERTIFICATION PROGRAM

This item may be approved for our Dock-To-Stock Certification Program and may, on receipt, go directly from our receiving location to our stock location with little or no incoming inspection. Certification of Conformance, supporting documentation, and other required records shall accompany each delivery and remain traceable to the item. Dock-to-Stock (DTS) items are subject to inspection and/or evaluation for conformity by Mason at any time. Supplier shall be responsible for all cost related to delivery of non-conforming product (Ref. QC 2).

QC 15. PARTS OBSOLESCENCE

When Supplier has knowledge that any hardware item or material to be provided in performance of this purchase order is obsolete, is identified for impending obsolescence, or has an established end of

| Form WI-020-2.3 Rev G | 9 of 15 |
| --- | --- |

Printed copies of this document are not controlled

| WI #: | Rev: | TYPE: |
| --- | --- | --- |
| WI-SQC | C | QA |

Work Instruction

production date, Supplier shall promptly (within five business days) provide notice thereof, including relevant information, to Buyer. Such notice shall include, but not be limited to,

- complete details of which parts are affected;

- date of obsolescence;

- end of production date;

- reason for obsolescence;

- pricing and availability of last-time buy;

- supportability terms (repair and warranty) for last-time buy, and

(7) Supplier’s recommendation for replacement hardware inclusive of known impacts to performance, pricing, availability, and lead time. It shall be the buyer responsibility to research and confirm supplier’s recommendation of replacement to ensure the part will perform as required. Supplier’s initial notifications of obsolescence shall be made through the end of the contracted warranty period for the items provided under this order.

QC 16. TRACEABILITY –MULTI LEVEL

Except for commercial off the shelf (COTS) items, Seller of assembled product or sub-assembly shall maintain traceability records of purchased items and materials utilized in the creation of the assembled product or sub-assembly.

- Seller shall be able to trace back from the shipment to MASON through each level of test and integration back to each lot or serial number (as applicable) of purchased items and materials. Upon request, the Supplier shall provide:

  - The purchased component name

  - Component part number

  - Component revision

  - Reference designator(s)

  - Quantity used per assembly

  - Lot numbers(s) or serial number(s)

  - Certification of Conformance tracing back to the OEM for each component

- Suppliers are required to provide OEM traceability within 48 hours of request. OEM packing slips/documentation that includes component traceability/lot code details are acceptable in lieu of OEM Certification. Component traceability must provide complete chain of custody through delivery to MASON. The Supplier's traceability system must account for all components that require replacement past initial installation. The traceability must be maintained throughout the manufacturing process from work order launch to shipping to MASON. In addition to the component traceability, the Supplier shall, upon request, provide all necessary processing history for the assembly in question. This shall include process name, date and time, location, and operator ID of the personnel performing the process function. Traceability records shall provide adequate documentation to determine the exact configuration of the product shipped to Mason.

- Suppliers (distributors) of commercial off the shelf (COTS) components shall provide only adequate documentation to determine the configuration and source of product shipped to Mason; documentation from the originating manufacturer to the distributor providing component traceability, lot code, and/or OEM certification are acceptable in lieu of assembled component multi-level traceability certification.

| Form WI-020-2.3 Rev G | 10 of 15 |
| --- | --- |

Printed copies of this document are not controlled

| WI #: | Rev: | TYPE: |
| --- | --- | --- |
| WI-SQC | C | QA |

Work Instruction

Note: (“Commercial off-the-shelf (COTS) item”— Means a commercial item sold in the commercial marketplace; and offered to Mason Controls under a purchase order, contract or subcontract at any tier, without modification in the same form in which it is sold in the commercial marketplace.)

QC 17. SUPPLIER PERFORMANCE EVALUATION

Supplier performance is monitored and rated on On-Time Delivery (OTD), Quality Acceptance, and responsiveness and may be weighted. Suppliers are expected to meet performance target of 98%. Supplier CAR may be issued to require improvement action when the overall rating is below 98%

Quality performance & On-time delivery (OTD) are each weighted as 50% of the combined rating. OTD is recognized as the purchase order line quantity for a negotiated on-dock date, +/- 2 days. When parts are received later than the negotiated on-dock date, OTD shall be valued as zero (0) for the line (lot) delivery.

Responsiveness is based on supplier partnering and acceptable reply action to Corrective Action Requests (CAR) with an initial value of zero (0) and can attribute negatively up to -10% of the overall rating at Mason’s sole discretion. (Ref. QC 2)

QC 18. PRESERVATION AND PACKAGING FOR ELECTRONICS

PRESERVATION. Electronic components preservation requirements

(Applies only to manufacturers of circuit card assemblies, integrated electronic assemblies solid-state devices, and Mason proprietary electronic components)

- Supplier shall manufacture products per J-STD-001 and inspect per IPC-610 (current rev) class as directed by drawing. (If the drawing is silent then the Seller shall use Class 3)

- Supplier shall assure that the shipping, handling & storage, manufacture, test, rework and repair processes for products have no short or long term quality or reliability impact.

- Supplier shall maintain an ESD Control Program compliant with an industry recognized standard such as MIL-HDBK-263, ANSI S20.20, or IEC 61340-5-1

- The Seller shall assure that moisture sensitive components are handled and processed in accordance with IPC/JEDEC J-STD-20.

PACKAGING.

All items, components, and parts shall be packaged to prevent moisture damage during handling and transit.

Packaging requirements identified by purchase order, like MIL-STD-129, MIL-STD-130, etc., shall be followed including UID, RFID, etc.

Each commercial shipping container must legibly show:

- Purchase order number,

- Mason’s part number,

- Quantity of goods contained therein.

- Electro Static Discharge (ESD) sensitive warning (when noted on PO or by nature of contents)

- Cautionary Handling Instructions (when applicable)

| Form WI-020-2.3 Rev G | 11 of 15 |
| --- | --- |

Printed copies of this document are not controlled

| WI #: | Rev: | TYPE: |
| --- | --- | --- |
| WI-SQC | C | QA |

Work Instruction

QC 19. FLOW DOWN OF MASON SUPPLIER QUALITY REQUIREMENTS

Except for commercially available off-the-shelf (COTS) items, Supplier shall flow down applicable provisions of Mason’s quality requirements and additional notes on Purchase Order to sub-tiers through all levels of the supply chain. (If supplied drawings identify an original equipment manufacturer (OEM) or other prime contractor, supplier shall ensure special processes are performed in compliance with each OEM or prime contractor’s approved supplier listing.)

Note: (“Commercial off-the-shelf (COTS) item”— Means a commercial item sold in the commercial marketplace; and offered to Mason Controls under a purchase order, contract or subcontract at any tier, without modification in the same form in which it is sold in the commercial marketplace.)

Mason may provide critical information or requirements in the form of a quality alert, even for COTS items. A quality alert provided by Mason is official notification of defects or potential non-conformance

within the supplier’s delivered parts. Mason quality alerts must be flowed to all relevant sub-tiers within the supplier’s supply chain and after a supplier receives a quality alert, the supplier is required to

construct and follow a remediation plan to avoid the described defects in future deliveries (internal /external CAR, etc.).

QC 20. FLOWDOWN OF ELECTRONICS COMPONENT MGMT. PLAN REQUIREMENT.

TBD. Not applicable. (Intended for special application of proprietary electronic components, not for general distribution suppliers)

QC 21. COUNTERFEIT POLICY

Supplier shall preclude introduction of counterfeit product into our supply chain through strict avoidance, mitigation, and disposition processes. Each supplier, distributor, and sub-tier shall practice, and maintain requirements, practices, and methods related to parts management, supplier management, procurement, and response strategies to adhere to the intent and guidelines of counterfeit electronics parts standards SAE AS5553 and SAE AS6174. Supplier shall maintain traceability to the OEM for purchases from original manufacturers or authorized distributors and retain the original purchase orders and other receiving documentation, including Manufacturers’ Certificate of Conformance, for the minimum purchase order required document retention period, (Default is 10 years.)

Supplier warrants that Counterfeit Goods are not contained in Goods delivered to Mason through the implementation of policies that include prevention, detection and risk mitigation methods to protect against the use of Counterfeit Parts. The supplier shall provide an unbroken chain of certification(s), tracing the movement of the parts to Mason from the Original Component Manufacturer (OCM) or mill – full supply chain traceability.

Certificate of conformance or other documentation shall be original and applicable to the delivered material, including:

- Lot and/or date codes on the packaging match the lot and /or dates codes of parts

- No alteration or changes to the documentation.

- Bar coding matches the printed part number (when applicable)

- An unbroken chain of documentation shall include links between documentation and product to C of C number and/or lot batch number date code etc.

| Form WI-020-2.3 Rev G | 12 of 15 |
| --- | --- |

Printed copies of this document are not controlled

| WI #: | Rev: | TYPE: |
| --- | --- | --- |
| WI-SQC | C | QA |

Work Instruction

Suppliers must purchase parts and components directly from the Original Component Manufacturer (OCM) / Original Equipment Manufacturer (OEMs), or an OCM/OEM authorized distributor. Procurement through an independent distributor, non-franchised distributor or broker is NOT authorized.

If Supplier becomes aware or suspects that it has furnished Counterfeit Parts, it shall immediately notify Buyer. When requested by Mason, Supplier shall provide (if available) Authorized Supplier documentation that authenticates traceability of the parts to the Authorized Supplier.

If goods delivered are, or may include, Counterfeit Parts, Supplier shall promptly report the event in writing to buyer and subsequently investigate, and analyze whether such Counterfeit Parts should be replaced with genuine parts conforming to the purchase order requirements, or recommend an alternative solution to meet purchase order requirements at Supplier’s sole expense. The parties shall then agree upon the appropriate course of action for isolation of product. If agreement not reached within 10 days of notification, goods will be returned to the supplier or otherwise disposed of at Mason’s sole discretion. Confirmed counterfeit parts, components, or items are, by definition, non-conforming and not useable for any intended purpose.

QC 22. MASON- FURNISHED MATERIALS/EQUIPMENT

Materials, equipment, or other property provided on this purchase order is furnished by Mason, Mason’s customer, or the government. The supplier shall maintain an accountable management system that includes:

- Inspection for transit damage

- Periodic inspection for handling damage and deterioration during storage

- Functional testing when required

- Proper identification and verification of quantity and protection from improper use or disposition.

- Non-conforming or damaged property shall be reported promptly.

- Supplier shall have a system of internal controls to manage (control, use, preserve, protect, repair and maintain) Mason or government property in its possession. In doing so, the supplier shall initiate and maintain the processes, systems, procedures, records, and methodologies necessary for effective and efficient control of loaned property. The supplier shall disclose any significant changes to its property management system to the Mason Buyer prior to implementation of changes. The supplier may employ customary commercial practices, voluntary consensus standards, or industry-leading practices and standards that provide effective and efficient property management that are necessary and appropriate for the performance of this contract (except where inconsistent with law or regulation).

- The supplier’s responsibility extends from the initial acquisition and receipt of property, through stewardship, custody, and use until formally relieved of responsibility by authorized means, including delivery, other disposition, or via a completed investigation, evaluation, and final determination by Mason for lost property. This requirement applies to all Mason or government property under the supplier’s accountability, stewardship, possession or control, including its vendors or subcontractors.

- Supplier shall establish and maintain procedures necessary to assess its property management system effectiveness and shall perform periodic internal reviews, surveillances, self-assessments, or audits. Significant findings or results of such reviews or audits pertaining to Mason or government property shall be made available to the Mason Buyer within 48 hours of request.

| Form WI-020-2.3 Rev G | 13 of 15 |
| --- | --- |

Printed copies of this document are not controlled

| WI #: | Rev: | TYPE: |
| --- | --- | --- |
| WI-SQC | C | QA |

Work Instruction

- The Supplier shall include the requirements of this clause in all subcontracts under which property is acquired or furnished for subcontract performance.

QC 23. FOREIGN OBJECT DEBRIS or DAMAGE (FOD)

Suppliers of FOD sensitive articles shall establish FOD preventive and corrective procedures in accordance with the intent of NAS 412. The FOD program shall prevent and eliminate Foreign Object Damage and/or contamination during manufacturing, assembly, test and inspection operations, shipping and preservation. Pass-thru distributors of commercial off the shelf (COTS) components shall maintain, at minimum, visual methods to ensure delivery of items to Mason free of Foreign Object Debris/Damage.

QC 24. FACILITY / PROCESS CHANGE

The Supplier shall provide a prompt notification and acquire approval from Mason prior to delivery of product process changed by any of the following:

- Location of manufacturing, and/or processing facilities,

- Major process change

- Major supplier sub-tier change

- Loss of industry controlled other party or other third party certification or accreditation status, like Nadcap or QMS.

Any of these changes will require a full/delta FAI for each part number per QC 3 requirements.

QC 25. SPECIAL PROCESS SOURCES REQUIRED

Special processing required for any part of this purchase order shall be conducted by NADCAP accredited sources for each process or Mason approved and designated sources. Each shipment must be accompanied by a legible and reproducible copy of a Certificate of Conformance containing an authorized acknowledgement of completion for all processes used (Ref. QC 8). Certificates shall include the processing used, specification the special process conforms to, and the name of each agency performing each process.

When parts are serialized, all serial numbers shall appear on the certification.

Additionally, when explicitly required by Mason’s PO, special processing shall be performed only by Mason’s customer approved vendors and suppliers.

Special processes include but are not limited to:

- Bonding,

- Heat Treatment(s)

- Non-destructive testing

- Chemical film coating

- Anodic coating

- Plating

- Titanium processing

- Surface enhancement (Shot Peening)

- Welding / Brazing

QC 26. SPECIALTY METALS SOURCE OF SUPPLY

All metal delivered to Mason shall be melted in the United States, its possessions, Puerto Rico or a qualifying country, in accord with DFARS 252.225-7008, 252.225.7009, 225.872-1, 225.003, and

| Form WI-020-2.3 Rev G | 14 of 15 |
| --- | --- |

Printed copies of this document are not controlled

| WI #: | Rev: | TYPE: |
| --- | --- | --- |
| WI-SQC | C | QA |

Work Instruction

225.7001. Certification of materials compliance is required. Chemical and Physical Test Reports are also required, from the manufacturer stating the batch, heat or lot number, the specification(s) the material was produced under, and traceable to the raw material source. Complete chain of control documentation from the producing mill or foundry to Mason shall be included as part of the material certification. Failure to comply will result in the rejection and return of the non-compliant materials at supplier expense.

QC 27. DOMESTIC SOURCE OF SUPPLY

The supplier must manufacture and/ or procure product from a domestic (USA) source of supply. The supplier shall flow down these requirements to all lower-tier subcontractors and suppliers. Compliance shall be stated in the supplier’s Certificate of Conformance or by a separate certificate.

QC 28. FAA FORM 8130-3

Completed and valid FAA form 8130-3 required with the purchased goods.

QC 29. RECORDS RETENTION

Records of manufacturing, testing, processing, inspection, packaging and shipping of items on a purchase order shall be retained for a minimum of ten (10) years after completion of the order unless otherwise specified in body of the Mason Purchase Order. Records shall be made available to Mason for review on request.

At least 30 days prior to destruction, supplier agrees to and shall offer possession of records to Mason. If Seller ceases operations, Seller shall notify Buyer in writing within ten (10) business days of decision to cease operations and transfer records to Mason in accordance with Buyer’s direction.

| Form WI-020-2.3 Rev G | 15 of 15 |
| --- | --- |

Printed copies of this document are not controlled