Rubber floor coverings and accessories

More than a surface

Imagine an environment that’s more comfortable, safe and quiet with every step.

That’s an idea worth hearing. In fact, we build

our products around it. For decades, we’ve

been listening to your needs and responding

with sustainable rubber floorings that makes

sense for your facility.

Noise absorbing, ergonomic and stain and slip

resistant, nora® floorings go beyond your basic

requirements. Safety. Comfort. Ease of

maintenance. Style. Who says you have to

sacrifice one for the other? With more than

300 colours and styles available, we merge function and aesthetic appeal to meet the unique demands of your facility.

Our floorings are more than a surface.

It’s a statement.

Two product lines - endless possibilities

norament®

A classic among rubber flooring products, norament® represents top-class quality and functionality. Robust norament® tiles have a highly dense and closed surface, making them extremely wear resistant. Because of its ability to withstand the pressures of heavy traffic, norament® floorings will show little to no signs of wear or loss in appearance, even after decades of use. norament® is recommended for areas subject to high traffic and intense strain.

noraplan®

The noraplan® system offers unlimited flooring design options and a coordinated range of accessories. Available as tiles and rolls, the versatile noraplan® collection provides a varied range of uses throughout any facility. Enhanced acoustic, slip and stain resistant qualities make noraplan® the ideal choice for a wide variety of applications.

CONTENTS

| norament® floorings | 4 – 13 |
| --- | --- |
| noraplan® floorings | 14 – 27 |
| nora® special floorings | 28 – 39 |
| norament® stairtreads | 40 – 43 |
| nora® stair accessories | 44 – 47 |
| nora® accessories | 48 – 53 |
| Technical data | 54 – 56 |

nor ament® Product Range

norament® 926/825

One-coloured, classic round pastille for use in extremely heavy (926) and heavy traffic areas (825).

| 0170 | 6173 |  | 0007 | 0884 |
| --- | --- | --- | --- | --- |

| 0214 |  | 2079 | 0319 | 0733 |
| --- | --- | --- | --- | --- |

| 2685 | 6172 | 6192 | 2074 |
| --- | --- | --- | --- |

|  | 0882 | 0749 |  | 0716 | 0702 |
| --- | --- | --- | --- | --- | --- |

| 0890 | 0866 | 6191 | 0846 |
| --- | --- | --- | --- |

norament® | nora systems 5

norament® floorings

norament® 926

20

Art. 926/354

■ ∼1004 mm x 1004 mm

∼27.5 mm

∼0.5 mm

∼3.5 mm   ∼4.0 mm

nora® profile connection dimension: E + U

Resists most oils and greases.

norament® 825

20

Art. 825/1902

■ ∼501 mm x 501 mm

| ∼27.5 mm |  |  |  | ∼0.5 mm |  | ∼3.2 mm |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | ∼2.7 mm |  |  |

nora® profile connection dimension: D + U

These colours can also be delivered as:

Special flooring norament® 928 ed

electrostatically dissipative, page 33

Stairtread norament® 926, page 40

= Price category

- nora systems | norament®

norament® 926 crossline

One-coloured, with a three dimensional carving structure for use in extremely heavy traffic areas.

| 6462* | 6463* | 6464* | 6465* |
| --- | --- | --- | --- |

| 6466* | 6467* | 6468 | 6469* |
| --- | --- | --- | --- |

| 0884 | 0882 | 6470* | 0866 |
| --- | --- | --- | --- |

|  |  |  |  | 0007 |  |  |  |  |  |  | 0749 |  |  |  |  | 0716 |  | 0702 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| norament® 926 crossline |  |  |  |  |  | = Price category |  |  |
| 16 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Art. 926 crossline/3076 |  |  |  |  |  |  |  |  |
| ■ ∼1004 mm x 1004 mm |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  | ∼3.5 mm |  | * Part of |  |  |

nora® profile connection dimension: E + U Resists most oils and greases.

norament® | nora systems 7

norament® floorings

- nora systems | norament®

norament® 926 grano

A granular design rich in contrast with a hammerblow surface for use in extremely heavy traffic areas.

4868	4869	4870               4871

4872	4873                4874	4875

| 4876 | 4877 | 4878 | 4879 |
| --- | --- | --- | --- |

| 4880 |  |  |  |  |  | 4881 |  |  |  |  | 4882 |  |  | 4883 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| norament® 926 grano |  |  | norament® 926 grano |  |
| 32 |  |  |  |  |  |  | 5 |  |  |  |  |
| Art. 926 grano/1880 |  |  |  |  | Art. 926 grano/1911 |  |
| ■ ∼1004 mm x 1004 mm |  |  | ■ ∼610 mm x 610 mm |  |
|  |  | ∼3.5 mm |  |  |  |  |  |  |  |  | ∼3.5 mm |  |
| nora® profile connection dimension: E + U |  |  | Resists most oils and greases. |  |

Resists most oils and greases.

norament® | nora systems 9

norament® floorings

4884	     4885	4886	4887

4888	4889              4890	4891

4892	4893	4894	4895

4896               4897               4898              4899

These colours can also be delivered as:

Special flooring norament® 928 grano ed electrostatically dissipative, page 33

Stairtread norament® 926 grano, page 41

- nora systems | norament®

norament® 926 satura

Tone-in-tone granular design with a hammerblow surface for use in extremely heavy traffic areas.

5101	         5102              5103	5104

5105	5106              5107              5108

5109	         5110	5111	5112

| 5113 | 5114 | 5115 | 5116 |
| --- | --- | --- | --- |
| norament® 926 satura |  | These colours can also be delivered as: |  |
| 32 |  | Stairtread norament® 926 satura, page 42 |  |
| Art. 926 satura/1880 |  |  |  |
| ■ ∼1004 mm x 1004 mm |  |  |  |

∼3.5 mm

nora® profile connection dimension: E + U

Resists most oils and greases.

norament® | nora systems 11

norament® floorings

5117	         5118	5119	5120

5121	5122	5123	5124

5125	5126              5127	5128

5129	5130	5131	5132

- nora systems | norament®

norament® 926 serra

Fine scatter design with a flat directional relief structure for use in extremely heavy traffic areas.

4914	4915	4916	4917

4918	4919	4920	4921

4922	4923	4824	4924

4925	4926	4927	4928

4823	4929	4821	4930

norament® 926 serra

20

Art. 926 serra/3016

■ ∼1004 mm x 502 mm

∼3.5 mm

nora® profile connection dimension: E + U Resists most oils and greases.

Order-related smaller formats can be cut for individual installation combinations without minimum quantity requirements from norament® 926 serra tiles with the standard dimensions of 1,004 mm x 502 mm.

We supply tiles with chamfered edges on request such that the tile character of the installed floor covering is even more emphasized.

norament® | nora systems 13

norament® floorings

nor aplan® Product Range

noraplan® eco

Smooth tone-in-tone granular design in a smooth surface for heavy traffic areas.

6620	6621	6622	6623

6624	6625	6626	6627

6628	6629	6630	6631

6632	6633	6634	6635

noraplan® eco

16

Art. 1490

∼1.22 m x 15.0 m

Art. 2490

■ ∼610 mm x 610 mm

15 ■ = 5.58 m² in one carton

∼2.0 mm

nora® profile connection dimension: A + U

noraplan® | nora systems 15

noraplan® floorings

- nora systems | noraplan®

noraplan® sentica

A changing base colour of harmoniously matched colour compositions in a smooth surface for heavy traffic areas.

6500	     6501	6502	6503

6504	       6505	6506	6507

| 6508 | 6509 | 6510 | 6511 |
| --- | --- | --- | --- |

| 6512 | 6513 | 6514 | 6515 |
| --- | --- | --- | --- |

| 6516 | 6517 | 6518 | 6519 |
| --- | --- | --- | --- |

6520	     6521	6522	6523

| 6524 | 6525 |  | 6526 |
| --- | --- | --- | --- |

| 6528 | 6529 | 6530 |
| --- | --- | --- |

| 6532 |  | 6533 | 6534 |
| --- | --- | --- | --- |

| 6536 |  |  |  | 6537 |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| noraplan® sentica | noraplan® sentica |
| 38 |  |  |  | 12 |  |  |  |
| Art. 1700 |  |  | Art. 1701 |
| ∼1.22 m x 15.0 m |  |  | ∼1.22 m x 12.0 m |
| Art. 2700 |  |  | Art. 2701 |
| ■ ∼610 mm x 610 mm | ■ ∼610 mm x 610 mm |
| 15 ■ = 5.58 m² in one carton | 10 ■ = 3.72 m² in one carton |
|  |  |  | ∼2.0 mm |  |  |  |  |  | ∼3.0 mm |

noraplan® | nora systems 17

noraplan® floorings

6527

6531

6535

These colours can also be delivered as:

Special flooring noraplan® sentica ed

electrostatically dissipative, page 34

Special flooring noraplan® sentica acoustic footfall-sound-absorbing 20 dB, page 37

nora® profile connection dimension: A + U	nora® profile connection dimension: D + U

- nora systems | noraplan®

noraplan® signa

A changing base colour consisting of three hamoniously matched colour components and characteristic granule inclusions in a smooth surface for heavy traffic areas.

| 2780 | 2930 | 2931 | 2932 |
| --- | --- | --- | --- |

2781	2933	2934	2935

| 2936 | 2937 | 2938 | 2939 |
| --- | --- | --- | --- |

2940	2941	2942	2943

| 2787 | 2784 | 2944 | 2945 |
| --- | --- | --- | --- |

2779	2785	2786	2946

noraplan® | nora systems 19

| 2947 | 2948 | 2949 | 2950 |
| --- | --- | --- | --- |

2951

2955

2959

2963

2967

noraplan® floorings

| 2952 | 2953 | 2954 |
| --- | --- | --- |

2956	2957	2958

2960	        2961	2962

2964	2965	2966

2968	2969	2970

noraplan® signa

48

Art. 1462

∼1.22 m x 15.0 m

Art. 2462

■ ∼610 mm x 610 mm

15 ■ = 5.58 m² in one carton

∼2.0 mm

noraplan® signa

17

Art. 1463

∼1.22 m x 12.0 m

Art. 2463

■ ∼610 mm x 610 mm

10 ■ = 3.72 m² in one carton

∼3.0 mm

These colours can also be delivered as:

Special flooring noraplan® signa ed

electrostatically dissipative, page 35

Special flooring noraplan® signa acoustic footfall-sound-absorbing 20 dB, page 38

nora® profile connection dimension: A + U	nora® profile connection dimension: D + U

- nora systems | noraplan®

noraplan® stone

Discreet, non-directional scatter design available in both reflection-breaking and smooth surfaces for heavy traffic areas.

noraplan® stone · reflection-breaking surface

6601	       1146               1862               2306

6602	         6603              6604               1279

6605	6606              6607              6608

6609	       6610	6611	6612

6613	       6614               6615               6616

noraplan® stone · reflection-breaking surface

20

Art. 149

∼1.22 m x 15.0 m

Art. 249

■ ∼610 mm x 610 mm

15 ■ = 5.58 m² in one carton

∼2.0 mm

These colours can also be delivered as:

Special flooring noraplan® stone ed

electrostatically dissipative, page 36

Special flooring noraplan® stone acoustic footfall-sound-absorbing 20 dB, page 39

nora® profile connection dimension: A + U

noraplan® | nora systems 21

noraplan® stone · smooth surface

noraplan® floorings

6601	1146	1862	2306

6613	6614	6607	1279

noraplan® stone · smooth surface

8

Art. 1600

∼1.22 m x 15.0 m

Art. 2600

■ ∼610 mm x 610 mm

15 ■ = 5.58 m² in one carton

∼2.0 mm

nora® profile connection dimension: A + U

- nora systems | noraplan®

noraplan® ultra grip

Safety floor covering with increased slip resistance, TRRL Pendulum Test 36+ in the wet and RZ value 20.1. Slip resistance R11 according to DIN 51 130 and BGR 181 or GUV-R 181, excellent environmental compatibility confirmed by BRE “A+” rating.

6014	6015	6016	6017

6018	6019	6020	6021

6023	6024	6027	6029

noraplan® ultra grip

Design with discretely dispersed granite chips

12

Art. 1569

∼1.20 m x 15.0 m

∼2.0 mm

nora® profile connection dimension: A + U

Resists most oils and greases.

noraplan® | nora systems 23

noraplan® floorings

- nora systems | noraplan®

noraplan® uni

One-coloured with a smooth surface for heavy traffic areas.

2446	6175	2140	2647

2454	1810	2457	2451

6176	2144	0131	6129

2452	6177	6178	2848

6179	2981	6009	0597

noraplan® uni

20

Art. 1461

∼1.22 m x 12.0 m

Art. 2461

■ ∼610 mm x 610 mm

15 ■ = 5.58 m² in one carton

∼2.0 mm

nora® profile connection dimension: A + U

noraplan® | nora systems 25

noraplan® floorings

- nora systems | noraplan®

noraplan® unita

A perfect combination of materials, comprising permanently resilient rubber and randomly dispersed granite chips with a smooth surface for heavy traffic areas. Available in two timeless designs.

6442	6443	6444	6445

6446	6447	6448	6449

6450	6451	6452	6453

| 6454* |  |  |  | 6455* | 6456* |  |  |  | 6457* |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| noraplan® unita |  | noraplan® unita |  |
| Design with discretely dispersed granite chips |  | Design with glimmering dispersed granite |  |
| 12 |  |  |  |  | 4 |  |  |  |  |
| Art. 1640 |  | Art. 1650* |  |
| ∼1.22 m x 15.0 m |  |  | ∼1.22 m x 15.0 m |  |
|  |  |  | ∼2.0 mm |  |  |  |  |  | ∼2.0 mm |  |
| nora® profile connection dimension: A + U |  | nora® profile connection dimension: A + U |  |

Please note: Granite is a natural product. For this reason, slight colour deviations may occur in the stone even within the same batch.

*  Art. 1650 is only available in colours:

6454, 6455, 6456 and 6457.

noraplan® | nora systems 27

noraplan® floorings

Special floorings

norament® 975 LL

For fast installation with the removable nora® quickfix system. This can be walked on immediately and is immediately resilient. Resists most oils and greases and is suitable for raised-access floors, on existing old floor coverings and for temporary installations.

norament® 975 LL (grano design)

Hammerblow surface

norament® 975 LL (grano design)

9

Art. 975 LL/1880

■ ∼1000 mm x 1000 mm

∼3.5 mm

nora® profile connection dimension: E + U

4877	4873	4886

4883	4879	4896

4899	4880	4882

Please note: norament® 975 LL is not suitable for installation

– in areas with a high or regular exposure to moisture (e.g. entrance area)

– in areas with high or frequently occurring dynamic pressure loads

– in areas with high temperature fluctuations, e.g. in case of direct, long-term exposure to sunlight

Design differences between norament® 975 LL and the standard products norament® 926 grano as well as norament® 926 serra are due to production-technical reasons. Please request individual colour samples of the required norament® product.

Special floorings | nora systems 29

norament® 975 LL (serra design)

Relief structure

4823	4929	4821

norament® 975 LL (serra design)

3

Art. 975 LL/3042

■ ∼1000 mm x 500 mm

|  |  |  | ∼3.5 mm | Please note: We supply tiles with chamfered |
| --- | --- | --- | --- | --- |
| nora® profile connection dimension: E + U |  |
|  | edges on request (Art. 3043). |

Special floorings

- nora systems | Special floorings

norament® 992/992 grano

For areas with extreme requirements (e.g. ice rinks, golf clubs, animal stables, etc.).

norament® 992

Round pastille

0702	0319	2079	0882

| 6172 | 0866 |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| norament® 992 |  |  | ∼27.5 mm |  |  |  |  |  | ∼0.5 mm |  |  |
| 6 |  |  |  |  |  |  |  |  | ∼2.5 mm | ∼9.0 mm |
|  |  |  |  |  |  |  |  |  | ∼6.0 mm |  |
| Art. 992/1956 |  |  |  |  |  |  |  |  |  |  |  |
|  | nora® profile connection dimension: N |  |
| ■ ∼1002 mm x 1002 mm |  |  |

Please note price group black/coloured

Special floorings | nora systems 31

norament® 992 grano

Hammerblow surface

4879	4882	4872	4876

| 4897 | 4880 |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| norament® 992 grano |  |  |  | ∼3.0 mm |  | ∼9.0 mm |
| 6 |  |  |  | ∼6.0 mm |  |  |
| Art. 992 grano/1955 | nora® profile connection dimension: N |  |
| ■ ∼1002 mm x 1002 mm |  |  |  |  |  |  |

Special floorings

- nora systems | Special floorings

norament® and noraplan® ec

Electrostatically conductive “ec” floorings for optimum ESD protection of electronic devices and equipment. Suitable for areas with a risk of explosions and fork-lift-truck areas (norament® 927 grano ec). Largely resistant to acids and alkalis (norament® 927 grano ec).

norament® 927 grano ec

norament® 927 grano ec

1

Art. 927 grano ec/1880

■ ∼1004 mm x 1004 mm

∼3.5 mm

nora® profile connection dimension: E + U

4617

noraplan® astro ec

on the electrostatic

properties as

y e a r s statedourwarrantyin w a r r a n t y conditions*.

* t o b e r e q u e s t e d f r o m o u r o f f i c e

6102	6007	6114	6056

noraplan® astro ec

4

Art. 1466

∼1.22 m x 12.0 m

Art. 2466

■ ∼610 mm x 610 mm

15 ■ = 5.58 m² in one carton

∼2.0 mm

nora® profile connection dimension: A + U

Special floorings | nora systems 33

norament® ed

Electrostatically dissipative “ed” floorings for optimum ESD protection of electronic devices and equipment. Protect against electrical shock, resist most oils and greases and are suitable for forklift truck areas.

norament® 928 ed

| 0884 | 0749 |  |  |  |  |  | 0319 |  | 0214 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| norament® 928 ed |  |  | ∼26 mm |  |  |  |  |  | ∼0.3 mm |  | ∼4.0 mm |  |
| 4 |  |  |  |  |  |  |  |  |  | ∼3.7 mm |  |  |  |
|  |  | nora® profile connection dimension: E + U |  |
| Art. 928 ed/399 |  |  |
| ■ ∼1002 mm x 1002 mm |  |  |  |  |  |  |  |  |  |  |  |  |  |

norament® 928 grano ed

| 4884 | 4871 | 4874 |  | 4878 |
| --- | --- | --- | --- | --- |

|  | 4879 |  |  |  |  | 4896 |  |  | 4882 |  |  |  | 4881 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| norament® 928 grano ed |  | norament® 928 grano ed |  |  |  |
| 8 |  |  |  |  |  | 5 |  |  |  |  |
| Art. 928 grano ed/1880 |  |  | Art. 928 grano ed/1911 |  |  |  |
| ■ ∼1004 mm x 1004 mm |  | ■ ∼610 mm x 610 mm |  |  |  |
|  |  |  | ∼3.5 mm |  |  |  |  |  | ∼3.5 mm |

on the electrostatic

properties as

y e a r s stated in

our warranty

* t o b e r e q u e s t e d f r o m o u r o f f i c e

Special floorings

nora® profile connection dimension: E + U

- nora systems | Special floorings

noraplan® ed

Electrostatically dissipative “ed” floorings for optimum ESD protection of electronic devices and equipment. Protect against electrical shock, resist most oils and greases.

noraplan® sentica ed

on the electrostatic properties as

y e a r s stated in

our warranty

* t o b e r e q u e s t e d f r o m o u r o f f i c e

6508	6509	6513	6512

6516	6517	6521	6520

6504	6505	6530	6529

noraplan® sentica ed

12

Art. 1702

∼1.22 m x 15.0 m

Art. 2702

■ ∼610 mm x 610 mm

15 ■ = 5.58 m² in one carton

∼2.0 mm

nora® profile connection dimension: A + U

noraplan® sentica ed

12

Art. 1703

∼1.22 m x 12.0 m

∼3.0 mm

nora® profile connection dimension: D + U

Please note: The colours 6504, 6505 and 6508 are only recommended for areas with a low incidence of stains and dirt (e.g. not for OP theatres or intensively frequented areas).

Special floorings | nora systems 35

noraplan® signa ed

2780	2930	2931	2936

Special floorings

2937	2939	2944	2949

2950	2953	2955	2959

| 2961 |  |  |  | 2963 |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| noraplan® signa ed |  | noraplan® signa ed |
| 14 |  |  |  | 14 |  |  |  |
| Art. 1390 |  | Art. 1523 |
| ∼1.22 m x 15.0 m |  | ∼1.22 m x 12.0 m |
| Art. 2390 |  |  |  |  |  |
| ■ ∼610 mm x 610 mm |  |  |  |  | ∼3.0 mm |
| 15 ■ = 5.58 m² in one carton |  | nora® profile connection dimension: D + U |
|  |  |  | ∼2.0 mm |  |  |  |  |  |

nora® profile connection dimension: A + U

- nora systems | Special floorings

noraplan® stone ed · reflection-breaking surface

6601	1146	2306	6603

noraplan® stone ed · reflection-breaking surface

4

Art. 129

∼1.22 m x 15.0 m

Art. 229

■ ∼610 mm x 610 mm

15 ■ = 5.58 m² in one carton

∼2.0 mm

nora® profile connection dimension: A + U

Special floorings | nora systems 37

noraplan® acoustic

For high footfall sound absorption with a footfall sound absorption improvement of 20 dB.

noraplan® sentica acoustic

6501	6510	6508	6536

Special floorings

6530	6531	6521	6520

6513	6512	6517	6516

noraplan® sentica acoustic

12

Art. 1705

∼1.22 m x 12.0 m

| ∼1.6 mm | ∼4.0 mm |  |
| --- | --- | --- |
| ∼2.4 mm |  |  |
|  |  | Please note: noraplan® acoustic floorings |
| nora® profile connection dimension: F + U |  |
|  | must be sealed with nora® hot welding rod. |

- nora systems | Special floorings

noraplan® acoustic

For high footfall sound absorption with a footfall sound absorption improvement of 20 dB.

noraplan® signa acoustic

2780	2930	2936	2937

2944	2949	2956	2959

noraplan® signa acoustic

8

Art. 1420

∼1.22 m x 12.0 m

| ∼1.6 mm |  | ∼4.0 mm |
| --- | --- | --- |
| ∼2.4 mm |  |  |

nora® profile connection dimension: F + U

Please note: noraplan® acoustic floorings

must be sealed with nora® hot welding rod.

Special floorings | nora systems 39

noraplan® stone acoustic · reflection-breaking surface

1146	1862	6604	1279

Special floorings

6605	6610	6607	6608

6613	6614	6615	6616

noraplan® stone acoustic · reflection-breaking surface

12

Art. 148

∼1.22 m x 12.0 m

∼1.6 mm  ∼4.0 mm  ∼2.4 mm

nora® profile connection dimension: F + U

Please note: noraplan® acoustic floorings must be sealed with nora® hot welding rod.

Nor ament® stairtreads

norament® stairtreads

Pre-shaped stair coverings consisting of stair nosing, riser and tread all in one piece for straight steps with right-angled edge. For extremely heavy traffic stairwell areas.

Stairtread norament® 926

One-coloured with classic round pastille, footfall sound absorption improvment of 12 dB

| 0214 | 0319 | 0733 | 0890 |
| --- | --- | --- | --- |

| 0007 | 0882 | 2074 | 6172 |
| --- | --- | --- | --- |

|  |  |  |  |  |  | 0884 |  |  |  |  |  |  |  |  | 0749 |  |  |  | 0716 |  |  | 0702 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | ∼50.5 cm |  |  |  |  |  |  |  |  |  | Stairtread norament® 926 |
|  |  |  |  | ∼16.5 cm |  |  |  |  |  |  | ∼9.5 cm |  |  |  | ∼24.5 cm |  | 12 |  |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Art. 926/465 – width 1,285 mm |
|  |  |  | ∼27.5 mm |  |  |  |  | ∼0.5 mm |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  | ∼4.5 mm |  |  |  |  |  |  |  |  |  | Art. 926/466 – width 1,614 mm |
|  |  |  |  |  |  |  |  |  | ∼4.0 mm |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

Art. 926/467 – width 2,004 mm

= Price category

norament® stairtreads | nora systems 41

Stairtread norament® 926 grano

Granular design rich in contrast with a hammerblow surface, footfall sound absorption improvment of 12 dB

4885	4877	4878	4879

4890	4898	4897	4896

|  |  |  | 4899 |  |  |  |  | 4881 |  |  |  | 4882 | 4883 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | ∼50.5 cm |  |  |  |  |  | Stairtread norament® 926 grano |
|  |  | ∼16.5 cm |  |  | ∼9.5 cm |  |  |  | ∼24.5 cm |  |  |  |  | 12 |

| ∼5.0 mm | Art. 926 grano/479 – width 1,285 mm |
| --- | --- |
|  | Art. 926 grano/468 – width 1,614 mm |
|  | Art. 926 grano/469 – width 2,004 mm |

norament® stairtreads

- nora systems | norament® stairtreads

Stairtread norament® 926 satura

Tone-in-tone granular design with a hammerblow surface, footfall sound absorption improvment of 12 dB

5102	5103	5107	5108

5110	5114	5115	5116

|  |  |  | 5118 |  |  |  |  |  |  | 5121 |  |  | 5127 | 5129 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  |  | ∼50.5 cm |  |  |  |  |  |  | Stairtread norament® 926 satura |
|  |  | ∼16.5 cm |  |  |  |  | ∼9.5 cm |  |  |  |  | ∼24.5 cm |  |  | 12 |  |  |

| ∼5.0 mm | Art. 926 satura/479 – width 1,285 mm |
| --- | --- |
|  | Art. 926 satura/468 – width 1,614 mm |
|  | Art. 926 satura/469 – width 2,004 mm |

norament® stairtreads | nora systems 43

norament® stairtreads with signal or safety stripes

norament® stairtreads can be equipped with the following signal or safety stripes:

0122	0895	6014	6029

- Signal stripes yellow, phosphorescent according to DIN 67 510, in a width of 2 cm, integrated into the tread area of the stair nosing

- Signal stripes uni, in a width of 2 or 3 cm in the colours 0122, light grey, and 0895, signal yellow, integrated into the tread area and alternatively also in the vertical part of the stair nosing

- Safety stripes ultra grip for increased slip resistance, in a width of 2 or 3 cm in the colours 6029, yellow, and 6014, grey, integrated into the tread area and alternatively also in the vertical part of the stair nosing

Signal and safety stripes in other widths and colours are available on request.

norament® stairtreads

Stair accessories

nora® accessories for stairwell areas

| Accessory range made of rubber |  | 8 | 4 |
| --- | --- | --- | --- |
| matched to suit norament® and |  |  | 3 |
| noraplan® floor coverings. Can also | 9 | 6 |  |
| be used in combination with other |  |  | 5 |
|  |  |  | 10 |
| types of floorings. nora® profiles are |  |  |  |
| impact and shock-resistant, do not |  | 7 | 2 |
| shrink, do not contain any plasticizers |  |  | 10 |
| and retain their functional reliability | 1 |
| long term. |  |

nora® stair nosings

With plug-in lip for quick and easy installation on all types of staircases.

T 5049/T 5044

8

Minimum order quantity: 5 r.m.

Standard length: 2.5 r.m.

Delivery in 5 fixed lengths possible:

1.00/1.25/1.65/2.0/2.50 r.m.

0214

0702

0716

0749

0884

4877

4885

4890

TA 1203

Aluminium stair nosing for stairs

made of norament® coverings

Delivery unit: 2.7 r.m.

mm

∼45

mm

∼45

1

Fixing with contact adhesive

∼50 mm

T 5049 A/C

For flooring thicknesses

of 2.0 to 2.7 mm

∼50 mm

T 5049 E/F

For flooring thicknesses

of 3.5 to 4.0 mm

2

Fixing with nora® stepfix 240 roll-type

dry adhesive

∼70 mm

|  |  | mm |
| --- | --- | --- |
|  | T 5044 A/C | 3 |
|  |  | . |
| mm |  | 26 |
|  | For flooring thicknesses |  |
| ∼43 |  |  |
|  | of 2.0 to 2.7 mm |  |

∼70 mm

T 5044 E/F

| mm | For flooring thicknesses |
| --- | --- |
| ∼43 |  |
|  | of 3.5 to 4.0 mm |

3

46.3 mm

1.2 mm

TA 1203

For flooring thicknesses of 3.5 mm

Stair accessories | nora systems 45

nora® stair angles

For the smooth finishing of right-angled stairs to the wall and banister side.

TW 7005 U/TW 7006 U/

TG 7003 U/TG 7004 U

34

Delivery unit: pieces

| TW 7006 U | TW 7005 U | TG 7004 U | TG 7003 U |
| --- | --- | --- | --- |
| (Outer angle) | (Inner angle) | (Outer angle) | (Inner angle) |
| 4 | 5 | 6 | 7 |

0007

0214

0319

0702

0716

0733

0749

0882

∼4.8 mm

4

∼50 mm

5

Wall side

With same cross-section as adjoining skirting S 1008 U

| 170∼ | mm |
| --- | --- |

∼170 mm

170∼ mm

| 170∼ | mm |
| --- | --- |

| ∼170 | ∼18 mm |
| --- | --- |
| mm |  |

|  | ∼8.2 mm |
| --- | --- |
| mm | 6 |
| ∼170 |  |
|  | 33∼ mm |
| ∼170 mm | 7 |
|  | Banister side |
| ∼170 | With same cross-section |
| mm | as stringer A 5013 U |

| 0884 |  |
| --- | --- |
| 0890 |  |
| 1146 |  |
| 1150 |  |
| 2074 |  |
| 2930 | nora® |
| 4877 |  |
|  | stair |
| 4878 |  |
|  | accessories |
| 4881 |  |
| 4885 |  |
| 4890 |  |
| 4896 |  |

nora® skirting and stringer profile

S 1008 U/A 5013 U

34

S 1008 U	A 5013 U

Multi-purpose skirting	For landings and ramps

Delivery unit: rolls of 10 r.m.	Delivery unit: in units of 2.5 r.m.

Connection profile for nora® stair	Connection profile for nora®

angles “TW”	stair angles “TG”

8	9

∼18 mm

∼4.8 mm

∼8.2 mm

mm∼50mm

∼33

4897

4898

5102

5103

5107

5108

5110

5114

5115

5116

5118

5121

5127

5129

- nora systems | Stair accessories

nora® stair margin

2

For wall and banister side.

Hammerblow surface with

granular design.

Art. 819

∼600 mm x 100 mm

Thickness 10 mm

Supplied as: pieces

4899	4883

- (see page 44)

10 mm

∼100

mm

| ∼600 | mm |
| --- | --- |

nora® stepfix 240

Special roll-type dry adhesive

For quick installation of norament® stairtreads,

stairwell installations with nora® stair nosing T 5044

and nora® stair margin.

The cost and eco-conscious adhesive innovation.

Suitable for new buildings and renovation.

Advantages: 3–5 times as quick, odourless, can be

walked on immediately, economic, eco-compatible,

and reliable thanks to excellent bonding performance.

Art. 907

Stair accessories | nora systems 47

nora® special range for stairwell areas

4

3

2

1

nora® stair nosings

T 5019/T 5033/T 5045/T 5005

1	2

The special range offers profiles with different cross-sections for further applications. The profiles shown here are examples only. Further individual designs are available on request. Delivery units and minimum order quantities on request.

3	4

| ∼50 mm | ∼50 mm | ∼50 mm |
| --- | --- | --- |
|  | ∼26 mm |  |

| mm | Connection | m | Connection | mm | Connection |  | Connection |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | m |  |  |  | m |  |
| ∼45 |  | 36 |  |  |  | m |  |
|  | dimensions |  | dimension | ∼60 | dimension |  | dimension |
|  |  | ∼ |  |  |  | 50 |  |
|  | T 5019 A = 2.1 mm |  | T 5033 A = 2.1 mm |  | T 5045 A = 2.1 mm | ∼ | T 5005 E = 3.7 mm |
|  | T 5019 C = 2.7 mm |  |  |  |  |  |  |
|  | T 5019 D = 3.1 mm |  |  |  |  |  |  |
|  | T 5019 F = 4.1 mm |  |  |  |  |  |  |
|  | T 5019 H = 5.0 mm |  |  |  |  |  |  |

nora® stair accessories

Accessories

nora® accessories

Accessory range made of rubber matched to suit nora® floor

coverings for convincing solutions both in visual and functional	5	4	1

6

terms. The materials are impact- and shock-resistant, do not contain any plasticizers and retain their functional reliability long term.

3

2

nora® skirtings

S 1023 U

Height 60 mm

89*

S 1023 U

For areas with stringent requirements in terms of appearance. The permanently resilient sealing lip of S 1023 U reliably accommodates pastille heights of up to 1 mm. Also suitable as wall stringer with raised-access floors.

Art. 712

Delivery unit: in rolls of 10 r.m.

*Further colours on request

S 1024 U

Height 100 mm

65*

S 1024 U

For areas with stringent requirements in terms of appearance. The permanently resilient sealing lip of S 1024 U reliably accommodates pastille heights of up to 1 mm. Also suitable as wall stringer with raised-access floors.

Art. 713

Delivery unit: in rolls of 10 r.m.

*Further colours on request

|  |  |  | 0007 |
| --- | --- | --- | --- |
|  |  |  | 0319 |
|  |  |  | 0702 |
| 5 |  |  | 0716 |
|  |  |  | 0749 |
| ∼2.8 mm |  |
|  |  |  | 0882 |
|  |  |  | 0884 |
|  |  | ∼60 mm | 1146 |
|  |  |  | 1150 |
| 12 | mm | 1162 |
|  |  |  | 1279 |
|  |  |  | 1362 |
|  |  |  | 0007 |
|  |  |  | 0319 |
|  |  |  | 0702 |
| 4 |  |  | 0716 |
|  |  |  | 0749 |
| ∼2.8 mm |  |
|  |  |  | 0882 |
|  |  |  | 0884 |
|  |  |  | 1146 |
|  |  | ∼100 mm | 1150 |
| 12 | mm |  |

1385

1581

1780

1862

2098

2099

2143

2398

2635

2636

2666

2680

1279

1385

1581

1780

1862

2099

2398

2635

2636

2925

2930

2931

2937

2944

2949

2950

2951

2953

2954

2962

2963

2666

2680

2925

2930

2931

2937

2944

2949

2950

2964

2966

2968

4873

4877

4881

4885

5109

5114

5115

5121

5122

2951

2953

2954

2962

2963

2964

2966

2968

4873

5128

6173

6178

6446

6448

6451

6501

6503

6504

6505

6506

6507

4877

4881

4885

6173

6178

6501

6503

6506

6507

6508

6509

6510

6511

6512

6513

6514

6515

6516

6517

6518

6519

6508

6509

6510

6511

6512

6513

6514

6515

6516

6522

6523

6528

6529

6530

6532

6536

6537

6598

6604

6606

6607

6517

6518

6519

6522

6523

6528

6529

6530

6532

6608

6609

6611

6612

6616

6536

6537

S 1008 U

Adjoining skirting for nora® stair angles “TW”

| 33* | 6 |
| --- | --- |
| S 1008 U | ∼4.8 mm |
| Multi-purpose skirting |  |
| Art. 705 |  |
| Delivery unit: in rolls of 10 r.m. |  |
| *Further colours on request |  |

|  | 0007 |
| --- | --- |
|  | 0214 |
|  | 0319 |
|  | 0702 |
|  | 0716 |
|  | 0733 |
|  | 0749 |
| ∼50 mm | 0805 |
|  | 0882 |

0884

0890

1146

1150

1780

2074

2680

2681

2786

2930

4877

4881

4885

4898

5103

5107

5108

5110

5114

5115

5118

5121

5127

5129

Accessories | nora systems 49

nora® skirting and skirting angles

Easy to clean, suitable for areas with stringent hygienic requirements.

SA 7002 Skirting outer angle

22*

SA 7002 A

22*

SA 7002 D

7*

| SA 7002 E |  |
| --- | --- |
| Suitable for Skirting S 3003. |  |
| Art. 508 |  |
| Delivery unit: as pieces | ∼200 |
| Connection dimensions: |  |
|  | mm |
| A = 2.1 mm |  |
| D = 3.1 mm |  |
| E = 3.7 mm |  |
| *Further colours on request |  |

S 3003 Skirting

22*

S 3003 A

22*

S 3003 D

7*

S 3003 E

Matching with skirting angles SI 7001 and SA 7002.

Art. 726

Delivery unit: in rolls of 10 r.m.

Connection dimensions:

| ∼150 | 1 |
| --- | --- |
|  | mm |

∼150 mm

∼200 mm

2

∼100 mm

∼50

mm

∼3 mm

∼100 mm

Connection

∼50 mm      dimension

SA 7002 A/S 3003 A/SI 7001 A

SA 7002 D/S 3003 D/SI 7001 D

nora®

A = 2.1 mm

D = 3.1 mm

E = 3.7 mm

*Further colours on request

0882

2398

2635

2930

2931

2937

2944

2949

2950

2953

2963

2964

4877

6504

6508

6509

6512

6513

6516

6517

6529

6530

accessories

SI 7001 Skirting inner angle

22*

SI 7001 A

22*

| SI 7001 D | ∼150 mm |
| --- | --- |

7*

SI 7001 E

Suitable for Skirting S 3003.

Art. 507

Delivery unit: as pieces

| Connection dimensions: |  |  |
| --- | --- | --- |
| A = 2.1 mm | ∼100 | mm |

D = 3.1 mm

E = 3.7 mm

*Further colours on request

3

| ∼150 | mm |
| --- | --- |

∼100 mm

∼100 mm

∼50 mm

SA 7002 E/S 3003 E/SI 7001 E

| 1146 | 4871 | 4884 |
| --- | --- | --- |
| 1150 | 4874 |  |
| 1780 | 4881 |  |

- nora systems | Accessories

nora® cushioned-edge profile

H 9010

For optimum transition between the

noraplan® floor coverings and the wall.

Delivery unit: 5 rolls of 10 r.m.

Art. 7731

∼15 mm

∼15 mm

nora® hot welding rod for noraplan®

Can be delivered in all colours to match the noraplan® floor covering colours.

Because noraplan® floor coverings do not contain any plasticizers, there is no shrinkage after installation. This is why the floorings do not have to be sealed. Only noraplan® acoustic floorings have to be sealed with the nora® hot welding rod. For the other floorings, we recommend sealing the joints when the flooring has been installed on a moisture-sensitive subfloor, in rooms with continual and intensive wet cleaning, in

areas with stringent hygiene requirements or for special requirements (e.g. in laboratories). In operating theatres or on other small noraplan® surfaces the vertical joints of the skirtings are sealed with nora® joint sealing compound.

Art. 946

Round, Ø 4 mm, rolls of 100 r.m.

nora® joint sealing compound

Since norament® and noraplan® floor coverings do not contain any plasticizers, there is no shrinkage after installation. This is why, with the exception of electrostatically dissipative norament® ed floorings, the floorings does not need to be sealed. It is, however, advisable to seal the joints in case of moisture-sensitive subfloors, in rooms permanently undergoing intensive wet cleaning or in areas with special hygienic requirements. For these special requirements, the sealing of all norament® and noraplan® floorings is suitable.

Art. 928

169

300 ml cartridge

1 disposable cartridge, sufficient for 15–18 r.m.

Please note: Joint cutter (art. no. 116950) and nora® liquid wax (art. no. 109914) may be ordered from our company.

| 0007 | 2780 | 2955 | 5101 | 5126 | 6469 | 6523 |
| --- | --- | --- | --- | --- | --- | --- |
| 0131 | 2781 | 2957 | 5102/2786 | 5127 | 6470 | 6524 |
| 0702 | 2784 | 2958/2147 | 5103 | 5128 | 6500 | 6525 |
| 0716 | 2785 | 2959 | 5104 | 5129 | 6501 | 6526 |
| 0733 | 2786 | 2962 | 5105 | 5130/6535 | 6502 | 6527 |
| 0749 | 2787 | 2963/2633 | 5106 | 5131 | 6503 | 6528 |
| 0866 | 2930 | 2964 | 5107 | 5132 | 6504 | 6529 |
| 0882 | 2931 | 2965 | 5108 | 6178/6502 | 6505 | 6530 |
| 0884 | 2933 | 2966 | 5109 | 6442 | 6506 | 6531/4877 |
| 1146/1253 | 2934 | 2967 | 5110 | 6443 | 6507 | 6532 |
| 1150/1254 | 2936 | 2968 | 5111 | 6444 | 6508 | 6533/2962 |
| 1385 | 2937 | 2969 | 5112 | 6446 | 6509 | 6534 |
| 1578 | 2938 | 2970 | 5113 | 6448 | 6510 | 6535 |

| 1581 | 2939/4877 | 4871 | 5114 | 6449 | 6511 | 6536 |
| --- | --- | --- | --- | --- | --- | --- |
| 1582 | 2941 | 4873 | 5115 | 6451 | 6512 | 6537 |
| 1585 | 2942/2142 | 4874 | 5116 | 6452 | 6513 | 6601/1254 |
| 2099/2940 | 2944 | 4877 | 5117 | 6453/6385 | 6514 | 6603/2940 |
| 2102/2947 | 2945/2897 | 4878/1780 | 5118 | 6457 | 6515 | 6613/1385 |

| 2106/2752 | 2946 | 4879/1254 | 5119 | 6462 | 6516 | 6615/2961 |
| --- | --- | --- | --- | --- | --- | --- |
| 2306/0716 | 2948 | 4881 | 5120 | 6463 | 6517 |  |
| 2380/2932 | 2949 | 4882/1253 | 5121 | 6464 | 6518 |  |
| 2398/2959 | 2950 | 4884 | 5122 | 6465 | 6519 |  |
| 2635/2961 | 2951 | 4885/2956 | 5123/6513 | 6466 | 6520 |  |
| 2636/2960 | 2953 | 4896/2680 | 5124 | 6467 | 6521/0882 |  |
| 2779 | 2954 | 4897/2681 | 5125 | 6468 | 6522 |  |

Accessories | nora systems 51

nora system blue® installation materials

| nora system blue® combines |  |  |  |  |
| --- | --- | --- | --- | --- |
| low-emission nora® rubber |  |  |  |  |
| floor coverings with low-emission |  |  |  |  |
| installation materials. The perfect |  |  |  |  |
| coordination of the individual system | 1 | 2 | 3 | 4 |
| components provides functional |  |  |  |  |
| reliability and ensures the highest |  |  |  |  |
| standards of quality. |  | The system design: 1 primer 2 filler 3 adhesive | 4 floor covering |

nora® hybrid 310	Art. 6610

Fiber-reinforced hybrid adhesive	For bonding norament® floorings on non-absorbent and

absorbent subfloors

nora® fiber 410	Art. 6611

Fiber-reinforced acrylic adhesive	For bonding nora® rubber floor coverings

nora® fiber ESD 414	Art. 6612

Fiber-reinforced, conductive	For bonding “ed” (dissipative) and “ec” (conductive)

acrylic adhesive	nora® rubber floor coverings

nora® level compound	Art. 6613

Fast spreading filler	For filling and levelling subfloors

nora® level compound FA*	Art. 6625*

Fiber-reinforced filler	For filling and levelling subfloors

nora® level compound SF	Art. 6626

Stable filler	For filling holes and patch-repairing transitions

nora® primer	Art. 6614

Acrylic special primer	Primer for cement screed, mastic asphalt and calcium sulphate

screed and as a bonding course between layers of filler

nora® 2-K primer/nora® primer plus	Art. 6615 / Art. 6646

Fast-drying acrylic special primer	Primer for cement screed, mastic asphalt and old encrusted

and water-resistant adhesive residues

nora® epoxy ground	Art. 6616

Two-component epoxy resin primer	Universal primer (e.g. for concrete and cement screed).

nora® accessories

* Article available in Germany only. Outside of Germany, nora® fibers (Art. 6654) are added to nora® level compound (Art. 6613).

- nora systems | Accessories

nora® dry adhesives

| nora® dryfix · Dry adhesive supplied in rolls |  |
| --- | --- |
| For the permanent fixing of norament® and noraplan® floor coverings. |  |
| The time-saving, cost- and eco-conscious adhesive innovation. Suitable for new buildings and renovations. |  |
| Advantages: 5 times as quick, can be walked on immediately, odourless, economic, eco-compatible |  |
| and reliable. |  |
| Art. 6556 |  |
| nora® profix · Dry adhesive tapes |  |
| nora® profix 50 | Processing of nora® skirtings |
| For quick installation of skirting S 1023 U. |  |
| Art. 992 |  |

nora® profix 90

For quick installation of skirtings S 1024 U, S 3003 as well as for pedestal formation through wall nosings (cushioned-edge profile).

Art. 993

nora® stepfix 240 · Dry adhesive supplied in rolls

For quick installation of norament® stairtreads, stairwell installations with nora® stair nosing T 5044 and nora® stair margin.

Art. 907

nora® quickfix squares

Bonding squares for short-time installation of norament® 975 LL

Art. 6505

nora® special range

The special range offers profiles with different cross-sections for further applications.

Delivery units and minimum oder quantities on request.

The profiles shown here are examples only. Further individual designs are available on request.

nora® skirting S 3014 N

Special skirting for norament® 992 and norament® 992 grano

nora® skirting S 1013 U

Skirting 10 cm high, also suitable for the use on other floor coverings

Delivery unit: in rolls of 10 r.m.

∼8.5 mm

∼150 mm

S 3014 N

∼8.6 mm

∼50 mm

∼100 mm

∼4.8 mm

S 1013 U

Accessories | nora systems 53

nora® pads

nora® pads are suitable for daily cleaning and intensive cleaning on extremely soiled nora® rubber floor coverings. Cleaning and polishing are mechanical processes – just with water and absolutely no chemicals at all. nora® pads can be used with most standard types of machine and are available in different sizes.

Art. 6627

• For routine cleaning with cleaning machines:

nora® pad 1 – 10"

Diameter 254 mm, delivery unit: 4 pieces in one carton Cleaning with nora® pads nora® pad 1 – 13"

Diameter 330 mm, delivery unit: 4 pieces in one carton nora® pad 1 – 14"

Diameter 356 mm, delivery unit: 4 pieces in one carton nora® pad 1 – 16"

Diameter 406 mm, delivery unit: 4 pieces in one carton

- For routine cleaning with cleaning machines and for initial cleaning with a single disk machine:

nora® pad 1 – 17"

Diameter 431 mm, delivery unit: 1 or 4 pieces in one carton

- For polishing cleaned floor coverings with a high speed machine: nora® pad 1 – 20"

Diameter 508 mm, delivery unit: 1 or 4 pieces in one carton

Art. 6628

- For intermediate and intensive cleaning with a single disk machine: nora® pad 2 – 17"

Diameter 431 mm, delivery unit: 1 or 4 pieces in one carton

Art. 6629

- For intensive cleaning of heavily soiled and scratched floor coverings with a single disk machine:

nora® pad 3 – 17"

Diameter 431 mm, delivery unit: 1 piece in one carton

nora® accessories

TECHNICAL DATA

norament®

|  | Test method | Requirements |  |  |  |  |  |  | Average test results from running production |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | 926 |  | 926 crossline926grano926satura926serra | 825 |  |  |  |  | 992992 grano | 975 LL |
| CE conformity | EN 14 041 |  |  |  |  |  |  | Manufacturer: nora systems GmbH, D-69469 Weinheim |  |  |  |  |  |  |
| DoP-No. | EN 14 041 |  |  |  | 0021 |  |  |  |  |  |  |  | 0004 |  |  |  | 0023 |  | 0024 |  |  |
| Dynamic coeﬃcient of friction | EN 13 893 | DS |  |  |  |  |  |  |  |  |  |  |  |  |  | Fulfilled |  |  |  |  |  |  |  |  |  |  |  |  |
| Reaction to fire | EN 13 501-1 | Not bonded |  |  |  | Cfl-s1 |  |  | Cfl-s1 |  |  |  | Cfl-s2 | Bfl-s1 |
| Reaction to fire | EN 13 501-1 | Bonded on mineral subfl oor |  |  |  | Bfl-s1 |  |  | Bfl-s1 |  |  |  | Cfl-s1 | – |
| Properties acc. to EN 1817/EN 12 199 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Thickness | EN ISO 24 346 | Mean value ± 0.20 mm |  | 4 mm |  |  |  |  |  |  |  |  |  |  |  | 3.2 mm |  |  |  | 9 mm |  |  |  |
|  |  | according to EN 12 199 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | (Art. 1956) |  |  |  |
|  |  | Mean value ± 0.15 mm |  |  |  |  |  | 3.5 mm |  |  |  |  |  |  |  |  | 9 mm | 3.5 mm |
|  |  | according to EN 1817 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | (Art. 1955) |  |
| Dimensional stability | EN ISO 23 999 | ±0.4% |  |  |  |  |  |  |  |  | ±0.3% |  |  |  |  |  |  |  |  |  |  |  |  |  | ±0.1% |  |  |
| Tear strength | ISO 34-1, | Mean value ≥ 20 N/mm |  | 35 N/mm |  |  |  | 35 N/mm |  |  | 30 N/mm |  |  |  | 40 N/mm | 40 N/mm |
|  | method B, procedure A |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Cigarette-burn resistance | EN 1399 | Procedure A (stubbed out) ≥ level 4 |  |  |  |  |  |  |  |  |  |  |  |  |  | Fulfilled |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  | Procedure B (burning) ≥ level 3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Flexibility | EN ISO 24 344, procedure A | Mandrel diameter 20 mm, no fissuring |  |  |  |  |  |  |  |  |  |  |  |  |  | Fulfilled |  |  |  |  |  |  |  |  |  |  |  |  |
| Hardness | ISO 7619 | ≥ 70 Shore A (EN 12 199) |  | 82 Shore A |  |  |  | 82 Shore A |  |  | 87 Shore A |  |  |  | 70 Shore A | 85 Shore A |
|  |  | ≥ 75 Shore A (EN 1817) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Residual indentation | EN ISO 24 343 | Mean value ≤ 0.25 mm at thickness ≥ 3.0 mm |  | 0.15 mm |  |  |  | 0.15 mm |  |  | 0.15 mm |  |  |  | 0.30 mm | 0.07 mm |
|  |  | Mean value ≤ 0.20 mm at thickness ≤ 3.0 mm |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Abrasion resistance | ISO 4649, procedure A | ≤ 250 mm³ |  | 115 mm³ |  |  |  | 115 mm³ |  |  | 130 mm³ |  |  |  | 90 mm³ | 145 mm³ |
| Colour fastness | ISO 105-B02, procedure 3, | At least level 6 on the blue scale; |  |  |  |  |  |  |  |  | Grey scale ≥ level 3 acc. to ISO 105-A02 |  |  |  |  |  |  |  |  |  |
| to artifi cial light | test conditions 6.1 a) | ≥ level 3 on the grey scale (= 350 MJ/m2) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Classifi cation | EN ISO 10 874 | Residential/Commercial/Industrial | 23/34/43 |  | 23/34/43 |  |  |  | 23/32/41 |  |  |  | 23/34/43 |  | 23/34/43 |  |  |
| Additional technical properties |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Toxicity of fire gases | DIN 53 436 |  |  |  | Carbonisation gases |  |  | – |  |  |  |  | – | Carbonisation gases |
|  |  |  |  |  | are non-toxic |  |  |  |  |  |  |  |  | are non-toxic |
| Anti-slip properties | DIN 51 130 | According to BGR 181 |  | R 9 |  |  |  |  | R 9 |  |  | R 9 |  |  |  | R 9 | grano: R 9 |
|  |  |  |  |  |  | serra + crossline = R 10 |  |  |  |  |  |  |  | serra: R 10 |
|  | DIN 51 097 |  |  | A; B |  | serra + crossline A; B |  |  | – |  |  |  |  | – | – |
| Improvement in footfall | ISO 10 140-3 |  |  | 12 dB |  |  |  |  | 10 dB |  |  | 9 dB |  |  |  | 15 dB | 8 dB |
| sound absorption |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Eﬀect of chemicals | EN ISO 26 987 |  |  |  |  |  |  |  | Resistant depending on concentration and time of exposure* |  |  |  |  |  |
| Thermal conductivity | EN 12 667 |  |  | 0.42 W/mK |  |  | 0.42 W/mK |  |  | 0.43 W/mK |  |  |  | 0.21 W/mK | 0.42 W/mK |
|  |  |  |  |  |  |  |  |  |  |  |  | Suitable for underfl oor heating systems |  |  |  |  |  |  |  |  |  |
| Electrical insulation properties | IEC 60 093, VDE 0303 T.30 |  |  |  |  |  |  |  |  |  |  |  |  |  | > 10¹⁰ Ohm |  |  |  |  |  |  |  |  |  |
| Electrical propensity | EN 1815 |  |  |  |  |  |  |  |  | Antistatic, charging in case of rubber soles < 2 kV |  |  |  |  |  |  |  |  |
| when walked upon |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Eﬀect of a castor chair | EN 425 |  |  |  |  |  |  | Suitable if castor wheels, type W, according to EN 12 529 are used |  |  |  |  |
| * In case of increased impact of oils, grease, acids, alkalis and other aggressive chemicals please contact us. |  |  | EN 1817: Specification for homogeneous and heterogeneous smooth elastomer floor coverings |  |  |  |
|  |  |  |  |  | EN 12 199: Specifi cation for homogeneous and heterogeneous profiled elastomer floor coverings |  |  |  |

Colour variations due to diﬀerent production batches as well as technical alterations to improve the product have to be accepted.

01/2015

Technical data | nora systems 55

noraplan®

|  |  | Test method | Requirements |  |  |  |  |  |  |  |  |  | Average test results from running production |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  | uni 2.0 mm |  | eco 2.0 mmsentica2.0 mmsigna2.0mmstone2.0mm |  |  | unita 2.0 mm |  |  | ultra grip 2.0 mm |  |  |  | sentica 3.0 mmsigna3.0mm |  | sentica acousticsignaacousticstoneacoustic |
| CE conformity |  | EN 14 041 |  |  |  |  |  |  |  |  |  | Manufacturer: nora systems GmbH, D-69469 Weinheim |  |  |  |  |  |  |  |  |  |
| DoP-No. |  | EN 14 041 |  | 0018 | 0016 |  |  |  |  |  |  |  | 0010 |  |  | 0016 |  |  |  | 0017 |  |  |  |  |
| Dynamic coeﬃcient of friction |  | EN 13 893 | DS |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Fulfilled |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Reaction to fire |  | EN 13 501-1 | Not bonded |  |  |  | Bfl-s1 |  |  |  | Bfl-s1, bonded |  |  | Cfl-s1 |  |  | Bfl-s1, bonded |  |  | Cfl-s1 |
| Reaction to fire |  | EN 13 501-1 | Bonded on mineral subfl oor |  |  |  | Bfl-s1 |  |  |  |  |  | Bfl-s1 |  |  |  |  |  |  |  |  | Cfl-s1 |  |  |  | Bfl-s1 |  |  | Bfl-s1 |
| Properties acc. to EN 1817 / EN 1816 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Thickness |  | EN ISO 24 346 | Mean value |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  | without foam backing ± 0.15 mm |  |  |  | 2.0 mm |  |  |  |  |  | 2.0 mm |  |  |  |  |  |  | 2.0 mm |  |  |  | 3.0 mm |  |  | – |
|  |  |  | with foam backing ± 0.20 mm |  |  |  | – |  |  |  |  |  | – |  |  |  |  |  |  |  |  | – |  |  |  |  | – |  |  | 4.0 mm |
| Dimensional stability |  | EN ISO 23 999 | ±0.4% |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | ±0.3% |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Cigarette-burn resistance |  | EN 1399 | Procedure A (stubbed out) level ≥ 4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Fulfilled |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  | Procedure B (burning) level ≥ 3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Flexibility |  | EN ISO 24 344, procedure A | Mandrel diameter 20 mm, no fissuring |  |  |  |  |  | Fulfilled |  |  |  |  |  |  |  | Not fulfilled | Fulfilled |  |  |  |  | – |  |  | Fulfilled |  |  |  |  |
| Hardness |  | ISO 7619 | ≥ 75 Shore A | 94 Shore A |  |  |  |  | 92 Shore A |  |  |  |  |  |  | 92 Shore A |  |  |  | 92 Shore A |  | 85 Shore A |
| Residual indentation |  |  | Mean value ≤ 0.15 mm at thickness < 2.5 mm |  |  | 0.05 mm |  |  |  |  | 0.05 mm |  |  |  |  |  |  | 0.05 mm |  |  |  |  | – |  |  | – |
|  |  | EN ISO 24 343 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  | Mean value ≤ 0.20 mm at thickness ≥ 2.5 mm |  |  |  | – |  |  |  |  |  | – |  |  |  |  |  |  |  |  | – |  |  |  | 0.05 mm |  |  | – |
|  |  |  | acoustic: Mean value ≤ 0.25 mm |  |  |  | – |  |  |  |  |  | – |  |  |  |  |  |  |  |  | – |  |  |  |  | – |  | 0.25 mm |
| Abrasion resistance |  | ISO 4649, procedure A | ≤ 250 mm³ |  |  | 130 mm³ |  |  |  |  | 150 mm³ |  |  |  |  |  |  | 90 mm³ |  |  |  | 150 mm³ |  | 130 mm³ |
| Colour fastness |  | ISO 105-B02, procedure 3, | At least level 6 on the blue scale; |  |  |  |  |  |  |  |  |  |  |  |  | Grey scale ≥ level 3 acc. to ISO 105-A 02 |  |  |  |  |  |  |  |  |  |  |  |  |  |
| to artifi cial light |  | test conditions 6.1 a) | ≥ level 3 on the grey scale (= 350 MJ/m2) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Classifi cation |  | EN ISO 10 874 | Residential/Commercial/Industrial | 23/34/42 | 23/34/42 |  |  |  |  |  |  | 23/34/42 |  |  | 23/34/43 |  |  |  | 23/33/– |
| Additional technical properties |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Toxicity of fire gases |  | DIN 53 436 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Carbonisation gases are non-toxic |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Anti-slip properties |  | DIN 51 130 | According to BGR 181 |  |  |  | R 9 |  | stone Art. 149/249: R 10 |  |  | R 11 |  |  |  |  | R 9 |  | stone acoustic: R 10 |
|  |  |  |  |  |  |  |  |  |  |  |  | Others: R 9 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Others: R 9 |
|  |  | DIN 51 097 |  |  |  |  | – |  | stone Art. 149/249: A; B | A;B;C |  |  |  |  | – |  |  | – |
|  |  | BS 7976 |  |  |  |  | – |  |  |  |  |  | – |  |  |  |  |  |  | 36+ |  |  |  |  | – |  |  | – |
|  |  | TRRL Pendulum |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Wet & dry |  |  |  |  |  |  |  |  |
|  |  | SATRA TM 144 |  |  |  |  | – |  |  |  |  |  | – |  |  |  |  |  |  | Wet: > 0.6 |  |  |  |  | – |  |  | – |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Dry: > 0.45 |  |  |  |  |  |  |  |  |
| Improvement in footfall |  | ISO 10 140-3 |  |  |  |  | 6 dB |  |  |  |  |  | 6 dB |  |  |  |  |  |  |  |  | 7 dB |  |  |  | 8 dB |  |  | 20 dB |
| sound absorption |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Eﬀect of chemicals |  | EN ISO 26 987 |  |  |  |  |  |  |  |  |  |  | Resistant depending on concentration and time of exposure* |  |  |  |  |  |  |  |  |  |
| Thermal conductivity |  | EN 12 667 |  | 0.54 W/mK |  |  |  |  | 0.61 W/mK |  |  |  |  |  |  | 0.61 W/mK |  |  |  | 0.61 W/mK |  | 0.12 W/mK |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Suitable for underfl oor heating systems |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Electrical insulation properties |  | IEC 60 093, VDE 0303 T.30 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | > 10¹⁰ Ohm |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Electrical propensity |  | EN 1815 |  |  |  |  |  |  |  |  |  |  |  | Antistatic, charging in case of rubber soles < 2 kV |  |  |  |  |  |  |  |  |  |  |  |
| when walked upon |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Eﬀect of a castor chair |  | EN 425 |  |  |  |  |  |  |  |  |  | Suitable if castor wheels, type W, according to EN 12 529 are used |  |  |  |  |  |  |  |  |
| * In case of increased impact of oils, grease, acids, alkalis and other aggressive chemicals please contact us. |  |  |  | EN 1817: | Specification for homogeneous and heterogeneous smooth elastomer floor coverings |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  | EN 1816: | Specifi cation for homogeneous and heterogeneous smooth elastomer floor coverings with foam backing |

Colour variations due to diﬀerent production batches as well as technical alterations to improve the product have to be accepted.

Technical data

01/2015

- nora systems | Technical data

nora® ESD floor coverings

|  | Test method | Requirements |  |  |  |  |  |  |  |  | Average test results from running production |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  | norament® |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | noraplan® |  |  |
|  |  |  |  | 928 ed |  |  |  |  |  | 928 grano ed |  |  |  | 927 grano ec |  |  |  | sentica ed 2.0 mmsignaed2.0mmstoneed2.0mm |  |  |  | sentica ed 3.0 mmsignaed3.0mm | astro ec |
| CE conformity | EN 14 041 |  |  |  |  |  |  |  | Manufacturer: nora systems GmbH, D-69469 Weinheim |  |  |  |  |  |  |
| DoP-No. | EN 14 041 |  | 0005 |  |  | 0005 |  |  |  | 0022 |  |  | 0001 |  |  |  | 0001 |  |  |  | 0011 |  |
| Dynamic coeﬃcient of friction | EN 13 893 | DS |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Fulfilled |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Electrical behaviour | EN 1081 | ed = ≤ 109 Ohm |  |  |  | Fulfilled |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Fulfilled |  |  |  |  |  |  |  |  |  |
|  |  | ec = ≤ 106 Ohm |  |  |  |  |  |  |  |  |  |  |  |  | Fulfilled |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Fulfilled |
| Reaction to fire | EN 13 501-1 | Not bonded |  | Cfl-s1, bonded |  |  |  | Cfl-s2 |  |  |  |  |  |  |  |  |  |  |  |  |  | Cfl-s1 |  |  |  |  |  |
| Reaction to fire | EN 13 501-1 | Bonded on mineral subfl oor |  |  |  | Bfl-s1 |  |  |  | Cfl-s1 |  |  |  |  |  |  |  | Bfl-s1 | Cfl-s1 |
| Properties acc. to EN 1817/EN 12 199 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Thickness | EN ISO 24 346 | Mean value ± 0.20 mm according to EN 12 199 |  | 4 mm |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  | Mean value ± 0.15 mm according to EN 1817 |  |  |  |  |  |  | 3.5 mm |  |  | 3.5 mm |  |  |  |  |  |  | 2.0 mm |  |  |  | 3.0 mm | 2.0 mm |
| Dimensional stability | EN ISO 23 999 | ±0.4% |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | ±0.3% |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Tear strength | ISO 34-1, | Mean value ≥ 20 N/mm |  |  | 45 N/mm |  |  | 30 N/mm |  |  |  |  |  |  |  |  |  |  |  |  |  | – |  |  |
|  | method B, procedure A |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Cigarette-burn resistance | EN 1399 | Procedure A (stubbed out) ≥ level 4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Fulfilled |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  | Procedure B (burning) ≥ level 3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Flexibility | EN ISO 24 344, procedure A | Mandrel diameter 20 mm, no fissuring |  |  |  |  |  |  |  |  |  |  | Fulfi lled |  |  |  |  |  |  |  |  |  |  |  |  |  |  | – | Fulfi lled |
| Hardness | ISO 7619 | ≥ 70 Shore A (EN 12 199) |  |  | 84 Shore A |  |  |  |  |  | 90 Shore A |  |  |  |  |  |  |  |  |  |  |  | 95 Shore A |  |  |  |  |
|  |  | ≥ 75 Shore A (EN 1817) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Residual indentation |  | Mean value ≤ 0.15 mm at thickness < 2.5 mm |  |  |  |  |  |  |  |  | – |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0.05 mm |  |  |
|  |  | Mean value ≤ 0.20 mm at thickness ≥ 2.5 mm |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | EN ISO 24 343 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  | Mean value ≤ 0.25 mm at thickness ≥ 3.0 mm |  |  |  |  |  | 0.05 mm |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | – |  |  |
|  |  | Mean value ≤ 0.20 mm at thickness ≤ 3.0 mm |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Abrasion resistance | ISO 4649, procedure A | ≤ 250 mm³ |  |  |  | 80 mm3 |  |  | 70 mm3 |  |  |  |  |  |  | 150 mm³ | 150 mm³ |
| Colour fastness | ISO 105-B02, procedure 3, | At least level 6 on the blue scale; |  |  |  |  |  |  |  |  |  |  |  |  | Grey scale ≥ level 3 acc. to ISO 105-A02 |  |  |  |  |  |  |  |  |  |  |  |  |
| to artifi cial light | test conditions 6.1 a) | ≥ level 3 on the grey scale (= 350 MJ/m2) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Classifi cation | EN ISO 10 874 | Residential/Commercial/Industrial |  |  | 23/34/43 |  |  |  |  |  |  |  | 23/34/42 |  |  | 23/34/43 |  | 23/34/42 |
| Additional technical properties |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Toxicity of fire gases | DIN 53 436 |  | Carbonisation gases are non-toxic |  |  | – |  |  |  |  |  |  | Carbonisation gases are non-toxic |
| Anti-slip properties | DIN 51 130 | According to BGR 181 |  |  |  |  |  |  |  |  | R 9 |  |  |  |  |  |  |  |  |  |  |  | stone ed: | R 10 | R 9 |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Others: | R 9 |  |
| Improvement in footfall | ISO 10 140-3 |  |  | 12 dB |  |  |  |  |  | 10 dB |  |  |  | 10 dB |  |  |  |  |  |  | 6 dB |  |  |  | 7 dB | 6 dB |
| sound absorption |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Eﬀect of chemicals | EN ISO 26 987 |  |  |  |  |  |  |  |  |  | Resistant depending on concentration and time of exposure* |  |  |  |  |
| Thermal conductivity | EN 12 667 |  |  |  | 0.40 W/mK |  |  | 0.56 W/mK |  |  |  |  |  |  | 0.54 W/mK | 0.45 W/mK |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Suitable for underfl oor heating systems |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Eﬀect of a castor chair | EN 425 |  |  |  |  |  |  |  | Suitable if castor wheels, type W, according to EN 12 529 are used |  |  |  |
| Electrical behaviour** |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Resistance to EPA ground | ESD STM 7.1/ | Measuring the installed floor at 23 °C (± 2 °C) and ≥ 25 % r.h. |  | 10⁶ – 9 x 10⁷ Ohm |  |  | < 10⁶ Ohm |  |  |  |  |  |  | 10⁶ – 9 x 10⁷ Ohm | < 10⁶ Ohm |
|  | IEC 61 340-4-1 | Measuring the installed floor at 23 °C (± 2 °C) and < 25 % r.h., |  | 10⁶ – 10⁹ Ohm*** |  |  | < 10⁶ Ohm |  |  |  |  |  |  | 10⁶ – 10⁹ Ohm*** | < 10⁶ Ohm |
|  |  | installed on an appropriate subfl oor build up |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Operator system – | ESD STM 97.1/ | For the system floor/conductive footwear (R < 5 x 106 Ohm) |  | ≤ 3.5 x 10⁷ Ohm |  |  | < 3.5 x |  |  |  |  |  |  | ≤ 3.5 x 10⁷ Ohm | < 3.5 x |
| Resistance to ground | IEC 61 340-4-5 | measuring the installed floor at 23 °C (± 2 °C) and ≥ 25 % r.h. |  |  |  |  | 10⁷ Ohm |  |  |  |  |  |  |  | 10⁷ Ohm |
| Body voltage generation | ESD STM 97.2 | Tested with defi ned conductive footwear |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | <10V |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | IEC 61 340-4-5 | with 21 °C and 20 % r.h. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Resistance to earth | EN 1081 |  |  | 10⁶ – 9 x 10⁷ Ohm |  |  | < 10⁶ Ohm |  |  |  |  |  |  | 10⁶ – 9 x 10⁷ Ohm | < 10⁶ Ohm |
| Insulation resistance | VDE 0100 - 600 |  |  | ≥ 5 x 10⁴ Ohm |  |  |  | – |  |  |  |  |  |  | ≥ 5 x 10⁴ Ohm | – |

- In case of increased impact of oils, grease, acids, alkalis and other aggressive chemicals please contact us.

- If installed electrically dissipative and conductive in conformity with our installation instruction and according to the recommendations of the adhesive manufacturer.

The used adhesive has to have a permanent resistance of R < 3 x 105 Ohm according to EN 13 415.

- If extremely low humidity values (< 25 % relative air humidity (= r.h.) are expected for a longer period, please contact nora systems GmbH, Technical Service, for advice.

EN 1817:	Specifi cation for homogeneous and heterogeneous smooth elastomer floor coverings

EN 12 199: Specifi cation for homogeneous and heterogeneous profiled elastomer floor coverings

Colour variations due to diﬀerent production batches as well as technical alterations to improve the product have to be accepted.

01/2015

nora systems 57

- nora systems

Notes

nora systems 59

Please note:

norament® and noraplan® have been developed for indoor

installation. nora® floor coverings are not suitable for installation

in outdoor applications or in areas with constant and direct wet

loads.

The particulars given in this brochure are for informational

purposes only concerning the products presented. They represent

descriptions or designations, but not any warranted qualities. This

information cannot cover all possible service conditions which our

floor coverings may encounter.

If the floor covering is going to be exposed to out-of-the-ordinary

service conditions and stresses (e.g. extreme UV radiation,

chemical substances or other aggressive media), please contact

us for advice.

We will be pleased to supply you on request with flooring

samples to enable you to carry out in-house tests. We reserve

the right to alter technical values as part of an ongoing product

improvement process.

This brochure as well as the pictures and illustrations

it contains are subject to a copyright owned by nora systems

GmbH, Weinheim, and may be used with its previous written

approval only.

Printed on 100 % chlorine-free bleached paper.

nora systems Shanghai Co. Ltd.

10 A/B, Long Life Building | 1566 Yan’an Road West | 200052 Shanghai, PR China Tel.: +86 21 - 3226 0077 | Fax: +86 21 - 5258 1958 www.nora.com/cn

nora systems GmbH (DMCC Branch)

2008 HDS Business Centre | Jumeirah Lakes Towers | PO Box 478392 | Dubai, UAE Tel.: +971 (4) 450 8175 | Fax: +971 (4) 450 8374 E-Mail: info@nora.com

www.nora.com/corp

nora flooring systems UK Ltd.

4–5 Allerton Road | Rugby CV23 0PA, Great Britain

Direct Dial Numbers: (01788) 513 160 – 513 169

Fax: (01788) 55 28 12

E-Mail: info-uk@nora.com

www.nora.com/uk

nora systems GmbH

Höhnerweg 2–4 | 69469 Weinheim, Germany

Tel.: +49 (0) 6201 - 80 66 33

E-Mail: info@nora.com

www.nora.com

117427.01/2015 A.