STANLEY COMMERCIAL HARDWARE

Full Line Catalog

STANLEY Commercial Hardware

Trusted experts. Proven reliability. Simply STANLEY.

When trust is earned, confidence is secured.

Backed by the strength and trust of our brand, Stanley Commercial Hardware products are designed to fit a variety of commercial applications. The door hardware in retail, banks, multi-family housing, assisted living facilities and other commercial buildings all have constant traffic that need to withstand continuous use and abuse.

The Stanley Commercial Hardware line of mechanical locks, exits, and closers delivers quality and durability at a mid-price point value. We’re easy to do business with, shipping all of our products from a single location and providing the industry’s best lead times. And most importantly, we ensure that trust is always built-in. Trust in the reliable performance our products provide, and in the heritage of the Stanley brand.

Security solutions are among your most important decisions. Make a choice in which you can have total confidence: Stanley Commercial Hardware.

Trusted experts. Proven reliability. Simply STANLEY.

Vertical Markets

Stanley Commercial Hardware products are an ideal fit for a variety of commercial applications and include the following market segments:

| Multi-Family/Multi-Use | Medical Office Buildings (MOB) |
| --- | --- |
| Retail/Strip Malls | Industrial |
| Commercial Office Buildings | Banking |
| Assisted Living/Nursing Homes | Other Commercial |

Table Of Contents

Intro	2

Vertical Markets	4

Spec Writing Services	6

Warranty	7

Mechanical Locks	8

Mortise Locks – Grade 1	9

QMS100 – Sectional

QME100 – Escutcheon

QML100 – Deadlock

Cylindrical Locks – Grade 1	15

QCL100 Series

Cylindrical Locks – Grade 2	19

QCL200 Series

Interconnected Locks – Grade 2	22

QCI200 Series

Tubular Locks – Grade 2	25

QTL200 Series

Auxiliary Deadbolts – Grade 1	28

QDB100 Series

Auxiliary Deadbolts – Grade 2	31

QDB200 Series

Keys and Cores	34

Exit Devices	36

Heavy-Duty – Grade 1	37

QED100 Series

QRM100 Series

QET100 Series

Heavy-Duty Narrow Stile – Grade 1	48

QED200 Series

QET200 Series

Standard-Duty – Grade 1	56

QED300 Series

QRM300 Series

QET300 Series

Standard-Duty – Grade 1	65

QRT300 Series

Door Closers	67

Extra Heavy-Duty – Grade 1	68

QDC100 Series

Heavy-Duty – Grade 1	71

QDC200 Series

Standard-Duty – Grade 1	74

QDC300 Series

Miscellaneous	77

Windstorm- & Hurricane-Compliance	78

Competitive Cross-Reference	80

Full Line Catalog STANLEY Commercial Hardware	5

Spec Writing Services

What does the Spec Writing Services division do?

Our staff of Architectural Hardware Consultants (AHC), Application Engineers, and security experts specialize in specification writing, owner specification manual drafting, section coordination, shop drawing and submittal review, and continuing education (American Institute of Architects – Continuing Education Systems).

Our expertise covers many specification sections including the following:

- 08 42 29Automatic Entrances

- 08 42 33Revolving Door Entrances

- 08 42 36Balanced Door Entrances

- 08 42 43ICU/CCU Entrances

- 08 71 00Door Hardware

- 08 71 13Automatic Door Operators

- 08 74 00Access Control Hardware

- 27 52 13Patient Monitoring & Telemetry Systems

- 27 52 23Nurse Call / Code Blue Systems

- 28 13 00Access Control

- 28 16 00Intrusion Detection

- 28 23 00Video Surveillance

- 28 46 00Electronic Detention Monitoring

  - Control Systems

From project review to system design and construction administration, we are equipped to provide the support to accurately and effectively assist you every step of the way with your project's architectural hardware, automatic entrance, and security system requirements.

For more information on how we can assist you, call our office to get in contact with an Architectural Construction Representative near you.

1-855-365-2407

- Full Line Catalog STANLEY Commercial Hardware

Warranty

Limited Lifetime Mechanical Warranty

3-Year Finish Warranty

1-Year Electrical Warranty

This product comes with a limited lifetime mechanical warranty and a three-year finish warranty to the original user of the Stanley Commercial Hardware product against defects in material and workmanship as long as the original user occupies/manages the premises upon which the product was originally installed. The warranty DOES NOT COVER scratches; abrasions; deterioration due to the use of paints, solvents and other chemicals; abuse; or misuse, and DOES NOT COVER US10B/613 “Oil Rubbed Bronze” finish as it is a “Living Finish” and a change in appearance is the natural characteristic of the finish. This warranty DOES NOT COVER 6CS and 7CS products as they have a 3-year warranty from the date of sale. This warranty DOES NOT COVER defects caused by improper installation or field modification. This warranty DOES NOT COVER the cost incurred in removing and installing

a replacement product. Upon return of a defective product, dormakaba may repair or replace the product or refund the purchase price. dormakaba is not liable for incidental or consequential damages. Some states do not allow the exclusion or limitation of incidental or consequential damages, so this may not apply to you. This warranty gives you specific legal rights and you may also have other rights that vary from state to state. If a mechanical or finish defect occurs, please call dormakaba at:

Product Support

6161 E. 75th Street

Indianapolis, IN 46250

1-855-365-2407

Full Line Catalog STANLEY Commercial Hardware	7

Mechanical Locks

QMS/QME 100 Series: Grade 1 Heavy-Duty Mortise Locks

Performance Features

• Tested to meet Grade 1 specification of 1,000,000 cycles.

• Clutching mechanism standard.

•	Thru-bolt design and heavy-duty spring tension provides longer performance life and prevents lever sag.

• ADA-compliant thumbturn.

• Mortise case is easily field reversible.

• Pre-assembled trims with spring-loaded spindles automatically adjust to

|  | door thickness and reduce installation time. |  |  |
| --- | --- | --- | --- |
| • | Partial security separator prevents spindle manipulation. | Escutcheon Sierra (E) | Escutcheon Slate (A) |
| • | Anti-friction throwbolt. |  |  |

Certifications

- ANSI/BHMA A156.13 – Grade 1

- UL/cUL listed (3 hours) for “A” label single-door applications (4' x 8') (1.219m x 2.438m)

- UL10C/UBC 7-2 (1997) Positive Pressure Rated

- UL10B Pressure Rated

- ADA-Compliant ANSI A117.1 Accessibility Code

- California State Reference Code (formerly Title 19 – Fire Marshal)

Product Specifications

- Template – 3 5⁄8" (92mm).

- Solid forged brass trim construction.

- Dual 8mm spindles.

- 1" (25.4mm) stainless steel deadbolt.

- Floating mounting tabs adjust to door bevel.

- Toggle button locking.

- Heavy gauge steel armor faceplate.

- Door thickness

–Sectional: 1 3⁄4" - 2" (44.5mm-51mm) standard; (57mm) optional

–Escutcheon: 1 3⁄4" - 2 1⁄4" (44.5mm-57mm) standard

Keying

- 6-pin or 5-pin cylinders. Many keying options available from our factory to include, but not limited to, master keying, grand master keying, and construction keying.

- 2 keys per lockset.

- Offered with the following keyway options: BF-BEST "F" SFIC, KW-Kwikset, WE-Weiser, SC-Schlage, GA-Yale, LA-Sargent, & LC-Less Cylinder.

Consult factory for other cylinder options.

Warranty

- Lifetime Mechanical, 3-year finish*, 1-year electrical

*(613/US10B carries no finish warranty)

Sectional Summit (M)

Functions

| ANSI | Series | Description |
| --- | --- | --- |
| — | QMS/QME120 | Single Dummy |
| — | QMS/QME122 | Full Dummy |
| F01 | QMS/QME130 | Passage |
| F22 | QMS/QME140 | Privacy |
| F19 | QMS/QME145 | Privacy w/ Deadbolt |
| F04 | QMS/QME150 | Entry |
| F13 | QMS/QME152 | Exit |
| F20 | QMS/QME154 | Corridor |
| F11 | QMS/QME158 | Dormitory |
| F05 | QMS/QME160 | Classroom |
| F32 | QMS/QME162 | Classroom Security |
| F09 | QMS/QME164 | Apartment |
| F07 | QMS/QME170 | Storeroom |
| F30 | QMS/QME172 | Institutional |
| F14 | QMS/QME174 | Store Door |

Finishes

| BHMA | US | Description |
| --- | --- | --- |
| 605 | US3 | Bright Brass |
| 613 | US10B | Oil Rubbed Bronze |
| 619 | US15 | Satin Nickel |
| 625 | US26 | Bright Chrome |
| 626 | US26D | Satin Chrome |

MECHANICAL LOCKS

| Full Line Catalog STANLEY Commercial Hardware | 9 |
| --- | --- |

MECHANICAL LOCKS

QMS/QME 100 Series: Grade 1 Heavy-Duty Mortise Locks

| Functions | ANSI |  |  |  |  | Description | Latch | Deadbolt | Auxiliary | Toggle | Cylinders | Case |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  | Bolt |  |  |  |  | Qty |
|  |  |  |  |  |  | Lever trim on one side |  |  |  |  |  |  |
| QMS/ |  |  |  |  |  | (no mortise case). |  |  |  |  |  |  |
| QME120 | — |  |  |  |  |  |  |  |  |  |  | 4 |
| Single Dummy |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  | Lever trim on both sides |  |  |  |  |  |  |
| QMS/ |  |  |  |  |  | (no mortise case). |  |  |  |  |  |  |
| QME122 | — |  |  |  |  |  |  |  |  |  |  | 4 |
| Full Dummy |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  | Latch bolt operated by lever from |  |  |  |  |  |  |
| QMS/ |  |  |  |  |  | either side at all times. |  |  |  |  |  |  |
| QME130 | F01 |  |  |  |  |  | X |  |  |  |  | 4 |
| Passage |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  | Latch bolt operated by lever from |  |  |  |  |  |  |
|  |  |  |  |  |  | either side except when outside |  |  |  |  |  |  |
| QMS/ |  |  |  |  |  | lever is locked by inside trim or |  |  |  |  |  |  |
| QME140 | F22 |  |  |  |  | button. Operating inside lever, | X |  |  |  |  | 4 |
|  |  |  |  |  |  | closing door or operating outside |  |  |  |  |  |  |
| Privacy |  |  |  |  |  | emergency release (accessible |  |  |  |  |  |  |
|  |  |  |  |  |  | under emergency cap) unlocks |  |  |  |  |  |  |
|  |  |  |  |  |  | outside lever. |  |  |  |  |  |  |
|  |  |  |  |  |  | Latch bolt operated by lever from |  |  |  |  |  |  |
| QMS/ |  |  |  |  |  | either side. Deadbolt operated by |  |  |  |  |  |  |
|  |  |  |  |  |  | turn from inside and emergency |  |  |  |  |  |  |
| QME145 | F19 |  |  |  |  | release from outside (accessible | X | X |  |  |  | 4 |
| Privacy w/ |  |  |  |  |  | under emergency cap). Operating |  |  |  |  |  |  |
|  |  |  |  |  |  | inside lever retracts both bolts. |  |  |  |  |  |  |
| Deadbolt |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  | Latch bolt operated by lever |  |  |  |  |  |  |
|  |  |  |  |  |  | from either side except when |  |  |  |  |  |  |
| QMS/ |  |  |  |  |  | outside lever is made inoperative |  |  |  |  |  |  |
| QME150 | F04 |  |  |  |  | by toggle. When outside lever is | X |  | X | X | Sgl | 4 |
|  |  |  |  |  |  | locked, latch bolt is retracted by |  |  |  |  |  |  |
| Entry |  |  |  |  |  | key from outside or by operating |  |  |  |  |  |  |
|  |  |  |  |  |  | inside lever. Auxiliary dead latch |  |  |  |  |  |  |
|  |  |  |  |  |  | deadlocks latch bolt. |  |  |  |  |  |  |
|  |  |  |  |  |  | Latch bolt operated by lever from |  |  |  |  |  |  |
|  |  |  |  |  |  | either side. Deadbolt is projected |  |  |  |  |  |  |
| QMS/ |  |  |  |  |  | by key from outside and turn |  |  |  |  |  |  |
| QME152 | F13 |  |  |  |  | piece from inside. Operating | X | X |  |  | Sgl | 4 |
|  |  |  |  |  |  | inside lever retracts both bolts and |  |  |  |  |  |  |
| Exit |  |  |  |  |  | unlocks outside. |  |  |  |  |  |  |
|  |  |  |  |  |  | Latch bolt operated by lever from |  |  |  |  |  |  |
|  |  |  |  |  |  | either side, except when outside |  |  |  |  |  |  |
|  |  |  |  |  |  | lever is made inoperative by |  |  |  |  |  |  |
|  |  |  |  |  |  | toggle. Deadbolt operated by key |  |  |  |  |  |  |
| QMS/ |  |  |  |  |  | outside or turn inside. Key outside |  |  |  |  |  |  |
|  |  |  |  |  |  | operates both bolts. Operating |  |  |  |  |  |  |
| QME154 | F20 |  |  |  |  | inside lever retracts both bolts | X | X |  | X | Sgl | 4 |
| Corridor |  |  |  |  |  | and outside remains locked. Latch |  |  |  |  |  |  |
|  |  |  |  |  |  | bolt is deadlocked when outside |  |  |  |  |  |  |
|  |  |  |  |  |  | lever is made inoperative or when |  |  |  |  |  |  |
|  |  |  |  |  |  | the deadbolt is projected. When |  |  |  |  |  |  |
|  |  |  |  |  |  | deadbolt is retracted, lever is |  |  |  |  |  |  |
|  |  |  |  |  |  | unlocked by toggle. |  |  |  |  |  |  |

- Full Line Catalog STANLEY Commercial Hardware

QMS/QME 100 Series: Grade 1 Heavy-Duty Mortise Locks

| Functions | ANSI |  |  |  | Description | Latch | Deadbolt | Auxiliary | Toggle | Cylinders | Case |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | Bolt |  |  |  |  | Qty |
|  |  |  |  |  | Latch bolt operated by lever from |  |  |  |  |  |  |
|  |  |  |  |  | either side except when outside |  |  |  |  |  |  |
| QMS/ |  |  |  |  | lever is made inoperative |  |  |  |  |  |  |
|  |  |  |  |  | by toggle. Deadbolt projected by |  |  |  |  |  |  |
| QME158 | F11 |  |  |  | key from either side. Deadbolt | X | X |  | X | Dbl | 4 |
| Dormitory |  |  |  |  | retracted by key from outside. |  |  |  |  |  |  |
|  |  |  |  |  | Both bolts retracted by inside |  |  |  |  |  |  |
|  |  |  |  |  | lever and outside remain locked. |  |  |  |  |  |  |
|  |  |  |  |  | Latch bolt operated by lever from |  |  |  |  |  |  |
|  |  |  |  |  | either side except when outside |  |  |  |  |  |  |
| QMS/ |  |  |  |  | lever is made inoperative |  |  |  |  |  |  |
|  |  |  |  |  | by key from outside. Inside lever |  |  |  |  |  |  |
| QME160 | F05 |  |  |  | always operative. Auxiliary dead | X |  | X |  | Sgl | 4 |
| Classroom |  |  |  |  | latch deadlocks latch bolt. |  |  |  |  |  |  |
|  |  |  |  |  | Latch bolt operated by lever |  |  |  |  |  |  |
|  |  |  |  |  | from either side except when |  |  |  |  |  |  |
| QMS/ |  |  |  |  | outside lever is locked from |  |  |  |  |  |  |
|  |  |  |  |  | inside or outside by key. When |  |  |  |  |  |  |
| QME162 | F32 |  |  |  | outside lever is locked, latch | X |  | X |  | Dbl | 4 |
| Classroom |  |  |  |  | bolt is retracted by key from |  |  |  |  |  |  |
|  |  |  |  |  | inside or outside or by operating |  |  |  |  |  |  |
| Security |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  | inside lever. Auxiliary dead latch |  |  |  |  |  |  |
|  |  |  |  |  | deadlocks latch bolt. |  |  |  |  |  |  |
|  |  |  |  |  | Latch bolt operated by lever from |  |  |  |  |  |  |
|  |  |  |  |  | either side, except when outside |  |  |  |  |  |  |
| QMS/ |  |  |  |  | lever is locked by key from inside. |  |  |  |  |  |  |
|  |  |  |  |  | When outside lever is locked, |  |  |  |  |  |  |
| QME164 | F09 |  |  |  | latch bolt is retracted by key | X |  | X |  | Dbl | 4 |
| Apartment |  |  |  |  | from outside or by operating |  |  |  |  |  |  |
|  |  |  |  |  | inside lever. Auxiliary dead latch |  |  |  |  |  |  |
|  |  |  |  |  | deadlocks latch bolt. |  |  |  |  |  |  |
|  |  |  |  |  | Latch bolt operated by key from |  |  |  |  |  |  |
|  |  |  |  |  | outside or by operating inside |  |  |  |  |  |  |
| QMS/ |  |  |  |  | lever. Outside lever is always |  |  |  |  |  |  |
|  |  |  |  |  | inoperative. Auxiliary dead latch |  |  |  |  |  |  |
| QME170 | F07 |  |  |  | deadlocks latch bolt. | X |  | X |  | Sgl | 4 |
| Storeroom |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  | Latch bolt operated by key from |  |  |  |  |  |  |
|  |  |  |  |  | either side. Both levers always |  |  |  |  |  |  |
| QMS/ |  |  |  |  | inoperative. Auxiliary dead latch |  |  |  |  |  |  |
|  |  |  |  |  | deadlocks latch bolt. |  |  |  |  |  |  |
| QME172 | F30 |  |  |  |  | X |  | X |  | Dbl | 4 |
| Institutional |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  | Latch bolt operated by lever from |  |  |  |  |  |  |
|  |  |  |  |  | either side. Deadbolt operated by |  |  |  |  |  |  |
| QMS/ |  |  |  |  | key from either side. |  |  |  |  |  |  |
| QME174 | F14 |  |  |  |  | X | X |  |  | Dbl | 4 |
| Store Door |  |  |  |  |  |  |  |  |  |  |  |

MECHANICAL LOCKS

Full Line Catalog STANLEY Commercial Hardware	11

How to Order

QMS/QME 100 Series: Grade 1 Heavy-Duty Mortise Locks

MECHANICAL LOCKS

Example

If you ordered: QME160 E626 KW6 KD

You would get: Grade 1 Classroom Mortise Lock, Sierra Lever Escutcheon Trim, Satin Chrome, Kwikset Keyway, Keyed Different.

- Single Dummy

- Full Dummy

- Passage

- Privacy

- Privacy w/ Deadbolt

- Entry

- Exit

- Corridor

- Dormitory

- Classroom

- Classroom Security

- Apartment

| 70 | Storeroom |  | E | Sierra |
| --- | --- | --- | --- | --- |
|  |  |  | M | Summit |
| 72 | Institutional |  |  |  |
|  |  |  | A | Slate |
| 74 | Store Door |  |  |  |

| KD | Keyed Different |
| --- | --- |
| KA | Keyed Alike |
| SK | Special Keying |
|  | -Construction Keyed |
|  | -Construction Master Keyed |
|  | -Maison Keyed |
|  | -Master Keyed |
|  | -Grand Master Keyed |
|  | -Great Grand Master Keyed |
| ZB | Zero Bitted |

|  |  |  |  |  |  |  |  | Base Part Number |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | Series |  | Function |  | Design |  | Finish |  | Keyway |  | # of Pins | Keying |  |
|  |  | QME1 |  | 60 |  | E |  | 626 |  |  |  | KW |  | 6 | KD |  |
| Escutcheon Trim | QME1 |  |  | 605 |  | Bright Brass |  |  |  |  |  | BF | BEST "F" SFIC |  |  |
| Sectional Trim | QMS1 |  |  |  |  |  |  |  |  |  |  |  | KW | Kwikset “KW” |  |  |
|  |  |  |  | 613 |  | Oil Rubbed Bronze |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  | WE | Weiser “E” |  |  |
|  |  |  |  |  |  | 619 |  | Satin Nickel |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  | SC | Schlage “C” |  |  |
|  |  |  |  |  |  | 625 |  | Bright Chrome |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  | GA | Yale “GA” |  |  |
|  |  |  |  |  |  | 626 |  | Satin Chrome |  |  |  |  |  | LA | Sargent “LA” |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | LC | Less Cylinder |  |  |

- Full Line Catalog STANLEY Commercial Hardware

QML 100 Series: Grade 1 Heavy-Duty Mortise Deadlocks

| Functions | ANSI | Description | Case Qty |
| --- | --- | --- | --- |
| QML180 | E06071 | Deadbolt operated by key from outside and | 10 |
| Single Cylinder |  | by turn from inside. |  |
| QML182 | E06061 | Deadbolt operated by key from either side. | 10 |
| Double Cylinder |  |  |  |
| QML184 | E06061 | Deadbolt operated by key from one side only. | 10 |
| Cylinder Only |  |  |  |
| QML186 | E06061 | Deadbolt operated by key from outside. Turn on inside retracts | 10 |
| Classroom* |  | but does not project the deadbolt. |  |

MECHANICAL LOCKS

NOTES: Consult factory for lead times on 605, 619 & 625 finishes.

*Classroom function requires handed cylinder turn. Specify handing when ordering.

Full Line Catalog STANLEY Commercial Hardware	13

How to Order

QML 100 Series: Grade 1 Heavy-Duty Mortise Deadlocks

Example

If you ordered: QML186 626 RH KW6 KD

You would get: Grade 1 Classroom Mortise Lock, Satin Chrome,

Right-Hand, Kwikset Keyway, Keyed Different.

LOCKS

- Single Cylinder

- Double Cylinder

- Cylinder Only

- Classroom

| KD | Keyed Different |
| --- | --- |
| KA | Keyed Alike |
| SK | Special Keying |
|  | -Construction Keyed |
|  | -Construction Master Keyed |
|  | -Maison Keyed |
|  | -Master Keyed |
|  | -Grand Master Keyed |
|  | -Great Grand Master Keyed |
| ZB | Zero Bitted |

MECHANICAL

Base Part Number

| Series | Function | Finish | Handing* | Keyway | # of Pins | Keying |
| --- | --- | --- | --- | --- | --- | --- |
| QML1 | 86 | 626 | RH | KW | 6 | KD |

| 605 | Bright Brass |
| --- | --- |
| 613 | Oil Rubbed Bronze |
| 619 | Satin Nickel |

- Bright Chrome

- Satin Chrome

| BF | BEST "F" SFIC |
| --- | --- |
| KW | Kwikset “KW” |
| WE | Weiser “E” |
| SC | Schlage “C” |
| GA | Yale “GA” |
| LA | Sargent “LA” |
| LC | Less Cylinder |

QML186 Only*

| RH | Right Hand |
| --- | --- |
| LH | Left Hand |

NOTES: Consult factory for lead times on 605, 619 & 625 finishes.

*Classroom function requires handed cylinder turn. Specify handing when ordering.

- Full Line Catalog STANLEY Commercial Hardware

QCL 100 Series: Grade 1 Heavy-Duty Cylindrical Locks

Performance Features

- Tested to meet Grade 1 specification of 800,000 cycles.

- Standard clutching mechanism provides resistance to damage caused by physical force.

- Thru-bolt design and heavy-duty spring tension provides longer performance life and prevents lever sag.

• Concealed mounting screws.	Sierra (E)	Summit (M)

- Compartmentalized packaging allows for quick and easy installation.

Certifications

- ANSI/BHMA A156.2 Series – Grade 1

- ANSI A117.1 Accessibility Code (ADA Compliant)

- UL/cUL Listed (3 hours) for “A” label single-door applications (4' x 8') (1.219m x 2.438m)

- UL10C/UBC 7-2 (1997) Positive Pressure Rated

- UL10B Pressure Rated

- California State Reference Code (formerly Title 19 – Fire Marshal)

- Hurricane Compliant – Miami-DADE N.O.A. See page 78 for more details.

Product Specifications

- Handing – All QCL100 Series Levers Locksets are non-handed.

- Door thickness – 1 3⁄8" - 2" (35mm-51mm) standard.

- Backset – 2 3⁄4" (70mm) square standard. 2 3⁄8" and 5" (60mm, 127mm) available.

- Exposed trim – Pressure cast zinc, plated to match finish designation.

- Strike – ANSI Strike 1 1⁄4" x 4 7⁄8" (32mm x 124mm) standard. Other strike options also available.

- Door prep – 2 1⁄8" (54mm) diameter cross bore.

- Latch bolt – Keyed/Exterior 1⁄2" (12.7mm) steel throw; Interior 1⁄2" (12.7mm) spring latch.

- Latch faceplate – 1 1⁄8" x 2 1⁄4" (29mm x 57mm) standard.

- Single dummy is surface mounted.

- Electrification options available.

Keying

- 6-pin non-IC brass cylinders. 6 or 7 pin SFIC option available. Many keying options available from our factory to include, but not limited to, master keying, grand master keying and construction keying.

- 2 keys per lockset.

- Offered with the following keyway options: BF-BEST "F" SFIC, KW-Kwikset, WE-Weiser, SC-Schlage, GA-Yale, LA-Sargent, & LC-Less Cylinder. Consult factory for other cylinder options.

Warranty

- Lifetime Mechanical, 3-year finish,* and 1-year electrical

*(613/US10B carries no finish warranty)

Slate (A)

Functions

| ANSI | Series | Description |
| --- | --- | --- |
| — | QCL120 | Single Dummy |
| F75 | QCL130 | Passage |
| F111 | QCL135 | Communicating |
| F76 | QCL140 | Privacy |
| F109 | QCL150 | Entry/Office |
| F109 | QCL151 | Entry/Office SFIC |
| F90 | QCL154 | Corridor |
| F90 | QCL155 | Corridor SFIC |
| F84 | QCL160 | Classroom |
| F84 | QCL161 | Classroom SFIC |
| F110 | QCL168 | Classroom Security |
| F110 | QCL169 | Classroom Security SFIC |
| F86 | QCL170 | Storeroom |
| F86 | QCL171 | Storeroom SFIC |
| — | QCL192 | Electronically Locked |
| — | QCL193 | Electronically Locked SFIC |
| — | QCL194 | Electronically Unlocked |
| — | QCL195 | Electronically Unlocked SFIC |

Finishes

| BHMA | Description |
| --- | --- |
| 605 | Bright Brass |
| 613 | Oil Rubbed Bronze |
| 619 | Satin Nickel |

- Bright Chrome

- Satin Chrome

| Full Line Catalog STANLEY Commercial Hardware | 15 |
| --- | --- |

MECHANICAL LOCKS

MECHANICAL LOCKS

QCL 100 Series: Grade 1 Heavy-Duty Cylindrical Locks

|  |  |  |  | A |  |
| --- | --- | --- | --- | --- | --- |
|  |  |  | B |  |  |  |
|  |  |  |  | D |  |  |
|  |  |  |  | C |  |  |
|  |  |  |  | Dimensions |  |  |
|  |  |  | A | B | C | D |
|  |  | Sierra | 4.895" | 2.985" | 3.543" | .407" |
|  |  |  | 124.32mm | 75.82mm | 90mm | 10.34mm |
|  |  | Summit | 4.929" | 3.034" | 3.543" | .407" |
| QCL150 |  |  | 125.20mm | 77.06mm | 90mm | 10.34mm |
|  |  | Slate | 4.937" | 2.993" | 3.543" | .407" |
| Sierra |  |  |  |  |  |  |
|  |  |  | 125.40mm | 76mm | 90mm | 10.34mm |
| Functions | ANSI | Description |  |  |  | Case Qty |
| QCL120 | — | Dummy trim for one side of door. Used for door pull or as matching inactive trim. No | 12 |
| Single Dummy |  | mechanical operation. Surface-mounted single dummy trim. |  |  |  |
| QCL130 | F75 | Both levers always unlocked and always free for immediate ingress & egress. |  | 6 |
| Passage |  |  |  |  |
| QCL135 | F111 | Blank plate outside. Inside lever always unlocked and always free. |  |  | 6 |
| Communicating |  |  |  |  |  |
| QCL140 |  | Push-button locking. Can be opened from outside with a small screwdriver. Turning |  |  |
|  | F76 | inside lever or closing door releases button. Inside lever is always free for immediate |  | 6 |
| Privacy |  | egress. Clutch feature disengages outside lever from latch when locked to prevent |  |  |
|  |  | vandalism. |  |  |  |  |
|  |  | Turn/push-button locking; pushing and turning button locks outside lever, requiring |  |  |
| QCL150/151 | F109 | use of key until button is manually unlocked. Push-button locking; pushing button |  | 6 |
| Entry/Office |  | locks outside lever until unlocked by key or by depressing inside lever. Clutch feature |  |
|  |  | disengages outside lever from latch when locked to prevent vandalism. Inside lever is |  |
|  |  | always free for immediate egress. |  |  |  |  |
| QCL154/155 |  | Deadlocking latch bolt operates by lever from either side except when outside |  |
|  | F90 | lever is locked by key in outside lever, or by push-button on inside. Key in outside | 6 |
| Corridor |  | lever locks or unlocks outside lever. Operating inside lever releases push-button. |  |
|  |  | Closing door releases push-button. Inside lever always operates latch bolt. |  |  |
| QCL160/161 | F84 | Key required to either lock or unlock outside lever. Inside lever is always unlocked and | 6 |
| Classroom |  | free for immediate egress. Clutch feature disengages outside lever from latch when |  |  |
|  |  | locked to prevent vandalism.sdf |  |  |  |  |
| QCL168/169 | F110 | Key in either lever required to lock or unlock outside lever. |  |  | 6 |
| Classroom Security |  | Inside lever is always unlocked for immediate egress. |  |  |  |  |
| QCL170/171 | F86 | Outside lever always locked. Entrance by key only. Inside lever unlocked and free for |  | 6 |
| Storeroom |  | immediate egress. Clutch feature disengages outside lever from latch when locked to |  |
|  |  | prevent vandalism. |  |  |  |  |

- Full Line Catalog STANLEY Commercial Hardware

QCL 100 Series: Grade 1 Heavy-Duty Cylindrical Locks

Electrified Options (Consult Factory For Lead Times)

| Model # | Description |
| --- | --- |

| QCL192 | Electronically locked (fail safe). Outside lever continuously locked electrically. Unlocked by key outside, by switch, or by power failure. |
| --- | --- |
| QCL193 (SFIC) | Inside always free for immediate egress. |
| QCL194 | Electronically unlocked (fail secure). Outside lever continuously locked until unlocked by |
| QCL195 (SFIC) | key or electric current. Inside always free for immediate egress. |
| QCL170—X | Request to exit. Switch monitors inside lever rotation. Incorporates into alarm systems or |
| QCL171—X (SFIC) | in conjunction with an electromagnet. |
| QCL192—X |  |
|  | Electronically locked (fail safe) with request to exit. Outside lever continuously locked electrically. Unlocked by key outside, by switch, or by |
| QCL193—X (SCFIC) | power failure. Inside always free for immediate egress. Ability to tie into alarm systems. |
| QCL194—X |  |
|  | Electronically unlocked (fail secure) with request to exit. Outside lever continuously locked until unlocked by key or electric current. |
| QCL195—X (SCFIC) | Inside always free for immediate egress. Ability to tie into alarm systems. |
| 8Q00314 | Fail Safe / Fail Secure 24VDC Power Supply |

MECHANICAL LOCKS

Electrified Product Specifications

- Consult factory for lead times.

- Electrification prices should be added to list price of lock.

- Standard door prep.

- Deadlocking latch.

- Key override allows key to retract latch bolt momentarily on electronically locked models.

- Inside lever always free for immediate egress.

- Continuous duty solenoids.

- Tie into alarm systems and electromagnetic locks.

- 12V AC/DC with .250 AMP current.

24V AC/DC with .150 AMP current.

- Specify voltage when ordering.

- Lifetime warranty on lock body; 1-year warranty on electric components.

- Uses power supply 8Q00314.

- Warranty: 1-year electrical.

Power Supply Specifications

- Consult factory for lead times.

- Provides power for fail safe or fail secure locking devices.

- UL listed, US & Canada, Class 2.

- Filtered and regulated 24DC constant voltage.

- 2 AMP load capacity.

- Over voltage/short-circuit protection.

- Surge suppression for locking devices.

- Interface relay to isolate the locking device current from the control switch.

- Auxiliary 24V DC constant voltage for powering stand-alone devices such as keypads, motion detectors, status indicators, etc.

- Field terminal block set at 45° for ease of installation.

- Can power up to twelve 24V cylindrical fail safe/ fail secure levers – refer to installation manual for additional details.

Example

If you ordered: QCL192 E626 S4 478S KW5 KA 24V X 625

You would get: Grade 1 Electronically Locked Cylindrical Lock, Sierra Lever, Satin Chrome x Bright Chrome, 2 3/4" Dead Latch Square, ANSI 4 7⁄8" x 1 1/4" Strike, Kwikset Keyway, Keyed Alike.

With options: 24-Volt Power and Request to Exit

Full Line Catalog STANLEY Commercial Hardware	17

How to Order

QCL 100 Series: Grade 1 Heavy-Duty Cylindrical Locks

Example

If you ordered: QCL170 E626 S4 478S F6 KA H

You would get: Grade 1 Hurricane Compliant Cylindrical Storeroom Lock, Sierra Lever,

Satin Chrome, 2 3⁄4" Dead Latch Square, ANSI 47⁄8" x 11⁄4" Strike, Standard “F” Keyway, Keyed Alike.

MECHANICAL LOCKS

| 20 | Single Dummy |
| --- | --- |
| 30 | Passage |
| 35 | Communicating |
| 40 | Privacy |

- Entry/Office

- Entry/Office SFIC

- Corridor

- Corridor SFIC

- Classroom

- Classroom SFIC

- Classroom Security

- Classroom Security SFIC

- Storeroom

- Storeroom SFIC

Added Functions (New)

- Electronically Locked (fail safe)

- Electronically Locked SFIC (fail safe)

- Electronically Unlocked (fail secure)

- Electronically Unlocked SFIC (fail secure)

|  |  |  | BF | BEST "F" SFIC |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | KW | Kwikset “KW” |  |  |  |
| 605 | Bright Brass |  | WE | Weiser “E” |  |  |  |
| 613 | Oil Rubbed Bronze |  |  |  |  |  |  |
|  |  |  | SC | Schlage “C” |  |  |  |
| 619 | Satin Nickel |  |  |  |  |  |  |
|  |  |  | GA | Yale “GA” |  |  |  |
| 625 | Bright Chrome |  |  |  |  |  |  |
|  |  |  | LA | Sargent “LA” |  |  |  |
|  |  |  |  |  |  | 24V | 24 Volt AC/DC |
| 626 | Satin Chrome |  | LC | Less Cylinder |  |  |  |
|  |  |  |  |  |  | 12V | 12 Volt AC/DC |

|  |  |  |  |  |  |  | Base Part Number |  |  |  |  |  |  |  |  |  |  |  | Additional Options |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Series |  | Function |  | Design | Finish |  | Latch |  | Strike |  | Keyway | # Of Pins |  | Keying |  |  | Hurricane |  | Power |  | Request To | 2nd Finish |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Compliant |  |  |  |  |  | Exit |  |  |
| QCL1 |  | 71 |  | E | 626 |  | S4 |  | 478S |  | F | 6 |  |  | KA |  |  | H |  | — |  |  |  | — | — |  |
|  |  | E | Sierra |  |  |  |  |  |  |  | 478S | ANSI 4 7⁄8" x 11⁄4" Strike |  |  |  |  |  |  |  |  |  | 625 |  |  | Bright Chrome |
|  |  |  |  |  |  |  |  |  |  |  |  |  | 118F | ANSI 11⁄8" x 21⁄4" Strike |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  | M | Summit |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  | A | Slate |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  | QD1 Latch Table (New) |  |  |  |  |  | KD |  | Keyed Different |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  | FR4 | Fire-Rated Radius 2-3/4 |  |  |  |  | KA |  | Keyed Alike |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  | FS4 | Fire-Rated Square 2-3/4 |  |  |  |  | SK |  | Special Keying |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  | NOL | No Latch |  |  |  |  |  |  |  |  |  |  |  |  |  |  | -Construction Keyed |  |  |  |  |  |  |
|  |  |  |  |  |  |  | R4 | Radius 2-3/4 |  |  |  |  |  |  |  |  |  |  | -Construction Master Keyed |  |  |  |  |  |  |
|  |  |  |  |  |  |  | R8 | Radius 2-3/8 |  |  |  |  |  |  |  |  |  |  | -Maison Keyed |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  | S4 | Square 2-3/4 |  |  |  |  |  |  |  |  |  |  | -Master Keyed |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  | S5 | Square 5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | -Grand Master Keyed |  |  |  |  |  |  |
|  |  |  |  |  |  |  | S8 | Square 2-3/8 |  |  |  |  |  |  |  |  |  |  | -Great Grand Master Keyed |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | ZB |  | Zero Bitted |  |  |  |  |  |  |  |  |  |  |

- Full Line Catalog STANLEY Commercial Hardware

QCL 200 Series: Grade 2 Standard-Duty Cylindrical Locks

Performance Features

- Tested to meet Grade 2 specification of 400,000 cycles.

- Standard clutching mechanism provides resistance to damage caused by physical force.

- Thru-bolt design and heavy-duty spring tension provides longer performance life and prevents lever sag.

- Concealed mounting screws.

- Compartmentalized packaging allows for quick and easy installation.

Certifications

- ANSI/BHMA A156.2 Series – Grade 2

- ANSI A117.1 Accessibility Code (ADA Compliant)

- UL/cUL Listed (3 hours) for “A” label single-door applications (4' x 8') (1.219m x 2.438m)

- UL10C/UBC 7-2 (1997) Positive Pressure Rated

- UL10B Pressure Rated

- California State Reference Code (formerly Title 19 – Fire Marshal)

- Hurricane Compliant – Miami-DADE N.O.A. See page 78 for more details.

Sierra (E)

Summit (M)

Slate (A)

Product Specifications

- Handing – All QCL200 Series Levers Locksets are non-handed.

- Door thickness – 1 3/8" - 2" (35mm-51mm) standard.

- Backset – 2 3⁄4" (70mm) square standard.

2 3⁄8" and 5" (60mm, 127mm) available.

- Exposed trim – Pressure cast zinc, plated to match finish designation.

- Strike – ANSI Strike 1 1⁄4" x 4 7⁄8" (32mm x 124mm) standard. Other strike options also available.

- Door prep – 2 1⁄8" (54mm) diameter cross bore.

- Latch bolt – Keyed/Exterior 1⁄2" (12.7mm) steel throw; Interior 1⁄2" (12.7mm) spring latch.

- Latch faceplate – 1 1⁄8" x 2 1⁄4" (29mm x 57 mm) standard.

Keying

- 6-pin non-IC brass cylinders. 6 or 7 pin SFIC option available. Many keying options available from our factory to include, but not limited to, master keying, grand master keying and construction keying.

- 2 keys per lockset.

- Offered with the following keyway options: BF-BEST "F" SFIC, KW-Kwikset, WE-Weiser, SC-Schlage, GA-Yale, LA-Sargent, & LC-Less Cylinder. Consult factory for other cylinder options.

Warranty

- Lifetime Mechanical and 3-year finish*

*(613/US10B carries no finish warranty)

Functions

| ANSI | Series | Description |
| --- | --- | --- |
| — | QCL220 | Single Dummy |
| F75 | QCL230 | Passage |
| F111 | QCL235 | Communicating |
| F76 | QCL240 | Privacy |
| F109 | QCL250 | Entry/Office |
| F109 | QCL251 | Entry/Office SFIC |
| F90 | QCL254 | Corridor |
| F90 | QCL255 | Corridor SFIC |
| F84 | QCL260 | Classroom |
| F84 | QCL261 | Classroom SFIC |
| F86 | QCL270 | Storeroom |
| F86 | QCL271 | Storeroom SFIC |

Finishes

| BHMA | Description |
| --- | --- |
| 605 | Bright Brass |
| 613 | Oil Rubbed Bronze |
| 619 | Satin Nickel |

- Bright Chrome

- Satin Chrome

| Full Line Catalog STANLEY Commercial Hardware | 19 |
| --- | --- |
| MECHANICAL LOCKS |

QCL 200 Series: Grade 2 Standard-Duty Cylindrical Locks

MECHANICAL LOCKS

QCL250

Sierra

|  | A |  | Dimensions |  |  |
| --- | --- | --- | --- | --- | --- |
|  |  |  | A | B | C | D |
|  |  | Sierra | 4.451" | 2.6" | 3.366" | .269" |
| B |  |  | 113.06mm | 66.04mm | 85.50mm | 6.84mm |
|  |  | Summit | 4.533" | 2.744" | 3.366" | .269" |
|  |  |  | 115.14mm | 69.70mm | 85.50mm | 6.84mm |
|  | D | Slate | 4.535" | 2.87" | 3.366" | .269" |
|  | C |  | 115.20mm | 72.90mm | 85.50mm | 6.84mm |
| Functions | ANSI | Description |  |  |  | Case Qty |
| QCL220 | — | Dummy trim for one side of door. Used for door pull or as matching inactive trim. No | 12 |
| Single Dummy |  | mechanical operation. Surface-mounted single dummy trim. |  |  |  |
| QCL230 | F75 | Both levers always unlocked and always free for immediate ingress & egress. |  | 6 |
| Passage |  |  |  |  |
| QCL235 | F111 | Blank plate outside. Inside lever always unlocked and always free. |  | 6 |
| Communicating |  |  |  |  |
| QCL240 |  | Push-button locking. Can be opened from outside with a small screwdriver. Turning |  |
|  | F76 | inside lever or closing door releases button. Inside lever is always free for immediate | 6 |
| Privacy |  | egress. Clutch feature disengages outside lever from latch when locked to prevent |  |
|  |  | vandalism. |  |  |  |  |
|  |  | Turn/push-button locking; pushing and turning button locks outside lever, requiring |  |
| QCL250/251 | F109 | use of key until button is manually unlocked. Push-button locking; pushing button | 6 |
| Entry/Office |  | locks outside lever until unlocked by key or by depressing inside lever. Clutch feature |  |
|  |  | disengages outside lever from latch when locked to prevent vandalism. Inside lever is |  |
|  |  | always free for immediate egress. |  |  |  |  |
| QCL254/255 |  | Deadlocking latch bolt operates by lever from either side except when outside lever is |  |
|  | F90 | locked by key in outside lever or by push-button on inside. Key in outside lever locks | 6 |
| Corridor |  | or unlocks outside lever. Operating inside lever releases push-button. Closing door |  |
|  |  | releases push-button. Inside lever always operates latch bolt. |  |  |  |
| QCL260/261 | F84 | Key required to either lock or unlock outside lever. Inside lever is always unlocked and | 6 |
| Classroom |  | free for immediate egress. Clutch feature disengages outside lever from latch when |  |
|  |  | locked to prevent vandalism. |  |  |  |  |
| QCL270/271 | F86 | Outside lever always locked. Entrance by key only. Inside lever unlocked and free for | 6 |
| Storeroom |  | immediate egress. Clutch feature disengages outside lever from latch when locked to |  |
|  |  | prevent vandalism. |  |  |  |  |

- Full Line Catalog STANLEY Commercial Hardware

How to Order

QCL 200 Series: Grade 2 Standard-Duty Cylindrical Locks

Example

If you ordered: QCL271 E626 S4 478S BF6 KA H 625

You would get: Grade 2 Hurricane Compliant Cylindrical Storeroom Lock, Sierra

Lever, Satin Chrome x Bright Chrome, 23⁄4" Deadlatch Square, ANSI 47⁄8" x 11⁄4"

Strike, SFIC “F” Keyway, Keyed Alike.

- Single Dummy

- Passage

- Communicating

| 40 | Privacy |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 50 | Entry/Office |  |  |  |  | BF | BEST "F" SFIC |
|  |  |  |  |  |  | KW | Kwikset “KW” |
| 51 | Entry/Office SFIC |  |  |  |  |  |  |
| 54 | Corridor |  |  |  |  | WE | Weiser “E” |
|  |  |  | 605 | Bright Brass |  |  |  |
| 55 | Corridor SFIC |  |  |  |  |  |  |
|  |  |  |  |  |  | SC | Schlage “C” |
|  |  |  | 613 | Oil Rubbed Bronze |  |  |  |
| 60 | Classroom |  |  |  |  |  |  |
|  |  |  |  |  |  | GA | Yale “GA" |
|  |  |  | 619 | Satin Nickel |  |  |  |
| 61 | Classroom SFIC |  |  |  |  |  |  |
|  |  |  | 625 | Bright Chrome |  | LA | Sargent “LA” |
| 70 | Storeroom |  |  |  |  |  |  |
|  |  |  | 626 | Satin Chrome |  | LC | Less Cylinder |
| 71 | Storeroom SFIC |  |  |  |  |  |  |

Base Part Number

| Series | Function | Design | Finish | Latch | Strike | Keyway | # of Pins | Keying |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| QCL2 | 71 | E | 626 | S4 | 478S | BF | 6 | KA |

Additional Options

Hurricane	2nd

Compliant	Finish

H	625

MECHANICAL LOCKS

| E | Sierra |  |  | 478S | ANSI 47⁄8" x 11⁄4" Strike |  |  | 613 | Oil Rubbed Bronze |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  |  |  | 625 | Bright Chrome |
| M | Summit |  |  |  |  |  |  |  |  |  |
|  |  |  |  | 118F | ANSI 11⁄8" x 21⁄4" Strike |  |  |  |  |
| A | Slate |  |  |  |  |  |  |  |  |  |
|  |  |  |  | FLS | Full Lip Square Corner Strike |  |  |  |  |
|  |  |  |  |  | FLR | Full Lip 1⁄4" Radius Corner Strike |  |  |  |  |

QCL2 Latch Table (New)

| FR4 | Fire-Rated Radius 2-3/4 |
| --- | --- |
| FS4 | Fire-Rated Square 2-3/4 |
| NOL | No Latch |
| NR4 | Narrow Radius 2-3/4 |
| NR8 | Narrow Radius 2-3/8 |
| NS4 | Narrow Square 2-3/4 |
| NS8 | Narrow Square 2-3/8 |
| R4 | Radius 2-3/4 |
| R8 | Radius 2-3/8 |
| S3 | Square 3-3/4 |
| S4 | Square 2-3/4 |
| S5 | Square 5 |
| S8 | Square 2-3/8 |

| KD | Keyed Different |
| --- | --- |
| KA | Keyed Alike |
| SK | Special Keying |
|  | -Construction Keyed |
|  | -Construction Master Keyed |
|  | -Maison Keyed |
|  | -Master Keyed |
|  | -Grand Master Keyed |
|  | -Great Grand Master Keyed |
| ZB | Zero Bitted |

Full Line Catalog STANLEY Commercial Hardware	21

QCI 200 Series: Grade 2 Standard-Duty Interconnected Locks

Applications

The QCI200 Series Interconnected Levers are designed for multi-family, assisted living, commercial

- mixed-use applications where single motion egress is required. These levers deliver premium performance and are designed to withstand the physical abuses of the applied environment.

Performance Features

- Tested to meet Grade 2 specification of 400,000 cycles.

- Single-motion egress provides easy emergency exit.

- Full 1" (25mm) throwbolt with saw-resistant hardened steel roller pin.

- Anti-drill design deadbolt – two (2) ball bearings inserted to prevent drill attacks.

| • ADA thumbturn. | Sierra (E) – Single-Locking |
| --- | --- |

- Tapered latch bolt to address warped door concerns.

MECHANICAL LOCKS

Certifications

- ANSI/BHMA A156.12 – 1999 Grade 2

- UL/cUL Listed (3 hours) for “A” label single-door applications (4' x 8') (1.219m x 2.438m)

- UL10C/UBC 7-2 (1997) Positive Pressure Rated

- UL10B Pressure Rated

- ANSI A117.1 Accessibility Code (ADA Compliant)

Product Specifications

- Door range – 1 3⁄8" - 1 3⁄4" (35mm-44.5mm).

- Heavy-duty cylindrical lock body.

- 4" center-to-center.

- Backset – 2 3⁄4" (70 mm) standard. 2 3⁄8" (60mm) available.

- Exposed trim – Wrought brass or bronze with cast zinc lever.

- Strikes – “T” strike 1 1⁄8" x 2 3⁄4” standard for lever,

deadbolt strike 1 1⁄8" x 2 3⁄4" standard. Other strike options also available.

- Latch bolt – Keyed 1⁄2" (13mm) steel throw with auxiliary latch, passage 1⁄2" (13mm) spring latch.

- Handing – All QCI200 locksets are non-handed.

- Standard door prep: 2 1⁄8" cross bore (54mm).

- Latch hole – 1" diameter edge bore.

- Rose diameter – 2 1⁄2" (63mm).

- Inside escutcheon – 3" x 8" (82.5mm x 203mm).

Optional exterior escutcheon – 3 1⁄4" x 8" (82.5mm x 203mm).

Keying

- 6-pin non-IC brass cylinders. 6 or 7 pin SFIC option available. Many keying options available from our factory to include, but not limited to, master keying, grand master keying and construction keying. Small format interchangeable core cylinder also available.

- 2 keys per lockset.

- Offered with the following keyway options: SMT-SmartKey, KW-Kwikset, WE-Weiser, SC-Schlage, GA-Yale, LA-Sargent, BF-BEST "F" SFIC, & LC-Less Cylinder. Consult factory for other cylinder options.

Warranty

- Lifetime Mechanical, 3-year finish* and 1-year electrical

*(613/US10B carries no finish warranty)

- Full Line Catalog STANLEY Commercial Hardware

Summit (M) – Double-Locking

Slate (A) – Indicator

Functions

| ANSI | Series | Description |
| --- | --- | --- |
| F95 | QCI230 | Single-Locking (Passage Lever) |
| F95 | QCI231 | Single-Locking SFIC (Passage Lever) |
| F97 | QCI250 | Double-Locking (Entry Lever) |
| F97 | QCI251 | Double-Locking SFIC (Entry Lever) |

—QCI285   Indicator (Passage Lever)

Finishes

| BHMA | Description |
| --- | --- |
| 605 | Bright Brass |
| 613 | Oil Rubbed Bronze |
| 619 | Satin Nickel |
| 626 | Satin Chrome |

QCI 200 Series: Grade 2 Standard-Duty Interconnected Locks

A

B

D

C

Dimensions

|  |  |  | A | B | C | D | LOCKS |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | Sierra | 3.96" | 2.25" | 2.50" | .375" |  |
|  |  |  | 100.58mm | 57.15mm | 63.50mm | 9.52mm |  |
|  |  | Summit | 4.0" | 2.20" | 2.50" | .375" | MECHANICAL |
|  |  |  | 101.60mm | 55.88mm | 63.50mm | 9.52mm |  |
|  |  | Slate | 4.47" | 4.67" | 2.50" | .375" |  |
|  |  |  | 113.50mm | 118.60mm | 63.50mm | 9.52mm |  |
| Functions | ANSI | Description |  |  |  | Case Qty |  |
| QCI230/231* |  | Latch bolt operated by lever from either side. Rotating turn from inside or key from |  |  |
| Single-Locking | F95 | outside extends deadbolt to locked position. Both deadbolt and latch bolt are retracted | 6 |  |
| (Passage Lever) |  | simultaneously to unlock position by operating inside lever. |  |  |  |  |
|  |  | Deadlocking latch bolt is operated by lever from either side except when outside lever |  |  |
| QCI250/251** |  | is made inoperable by locking device inside. When outside lever is locked, deadlocking |  |  |
| Double-Locking (Entry | F97 | latch bolt is operated by key outside. Inside locking device is manually operated to | 6 |  |
|  |  | unlock outside lever. Rotating turn from inside or key from outside extends deadbolt to |  |  |
| Lever) |  |  |  |  |
|  |  | locked position. Operating inside lever bolt retracts both deadbolt and deadlocking latch |  |  |
|  |  | simultaneously. Closing door shall not release locking device inside. |  |  |  |
| QCI285 |  | Latch bolt operated by lever from either side. Rotating turn from inside extends deadbolt |  |  |
| Indicator | — | to locked position. Both deadbolt and latch bolt are retracted simultaneously to unlock | 6 |  |
|  |  | position by operating inside lever. Outside indicator visually shows red closed padlock for |  |  |
| (Passage Lever) |  |  |  |  |
|  |  | locked/in-use, green open door padlock for unlocked/vacant. Emergency key included. |  |  |

NOTES: *SmartKey available on QCI230 functions only.

**QCI251 available at extended lead time. Consult factory.

| Full Line Catalog STANLEY Commercial Hardware | 23 |
| --- | --- |

How to Order

QCI 200 Series: Grade 2 Standard-Duty Interconnected Locks

MECHANICAL LOCKS

Example

If you ordered: QCI230 E626 NR4 118F F6 KD

You would get: Grade 2 Interconnect Single Lock, Sierra Lever, Satin Chrome, 23⁄4" Narrow Radius

Latches, “T” Strike with Standard Deadbolt Strike, Standard “F” Keyway, Keyed Different.

|  |  |  |  |  |  | BF | BEST "F" SFIC |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | KW | Kwikset “KW” |
|  |  |  |  |  |  | WE | Weiser “E” |
| 30 | Single-Locking (Passage Lever) |  |  |  |  |  |  |
|  |  |  |  |  |  | SC | Schlage “C” |
| 31 | Single-Locking SFIC (Passage Lever) |  | 605 | Bright Brass |  |  |  |
|  |  |  |  |  |  | GA | Yale “GA” |
|  |  |  | 613 | Oil Rubbed Bronze |  |  |  |
| 50 | Double-Locking (Entry Lever) |  |  |  |  |  |  |
| 51 | Double-Locking SFIC (Entry Lever) |  | 619 | Satin Nickel |  | LA | Sargent “LA” |
| 85 | Indicator (Passage Lever) |  | 626 | Satin Chrome |  | LC | Less Cylinder |

Base Part Number

| Series | Function | Design | Finish | Latch | Strike | Keyway | # Of Pins | Keying |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| QCI2 | 31 | E | 626 | NR4 | 118F | F | 6 | KD |

- Sierra

- Summit

ASlate

| Order w/Lock | Lever & Deadbolt Latch |
| --- | --- |
| NR4 | Narrow Radius 2-3/4 |
| NS4 | Narrow Square 2-3/4 |
| NS8 | Narrow Square 2-3/8 |
| R4 | Radius 2-3/4 |
| S4 | Square 2-3/4 |
| S8 | Square 2-3/8 |

| KD | Keyed Different |
| --- | --- |
| KA | Keyed Alike |
| SK | Special Keying |
|  | -Construction Keyed |
|  | -Construction Master Keyed |
|  | -Maison Keyed |
|  | -Master Keyed |
|  | -Grand Master Keyed |
|  | -Great Grand Master Keyed |
| ZB | Zero Bitted |

| Order w/Lock | Lever Latch | Deadbolt Latch |
| --- | --- | --- |
| NR8 | Narrow Radius 2-3/8 | Narrow Radius 2-3/4 |
| R8 | Radius 2-3/8 | Radius 2-3/4 |

| Order w/Lock | Lever Strike | Deadbolt Strike |
| --- | --- | --- |
| 118F | 118F | DBS |
| 478S | 478S | DBS |
| FLS | FLS | DBS |
| FLR | FLR | DBS |
| FLS2 | FLS | FLS |
| FLR2 | FLR | FLR |

- Full Line Catalog STANLEY Commercial Hardware

QTL 200 Series: Grade 2 Standard-Duty Tubular Locks

Performance Features

- Tested to meet Grade 2 specification of 400,000 cycles.

- Heavy-duty torsion springs provide longer performance life and prevent lever sag.

- Concealed mounting screws.

- “Anti-Lockout” feature. The entry function will have a free interior. If the door is locked from the inside, it will unlock with the push of the interior side of the lever only or the turn of the button.

- 1/2" (13mm) latch bolt made of stainless steel black powder metallurgy for enhanced durability and strength.Compartmentalized packaging allows for quick and easy installation.

Certifications

- ANSI/BHMA A156.2 Series – Grade 2

- ANSI A117.1 Accessibility Code (ADA Compliant)

- UL/cUL Listed (3 hours) for “A” label single-door applications (4' x 8') (1.219m x 2.438m)

- UL10C/UBC 7-2 (1997) Positive Pressure Rated

- UL10B Pressure Rated

- California State Reference Code (formerly Title 19 – Fire Marshal)

- Hurricane Compliant – Miami-DADE N.O.A. See page 78 for more details.

Product Specifications

- Handing – All QTL200 Series Levers Locksets are non-handed.

- Door thickness – 1 3⁄8" - 1 3⁄4" (35mm-51mm) standard.

- Backset – Universal backset standard, will fit either 2 3⁄8" or 2 3⁄4" backsets (60mm-70mm).

- Exposed trim – Pressure cast zinc, plated to match finish designation.

- Strike – Full-lip strike standard (57mm x 44.4mm). Other strike options also available.

- Latch bolt –1⁄2" (13mm) steel throw.

- Latch faceplate – 1" x 2 1⁄4" (25.4mm x 57mm) standard.

Keying

- 6-pin non-IC brass cylinders. 6 or 7 pin SFIC option available. Many keying options available from our factory to include, but not limited to, master keying, grand master keying and construction keying.

- 2 keys per lockset.

- Offered with the following keyway options: BF-BEST "F" SFIC, KW-Kwikset, WE-Weiser, SC-Schlage, GA-Yale, LA-Sargent, & LC-Less Cylinder. Consult factory for other cylinder options.

Warranty

- Lifetime Mechanical and 3-year finish*

Sierra (E)

Summit (M)

Slate (A)

Functions

| ANSI | Series | Description |
| --- | --- | --- |
| — | QTL220 | Single Dummy |
| F75 | QTL230 | Passage |
| F76B | QTL240 | Privacy |
| F82 | QTL250 | Entry/Office |
| F82 | QTL251 | Entry/Office SFIC |
| F84 | QTL260 | Classroom |
| F84 | QTL261 | Classroom SFIC |
| F86 | QTL270 | Storeroom |
| F86 | QTL271 | Storeroom SFIC |

Finishes

| BHMA | Description |
| --- | --- |
| 605 | Bright Brass |
| 613 | Oil Rubbed Bronze |
| 619 | Satin Nickel |

- Bright Chrome

- Satin Chrome

MECHANICAL LOCKS

*(613/US10B carries no finish warranty)

| Full Line Catalog STANLEY Commercial Hardware | 25 |
| --- | --- |

QTL 200 Series: Grade 2 Standard-Duty Tubular Locks

MECHANICAL LOCKS

|  |  |  | QTL250 |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  | Sierra |  |  |  |
|  |  | A |  | Dimensions |  |  |
|  |  |  | A | B | C | D |
|  |  | Sierra | 4.103" | 2.635" | 2.953" | .443" |
| B |  |  | 104.21mm | 66.93mm | 75mm | 11.24mm |
|  |  | Summit | 4.224" | 2.663" | 2.953" | .443" |
|  |  |  | 107.29mm | 67.64mm | 75mm | 11.24mm |
|  |  | Slate | 4.488" | 2.728" | 2.953" | .443" |
|  | D |  | 114mm | 69.30mm | 75mm | 11.24mm |
|  | C |  |  |  |  |  |
| Functions | ANSI | Description |  |  |  | Case Qty |
| QTL220 | — | For one side of door. Used for door pull or as matching inactive trim. |  | 12 |
| Single Dummy |  | No mechanical operation. Surface-mounted single dummy trim. |  |  |
| QTL230 | F75 | Both levers always unlocked and always free for immediate ingress & egress. |  | 10 |
| Passage |  |  |  |  |
| QTL240 | F76B | Turn-button locking. Can be opened from outside with small screwdriver. Turning | 10 |
| Privacy |  | inside lever releases turn-button. Inside lever is always free for immediate egress. |  |
| QTL250/251 | F82 | Unlocked by key from outside when outside lever is locked by turn-button on inside | 10 |
| Entry/Office |  | lever. Inside lever always unlocked and available for immediate egress. |  |  |
| QTL260/261 | F84 | Outside lever locked or unlocked by key. Inside lever is always unlocked and free for | 10 |
| Classroom |  | immediate egress. |  |  |  |  |
| QTL270/271 | F86 | Outside lever always locked. Entrance by key only. Inside lever always unlocked and free | 10 |
| Storeroom |  | for immediate egress. |  |  |  |  |

- Full Line Catalog STANLEY Commercial Hardware

How to Order

QTL 200 Series: Grade 2 Standard-Duty Tubular Locks

Example

If you ordered: QTL270 E626 SA FLR F6 KA H 625

You would get: Grade 2 Hurricane Compliant Tubular Storeroom Lock, Sierra Lever, Satin Chrome x Bright Chrome, Adjustable Square Latch, Full Lip 1⁄4" Radius Corner Strike, Standard “F” Keyway, Keyed Alike.

| 20 | Single Dummy |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 30 | Passage |  |  |  |  |  |  |
|  |  |  |  |  |  | BF | BEST "F" SFIC |
| 40 | Privacy |  |  |  |  |  |  |
|  |  |  |  |  |  | KW | Kwikset “KW” |
| 50 | Entry/Office |  |  |  |  |  |  |
|  |  |  | 605 | Bright Brass |  |  |  |
|  |  |  |  |  |  | WE | Weiser “E” |
| 51 | Entry/Office SFIC |  |  |  |  |  |  |
|  |  |  | 613 | Oil Rubbed Bronze |  |  |  |
|  |  |  |  |  |  | SC | Schlage “C” |
| 60 | Classroom |  |  |  |  |  |  |
|  |  |  | 619 | Satin Nickel |  |  |  |
|  |  |  |  |  |  | GA | Yale “GA” |
| 61 | Classroom SFIC |  |  |  |  |  |  |
|  |  |  | 625 | Bright Chrome |  |  |  |
|  |  |  |  |  |  | LA | Sargent “LA” |
| 70 | Storeroom |  |  |  |  |  |  |
|  |  |  | 626 | Satin Chrome |  |  |  |
| 71 | Storeroom SFIC |  |  |  |  | LC | Less Cylinder |

|  |  |  |  |  |  |  | Base Part Number |  |  |  |  |  |  |  |  |  |  |  | Additional Options |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Series | Function | Design |  | Finish | Latch |  | Strike |  | Keyway | # of Pins |  | Keying |  |  |  | Hurricane |  | 2nd |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Compliant |  | Finish |
| QTL2 | 71 |  |  | E |  | 626 |  | SA |  | FLR |  | F | 6 |  | KA |  |  |  |  |  | H |  | 625 |  |
|  |  | E | Sierra |  |  |  |  |  | 478S |  | ANSI 47⁄8" x 11⁄4" Strike |  |  |  |  |  | 625 |  | Bright Chrome |  |
|  |  | M | Summit |  |  |  |  |  | 118F |  | ANSI 11⁄8" x 21⁄4" Strike |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  | A | Slate |  |  |  |  |  | FLS |  | Full Lip Square Corner Strike |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  |  | FLR |  | Full Lip 1⁄4" Radius Corner Strike |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  | QTL2 Latch Table (New) |  |  |  |  |  |  |  |  |  | KD |  | Keyed Different |  |  |
|  |  |  |  | RA |  | Adjustable Radius |  |  |  |  |  |  |  |  |  | KA |  | Keyed Alike |  |  |
|  |  |  |  | SA |  | Adjustable Square |  |  |  |  |  |  |  |  |  | SK |  | Special Keying |  |  |
|  |  |  |  | NOL |  | No Latch |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | -Construction Keyed |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | -Construction Master Keyed |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | -Maison Keyed |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | -Master Keyed |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | -Grand Master Keyed |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | -Great Grand Master Keyed |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | ZB |  | Zero Bitted |  |  |

MECHANICAL LOCKS

Full Line Catalog STANLEY Commercial Hardware	27

LOCKS

QDB 100 Series: Grade 1 Heavy-Duty Auxiliary Deadbolts

Performance Features

- Tested to meet Grade 1 specification of 250,000 cycles.

- Solid forged housing provides enhanced strength and durability.

- Full 1" (25.4mm) throwbolt with saw-resistant hardened steel roller pin.

- Anti-drill design – two (2) ball bearings inserted to prevent drill attacks.

- ADA thumbturn.

- Compartmentalized packaging allows for quick and easy installation.

Certifications

- ANSI/BHMA A156.5 Series – Grade 1

| • | ANSI A117.1 Accessibility Code (ADA Compliant) | Single Cylinder |
| --- | --- | --- |

- UL/cUL Listed (3 hours) for “A” label single-door applications (4' x 8') (1.219m x 2.438m)

- UL10C/UBC 7-2 (1997) Positive Pressure Rated

- UL10B Pressure Rated

- California State Reference Code (formerly Title 19 – Fire Marshal)

- Hurricane Compliant – Miami-DADE N.O.A. See page 78 for more details.

Double Cylinder

Product Specifications

MECHANICAL

- Door range – 1 3⁄8" (35 mm) to 2" (51 mm).

Service part number 8Q00082 spacer rings required for 1 3⁄8" doors.

- Backset – 2 3⁄4" (70mm) square standard.

2 3⁄8" (60mm) available.

- Exposed trim – Solid forged brass, plated to match finish designation.

- Strike – Standard deadbolt strike 1 1⁄8" x 2 3⁄4" (32mm x 70mm). Other strike options also available.

- Door prep – 2 1⁄8" (54mm) diameter cross bore.

- Latch bolt – Full 1" (25.4mm) throw with hardened steel roller; Faceplate – 1 1⁄8" x 2 1⁄4" (29mm x 57mm).

Keying

- 6-pin non-IC brass cylinders. 6 or 7 pin SFIC option available. Many keying options available from our factory to include, but not limited to, master keying, grand master keying and construction keying. Small format interchangeable core cylinder also available.

- 2 keys per lockset.

- Offered with the following keyway options: KW-Kwikset, WE-Weiser, SC-Schlage, GA-Yale, LA-Sargent, BF-BEST "F" SFIC, & LC-Less Cylinder. Consult factory for other cylinder options.

Warranty

- Lifetime Mechanical and 3-year finish*

Functions

| ANSI | Series | Description |
| --- | --- | --- |
| E0151 | QDB180 | Single Cylinder |
| E0151 | QDB181 | Single Cylinder SFIC |
| E0141 | QDB182 | Double Cylinder |
| E0141 | QDB183 | Double Cylinder SFIC |
| E0171 | QDB186 | Classroom |
| E0171 | QDB187 | Classroom SFIC |

Finishes

| BHMA | Description |
| --- | --- |
| 605 | Bright Brass |
| 613 | Oil Rubbed Bronze |
| 619 | Satin Nickel |

- Bright Chrome

- Satin Chrome

*(613/US10B carries no finish warranty)

- Full Line Catalog STANLEY Commercial Hardware

QDB 100 Series: Grade 1 Heavy-Duty Auxiliary Deadbolts

QDB180

A	B

| C | D | E |
| --- | --- | --- |

|  |  |  |  |  |  | LOCKS |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | MECHANICAL |
|  |  | Dimensions |  |  |  |  |
| A | B | C | D | E |  |  |
| 1.06" | .920" | 2.5" | 2.52" | 2.02" |  |  |
| 26.90mm | 23.37mm | 63.50mm | 64mm | 51.31mm |  |  |

| Model/Series | ANSI | Functions | Description | Case |
| --- | --- | --- | --- | --- |
|  |  |  |  | Qty |

| QDB180/181 | E0151 | Single Cylinder | Deadbolt is operated by a key outside and a thumbturn inside. | 12 |
| --- | --- | --- | --- | --- |
| Single Cylinder |  |  |  |  |
| QDB182/183 | E0141 | Double Cylinder | Deadbolt is operated by a key on both sides. | 12 |
| Double Cylinder |  |  |  |  |
| QDB186/187 | E0171 | Classroom | Deadbolt is operated by a key from outside. Turnpiece retracts deadbolt | 12 |
| Classroom |  |  | for egress but can not project it. |  |

Full Line Catalog STANLEY Commercial Hardware	29

How to Order

QDB 100 Series: Grade 1 Heavy-Duty Auxiliary Deadbolts

MECHANICAL LOCKS

Example

If you ordered: QDB182 626 S8 DBS F6 KD H

You would get: Grade 1 Double Cylinder Auxiliary Deadbolt, Satin Chrome, 23⁄8" Deadbolt

Latch Square, Standard Deadbolt Strike, Standard “F” Keyway, Keyed Different, Hurricane Compliant.

|  |  |  |  |  |  | BF | BEST "F" SFIC |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | KW | Kwikset “KW” |
| 80 | Single Cylinder |  |  |  |  |  |  |
|  |  |  | 605 | Bright Brass |  | WE | Weiser “E” |
| 81 | Single Cylinder SFIC |  |  |  |  |  |  |
|  |  |  | 613 | Oil Rubbed Bronze |  |  |  |
|  |  |  |  |  |  | SC | Schlage “C” |
| 82 | Double Cylinder |  |  |  |  |  |  |
|  |  |  | 619 | Satin Nickel |  | GA | Yale “GA” |
| 83 | Double Cylinder SFIC |  |  |  |  |  |  |
|  |  |  | 625 | Bright Chrome |  | LA | Sargent “LA” |
| 86 | Classroom |  |  |  |  |  |  |
| 87 | Classroom SFIC |  | 626 | Satin Chrome |  | LC | Less Cylinder |

|  |  |  | Base Part Number |  |  |  |  | Additional Options |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Series | Function | Finish | Latch | Strike | Keyway | # of Pins | Keying |  | Hurricane Compliant |
| QDB1 | 83 | 626 | S8 | DBS | F | 6 | KD |  | H |

QDB1 LATCH TABLE (New)

| NOL | No Latch |
| --- | --- |
| NR4 | Narrow Radius 2-3/4 |
| NR8 | Narrow Radius 2-3/8 |
| NS4 | Narrow Square 2-3/4 |
| NS8 | Narrow Square 2-3/8 |
| R4 | Radius 2-3/4 |
| R8 | Radius 2-3/8 |
| S4 | Square 2-3/4 |
| S8 | Square 2-3/8 |

| KD | Keyed Different |
| --- | --- |
| KA | Keyed Alike |
| SK | Special Keying |
|  | -Construction Keyed |
|  | -Construction Master Keyed |
|  | -Maison Keyed |
|  | -Master Keyed |
|  | -Grand Master Keyed |
|  | -Great Grand Master Keyed |
| ZB | Zero Bitted |

| 478S | ANSI 47⁄8" x 11⁄4" Strike |
| --- | --- |
| DBS | Deadbolt Strike 11⁄8" x 2 3⁄4" Square |
| FLS | Full Lip Square Corner Strike |
| FLR | Full Lip 1⁄4" Radius Corner Strike |

- Full Line Catalog STANLEY Commercial Hardware

QDB 200 Series: Grade 2 Standard-Duty Auxiliary Deadbolts

Performance Features

- Tested to meet Grade 2 specification of 150,000 cycles.

- Full 1" (25.4mm) throwbolt with saw-resistant hardened steel roller pin.

- Free-spinning cylinder collar prevents against wrench attacks.

- Anti-drill design – Two (2) ball bearings inserted to prevent drill attacks.

- ADA thumbturn.

- Compartmentalized packaging allows for quick and easy installation.

• Available with SmartKey Technology.	Single Cylinder	Double Cylinder

Certifications

- ANSI/BHMA A156.12 – 1999 Grade 2

- ANSI A117.1 Accessibility Code (ADA Compliant)

- UL/cUL Listed (3 hours) for “A” label single-door applications (4' x 8') (1.219m x 2.438m)

- UL10C/UBC 7-2 (1997) Positive Pressure Rated

- UL10B Pressure Rated

• Hurricane Compliant – Miami-DADE N.O.A. See page 78 for more details.	QDB285 Indicator	QDB288 Key Control

LOCKS

Product Specifications

- Door range – 1 3⁄8" (35mm) to 2"(51 mm).

Service part number 8Q00082 spacer rings required for 1 3⁄8" doors.

- Backset – 2 3⁄4" (70mm) square standard. 2 3⁄8" (60mm) available.

- Exposed trim – Stainless steel with iron forged cylinder guard.

- Strike – Standard deadbolt strike 1 1⁄8" x 2 3⁄4" (32mm x 70mm). Other strike options also available.

- Latch bolt – Full 1" (25.4mm) throw with hardened steel roller.

- Faceplate – 1 1⁄8" x 2 1⁄4" (29mm x 57mm) standard. 1" x 2 1⁄4" (25.4mm x 57mm) faceplate available.

Keying

- 6-pin non-IC brass cylinders. 6 or 7 pin SFIC option available. Many keying options available from our factory to include, but not limited to, master keying, grand master keying and construction keying. Small format interchangeable core cylinder also available.

- 2 keys per lockset.

- Offered with the following keyway options: SMT-SmartKey, KW-Kwikset, WE-Weiser, SC-Schlage, GA-Yale, LA-Sargent, BF-BEST "F" SFIC, & LC-Less Cylinder. Consult factory for other cylinder options.

Warranty

- Lifetime Mechanical and 3-year finish*

*(613/US10B carries no finish warranty)

Functions

| ANSI | Series | Description |
| --- | --- | --- |
| E0152 | QDB280 | Single Cylinder |
| E0152 | QDB281 | Single Cylinder SFIC |
| E0142 | QDB282 | Double Cylinder |
| E0142 | QDB283 | Double Cylinder SFIC |
| E0193 | QDB284 | Inside Turnbolt |
| — | QDB285 | Indicator |
| E0172 | QDB286 | Classroom |
| E0172 | QDB287 | Classroom SFIC |
| E0152 | QDB288 | Key Control |

Finishes

| BHMA | Description |
| --- | --- |
| 605 | Bright Brass |
| 613 | Oil Rubbed Bronze |
| 619 | Satin Nickel |

- Bright Chrome

- Satin Chrome

| Full Line Catalog STANLEY Commercial Hardware | 31 |
| --- | --- |

MECHANICAL

QDB 200 Series: Grade 2 Standard-Duty Auxiliary Deadbolts

QDB280

MECHANICAL LOCKS

A	B

| C | D | E |  |  | Dimensions |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | A | B | C | D | E |
|  |  |  | 1.06" | .920" | 2.5" | 2.56" | 2.02" |
|  |  |  | 26.8mm | 23.37mm | 63.5mm | 65mm | 51.31mm |

| Model/Series | ANSI |  | Description | Case Qty |
| --- | --- | --- | --- | --- |

| QDB280/281 | E0152 | Deadbolt is operated by a key outside and a thumbturn inside. | 12 |
| --- | --- | --- | --- |
| Single Cylinder |  |  |  |
| QDB282/283 | E0142 | Deadbolt is operated by a key on both sides. | 12 |
| Double Cylinder |  |  |  |
| QDB284 | E0193 | Deadbolt is operated by a thumbturn inside. | 20 |
| Inside Turnbolt |  | There is no trim on the other side. |  |
| QDB285 |  | Deadbolt is operated by turn inside. Occupancy indicator plate on outside. Indicator |  |
| Indicator | — | visually shows red closed padlock for locked/in-use, green opened padlock for unlocked/ | 12 |
|  |  | vacant. Emergency key included. |  |
| QDB286/287* | E0172 | Deadbolt operated by key from outside. Thumbturn retracts deadbolt for egress but | 12 |
| Classroom |  | cannot project it. |  |
| QDB288† | E0152 | Deadbolt operated by either tenant or control key from outside. Thumbturn on inside | 12 |
| Key Control |  | projects and retracts deadbolts. |  |

NOTES: *Classroom indicator deadbolts available in 626 finish at standard lead times. Consult factory for lead times on alternative finishes.

†Key control deadbolt available with SmartKey cylinders only.

- Full Line Catalog STANLEY Commercial Hardware

How to Order

QDB 200 Series: Grade 2 Standard-Duty Auxiliary Deadbolts

Example

If you ordered: QDB282 626 S8 DBS F6 KD H

You would get: Grade 2 Double Cylinder Auxiliary Deadbolt, Satin Chrome, 2 3⁄8" Deadbolt

Latch Square, Standard Deadbolt Strike, Standard “F” Keyway, Keyed Different, Hurricane Compliant.

| 80 | Single Cylinder |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 81 | Single Cylinder SFIC |  |  |  |  |  |  |
|  |  |  |  |  |  | BF | BEST "F" SFIC |
| 82 | Double Cylinder |  |  |  |  |  |  |
|  |  |  |  |  |  | KW | Kwikset “KW” |
| 83 | Double Cylinder SFIC |  |  |  |  |  |  |
|  |  |  | 605 | Bright Brass |  | WE | Weiser “E” |
| 84 | Inside Turnbolt |  |  |  |  |  |  |
|  |  |  | 613 | Oil Rubbed Bronze |  | SC | Schlage “C” |
| 85 | Indicator |  |  |  |  |  |  |
|  |  |  | 619 | Satin Nickel |  | GA | Yale “GA” |
| 86 | Classroom |  |  |  |  |  |  |
|  |  |  | 625 | Bright Chrome |  | LA | Sargent “LA” |
| 87 | Classroom SFIC |  |  |  |  |  |  |
|  |  |  | 626 | Satin Chrome |  | LC | Less Cylinder |
| 88 | Key Control† |  |  |  |  |  |  |

|  |  |  |  | Base Part Number |  |  |  |  |  |  |  |  |  | Additional Options |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Series | Function | Finish |  | Latch |  | Strike |  | Keyway | # of Pins | Keying |  |  | Hurricane |
|  |  |  |  |  |  |  |  |  |  |  |  |  | Compliant |
| QDB2 | 83 | 626 |  |  | S8 |  | DBS |  | F | 6 |  | KD |  |  | H |
|  |  | QDB2 Latch Table (New) |  |  |  |  |  |  |  |  |  | KD |  | Keyed Different |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  | KA |  | Keyed Alike |  |  |
|  |  | 6A | 6-Way Adjustable |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  | SK |  | Special Keying |  |  |
|  |  | NOL | No Latch |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | -Construction Keyed |  |  |
|  |  | NR4 | Narrow Radius 2-3/4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | -Construction Master Keyed |  |  |
|  |  | NR8 | Narrow Radius 2-3/8 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  | -Maison Keyed |  |  |
|  |  | NS4 | Narrow Square 2-3/4 |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  | -Master Keyed |  |  |
|  |  | NS8 | Narrow Square 2-3/8 |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | -Grand Master Keyed |  |  |
|  |  | RA | Adjustable Radius |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | -Great Grand Master Keyed |  |  |
|  |  | R4 | Radius 2-3/4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  | ZB |  | Zero Bitted |  |  |
|  |  | R8 | Radius 2-3/8 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  | SA | Adjustable Square |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  | S4 | Square 2-3/4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  | S8 | Square 2-3/8 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  | 478S | ANSI 47⁄8" x 11⁄4" Strike |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  | DBS | Deadbolt Strike 11⁄8" x 2 3⁄4" Square |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  | DBR | Deadbolt Strike 11⁄8" x 2 3⁄4" Radius |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  | FLS | Full Lip Square Corner Strike |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  | FLR | Full Lip 1⁄4" Radius Corner Strike |  |  |  |  |  |  |  |

NOTES: †Key control deadbolt only available with SmartKey cylinders.

MECHANICAL LOCKS

Full Line Catalog STANLEY Commercial Hardware	33

SFIC and Standard Keys and Cores

Keying

- Two keys provided with each lockset.

- Keying options available include: masterkeying, grand masterkeying and construction keying.

- Key stamping.

Base Part Number

|  | Key |  | Key Type | Keyway |  | Cut Code | Pin Size | Options |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 6AQ |  | 1 | KW |  | 1 | 7 | DND |
|  | 6AQ - Standard | 1 - Operating or blank | KW - Kwikset | 1 | - Blank | 6 - 6-pin | S - Key Serialization |
|  |  |  | 2 | - Control | WS - Weiser | 2 | - Cut | 7 - 7-pin | DND - Do Not Duplicate |
|  |  |  | 3 | - Master | SC - Schlage C |  |  |  |  |  |  |  |
|  |  |  | 4 | - Submaster | SE - Schlage E |  |  |  |  |  |  |  |
|  |  |  | 5 | - Grand Master | GA - Yale |  |  |  |  |  |  |  |
|  |  |  |  |  |  | LA - Sargent |  |  |  |  |  |  |  |
|  |  |  |  |  |  | AA - Arrow |  |  |  |  |  |  |  |

MECHANICAL LOCKS

Example

If you ordered: 6AQ1KW17DND

You would get: Standard Operating Key, Kwikset Keyway, cut for 7-pin, marked Do Not Duplicate.

SFIC Cores

- A2 keying system offered with multiple levels of master keying.

- Standard keyway BF: BEST “F.”

- Offered in three finishes (626, 605, 690).

- Complies to Buy American Act

- Plastic construction core available.

Base Part Number

| Core | Lock Body | Keyway |  | Combination Code | Finish |
| --- | --- | --- | --- | --- | --- |
| Type |  |  |  |  |  |
| 6CS | 7 | BF |  |  | 2 | 626 |
| 6CS - | 6 - 6-pin | BF - BEST “F” |  | 1 | - Uncombinated | 605 Bright Brass |
| SFIC | 7 - 7-pin | SFIC |  | 2 | - Combinated | 626 Satin Chrome |
|  |  |  |  |  |  |  |  |  |  | 690 DK Bronze Powder Coat |

| 626 | 605 | 690 |
| --- | --- | --- |
| Satin | Bright | Dark Bronze |
| Chrome | Brass | Powder Coat |

Example

If you ordered: 6CS 7BF2 626

You would get: Small Format Interchangeable Core (SFIC),

7-pin, Best “F” Keyway, Factory Combinated, Satin Chrome.

Warranty

- Lifetime Mechanical, 3-year finish,* 1-year electrical

*(613 carries no finish warranty)

- Full Line Catalog STANLEY Commercial Hardware

How to Order

Standard Cores

Standard Cores

- BF: BEST "F" Keyway.

- Various keyways available include, but are not limited to: Schlage, Sargent and Yale.

- Optional construction keying available.

- Construction use – Prepared at the factory with construction pinning and key.

- Standard use – First use of operating key will supersede all construction keys.

Base Part Number

|  | Core Type | Core Type | Lock Body | Keyway | Combination Code | Finish | Tailpiece | Length | Options |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 6EQ | L | 6 | KW | 1 | 626 | QCL160 | — | — |
|  | 6EQ - | L - Key-in-Lever | 6 - 6-pin | KW - Kwikset | 1 - Uncombinated | 605 - Bright | Series/ | 118 - 1 1/8" | CC - |
|  | Standard | M - Mortise |  |  | SC - Schlage “C” | 2 - Combinated | Brass | Function | 138 - 1 3/8" | Construction |
|  | Core | D - Deadbolt |  |  | SE - Schlage “E” |  |  |  |  |  |  | (Mortise | (Optional) |
|  |  |  | R - Rim |  |  | CB - C4 Corbin |  |  | 626 - Satin |  |  | Cylinder |  |
|  |  |  |  |  |  |  | GA - Yale “GA” |  |  | Chrome |  |  | only) |  |
|  |  |  |  |  |  |  | LA - Sargent “LA” |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  | AA - Arrow |  |  |  |  |  |  |  |  |

Example

If you ordered: 6EQL 6KW1 626 QCL160

You would get: Standard Key-in-Lever Cylinder, 6-pin, Kwikset Keyway,

Uncombinated, Satin Chrome, QCL160 Tailpiece.

Warranty

- Lifetime Mechanical, 3-year finish,* 1-year electrical

*(613 carries no finish warranty)

| Full Line Catalog STANLEY Commercial Hardware | 35 |
| --- | --- |

MECHANICAL LOCKS

Exit Devices

QED 100 Series: Grade 1 Heavy-Duty Exit Devices

Rim Type

Performance Features

- Tested and certified to significantly exceed 1,000,000 cycles – well above the requirements for Grade 1 certification.

- Thru-bolt trim design for increased security and durability.

- Wide variety of trim options to fit any job.

- Consistent styling allows for harmonization with other STANLEY Commercial Hardware products.

Certifications

- ANSI/BHMA A156.3 – Grade 1

- UL/cUL listed (3 hours) for “A” label door applications (8' x 8')

- ANSI A117.1 Section 404.2.6 Accessibility Code (ADA Compliant)

- Hurricane Compliant – Miami-DADE N.O.A. See page 78 for more details.

QED111

Sierra (E)	Summit (M)	Slate (A)	Pull Plate (L)

Product Specifications

- Handing – All QED100 Series Exit Devices are non-handed.

- Door thickness – 1 3⁄4" standard (44.5mm).

- Latch bolt – Stainless steel 3⁄4" standard (19mm).

- Fasteners – Wood screws, machine screws and sex bolts standard.

- Head cap & end cap – Zinc die-cast.

- Trims – Sierra, Summit and Slate styles available. Escutcheon offering – Dummy, passage, keyed, night latch. Pull plate offering – Dummy, thumbpiece, night latch, flat plate.

- Stile width – 4 1⁄4" minimum (108mm).

- Dogging – Hex key dogging and cylinder dogging available.

- 36" field sizeable to 32" door. 48" field sizeable to 36" door.

- Standard backset – 2 7⁄8" (62mm) to face of doorstop.

- Electrification options available.

Keying

- Offered with the following keyway options: BF-SFIC "F", KW-Kwikset, WE-Weiser, SC-Schlage, GA-Yale, LA-Sargent & LC-Less Cylinder. Consult factory for other cylinder options and for details on Mortise and Rim Cylinder requirements.

Warranty

- Lifetime Mechanical, 3-year finish, 1-year electrical

Functions

| Series | Description |
| --- | --- |
| QED111 | Rim Hex Dog |
| QED112 | Rim Cylinder Dog |
| QED113 | Rim Fire-Rated |

Exit Trim Offerings

| ANSI | Series | Description |
| --- | --- | --- |
| 02 | QET120 | Dummy Lever Escutcheon |
| 02 | QET125 | Dummy Pull Plate |
| 14 | QET130 | Passage Lever Escutcheon |
| 08 | QET160 | Keyed Lever Escutcheon |
| 05 | QET165 | Thumbpiece |
| 02 | QET167 | Dummy Thumbpiece |
| 09 | QET170 | Night Latch Lever Escutcheon |
| 03 | QET175 | Night Latch Pull |
| 01 | QET190 | Flat Plate |

Finishes

| BHMA | Description |
| --- | --- |
| 605 | Bright Brass |
| 710 | Anodized Duranodic Bronze |
| 626 | Satin Chrome |

EXIT DEVICES

Full Line Catalog STANLEY Commercial Hardware	37

QED 100 Series: Grade 1 Heavy-Duty Exit Devices

Surface Vertical Rod (SVR) Type

Performance Features

- Tested and certified to significantly exceed 1,000,000 cycles – well above the requirements for Grade 1 certification.

- Thru-bolt trim design for increased security and durability.

- Wide variety of trim options to fit any job.

| • Consistent styling allows for harmonization with other STANLEY | Sierra (E) | Summit (M) | Slate (A) | Thumbpiece |
| --- | --- | --- | --- | --- |
| Commercial Hardware products. |  |  |  | Plate (L) |

Certifications

| • | ANSI/BHMA A156.3 – Grade 1 |  |
| --- | --- | --- |
| • | UL/cUL listed (3 hours) for “A” label door applications (8' x 8') | QED115 |

- ANSI A117.1 Section 404.2.6 Accessibility Code (ADA Compliant)

- Hurricane Compliant – Miami-DADE N.O.A. See page 72 for more details.

EXIT DEVICES

Product Specifications

- Handing – All QED100 Series Exit Devices are non-handed.

- Door thickness – 1 3⁄4" standard (44.5mm).

- Door height – 7' standard with 84" rods; 8' with 96" rods.

- Latch bolt – Stainless steel 1 ⁄2" throw (12.7mm).

- Fasteners – Wood screws, machine screws and sex bolts standard.

- Head cap & end cap – Zinc die-cast.

- Trims – Sierra, Summit and Slate styles available. Escutcheon offering – Dummy, passage, keyed, night latch. Pull plate offering – Dummy, thumbpiece, night latch, flat plate.

- Stile width – 3 1⁄2" minimum (89mm). Consult installation template for appropriate device length to ensure proper fit.

- Dogging – Hex key dogging and cylinder dogging available.

- 36" field sizeable to 32" door. 48" field sizeable to 36" door.

- Standard backset – 2 7⁄8" (62mm) to face of doorstop.

- Electrification options available.

- QED119 includes bottom fire latch.

Keying

- Offered with the following keyway options: BF-SFIC "F", KW-Kwikset, WE-Weiser, SC-Schlage, GA-Yale, LA-Sargent & LC-Less Cylinder.

Consult factory for other cylinder options and for details on Mortise and Rim Cylinder requirements.

Warranty

- Lifetime Mechanical, 3-year finish, 1-year electrical

Functions

| Series | Description |
| --- | --- |
| QED114 | SVR Hex Dog |
| QED115 | SVR Cylinder Dog |
| QED116 | SVR Fire-Rated |
| QED117 | SVR Less Bottom Rod – Hex Dog |
| QED118 | SVR Less Bottom Rod – Cylinder Dog |
| QED119 | SVR Less Bottom Rod – Fire-Rated |

Exit Trim Offerings

| ANSI | Series | Description |
| --- | --- | --- |
| 02 | QET120 | Dummy Lever Escutcheon |
| 02 | QET125 | Dummy Pull Plate |
| 14 | QET130 | Passage Lever Escutcheon |

- QET160   Keyed Lever Escutcheon

- QET165   Thumbpiece

| 02 | QET167 | Dummy Thumbpiece |
| --- | --- | --- |
| 09 | QET170 Night Latch Lever Escutcheon |
| 03 | QET175 | Night Latch Pull |
| 01 | QET190 | Flat Plate |

Finishes

| BHMA | Description |
| --- | --- |
| 605 | Bright Brass |
| 710 | Anodized Duranodic Bronze |
| 626 | Satin Chrome |

- Full Line Catalog STANLEY Commercial Hardware

QED 100 Series: Grade 1 Heavy-Duty Exit Devices

Concealed Vertical Rod (CVR) Type

Performance Features

- Tested and certified to significantly exceed 1,000,000 cycles – well above the requirements for Grade 1 certification.

- Thru-bolt trim design for increased security and durability.

- Wide variety of trim options to fit any job.

- Consistent styling allows for harmonization with other STANLEY Commercial Hardware products.

Certifications

- ANSI/BHMA A156.3 – Grade 1

- UL/cUL listed (3 hours) for “A” label door applications (8' x 8')

- ANSI A117.1 Section 404.2.6 Accessibility Code (ADA Compliant)

Product Specifications

- Handing – All QED100 Series Exit Devices are non-handed.

- Door thickness – 1 3⁄4" standard (44.5mm).

- Door height – 7' standard with 84" rods; 8' with 96" rods.

- Latch bolt – Stainless steel 1⁄2" throw (12.7mm).

- Fasteners – Wood screws, machine screws and sex bolts standard.

- Head cap & end cap – Zinc die-cast.

- Trims – Sierra, Summit and Slate styles available. Escutcheon offering – Dummy, passage, keyed, night latch. Pull plate offering – Dummy, thumbpiece, night latch, flat plate.

- Stile width – 3 1⁄2" minimum (89mm). Consult installation template for appropriate device length to ensure proper fit.

- Dogging – Hex key dogging and cylinder dogging available.

- 36" field sizeable to 32" door. 48" field sizeable to 36" door.

- Standard backset – 2 7⁄8" (62mm) to face of doorstop.

- Electrification options available.

- QED129 includes bottom fire latch.

Keying

- Offered with the following keyway options: BF-SFIC "F", KW-Kwikset, WE-Weiser, SC-Schlage, GA-Yale, LA-Sargent & LC-Less Cylinder. Consult factory for other cylinder options and for details on Mortise andRim Cylinder requirements.

Warranty

- Lifetime Mechanical, 3-year finish, 1-year electrical

Sierra (E)	Summit (M)	Slate (A)	Thumbpiece

Plate (L)

QED124

Functions

| Series | Description |
| --- | --- |
| QED124 | CVR Hex Dog |
| QED125 | CVR Cylinder Dog |
| QED126 | CVR Fire-Rated |
| QED127 | CVR Less Bottom Rod – Hex Dog |
| QED128 | CVR Less Bottom Rod – Cylinder Dog |
| QED129 | CVR Less Bottom Rod – Fire-Rated |

Exit Trim Offerings

| ANSI | Series | Description |
| --- | --- | --- |
| 02 | QET120 | Dummy Lever Escutcheon |
| 02 | QET125 | Dummy Pull Plate |
| 14 | QET130 | Passage Lever Escutcheon |
| 08 | QET160 | Keyed Lever Escutcheon |
| 05 | QET165 | Thumbpiece |
| 02 | QET167 | Dummy Thumbpiece |
| 09 | QET170 | Night Latch Lever Escutcheon |
| 03 | QET175 | Night Latch Pull |
| 01 | QET190 | Flat Plate |

Finishes

| BHMA | Description |
| --- | --- |
| 605 | Bright Brass |
| 710 | Anodized Duranodic Bronze |
| 626 | Satin Chrome |

EXIT DEVICES

Full Line Catalog STANLEY Commercial Hardware	39

EXIT DEVICES

QED 100 Series: Grade 1 Heavy-Duty Exit Devices

C

D

| E |  |  |  | B |  |  |  | F |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | A |  |

|  |  | 36" Device |  |  | 48" Device |  |  | All QED100 Devices |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| QED100 Series |  |  |  |  |  |  |  |  |  |  |
|  | Minimum | Device | Pushpad | Minimum | Device | Pushpad | Head Cap | Head Cap | Head Cap | End Cap |
|  | Door Width | Length | Length | Door Width | Length | Length | Length | Length | Width | Length |

| Measurement |  |  | A | B |  | A | B | C | D |  | E | F |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Panic-Rated | 30" | 33" | 20.5" | 36" | 45" | 24.5" |  | 3.625" | 2.75" | 9" | 2.5" |
| (with Dogging) |  | 762mm | 838.20mm | 520.70mm | 914.40mm | 1143mm | 622.30mm | 92.10mm | 69.90mm | 228.60mm | 63.50mm |
| Fire-Rated or Panic | 29" | 33" | 20.5" | 33" | 45" | 24.5" |  | 3.625" | 2.75" | 9" | 2.5" |
| (with Dogging |  | 736.60mm | 838.20mm | 520.70mm | 838.20mm | 1143mm | 622.30mm | 92.10mm | 69.90mm | 228.60mm | 63.50mm |
| Removed) |  |  |  |  |  |  |  |  |  |  |  |
| Model/Series |  | Functions |  |  |  |  |  |  |  |  | Style |  | Case Qty |
| QED111 |  | Rim Hex Dog |  |  |  |  |  |  |  |  | — |  |  | 1 |
| QED112 |  | Rim Cylinder Dog |  |  |  |  |  |  |  | — |  |  | 1 |
| QED113 |  | Rim Fire-Rated |  |  |  |  |  |  |  |  | — |  |  | 1 |
| QED114 |  | SVR Hex Dog |  |  |  |  |  |  |  |  | 7FT |  |  | 1 |
| QED115 |  | SVR Cylinder Dog |  |  |  |  |  |  |  | 7FT |  |  | 1 |
| QED116 |  | SVR Fire-Rated |  |  |  |  |  |  |  |  | 7FT |  |  | 1 |
| QED117 |  | SVR Less Bottom Rod (LBR) Hex Dog |  |  |  |  |  |  | 7FT |  |  | 1 |
| QED118 |  | SVR LBR Cylinder Dog |  |  |  |  |  |  |  | 7FT |  |  | 1 |
| QED119 |  | SVR LBR Fire-Rated |  |  |  |  |  |  |  | 7FT |  |  | 1 |
| QED124 |  | CVR Hex Dog |  |  |  |  |  |  |  |  | 7FT |  |  | 1 |
| QED125 |  | CVR Cylinder Dog |  |  |  |  |  |  |  | 7FT |  |  | 1 |
| QED126 |  | CVR Fire-Rated |  |  |  |  |  |  |  |  | 7FT |  |  | 1 |
| QED127 |  | CVR LBR Hex Dog |  |  |  |  |  |  |  | 7FT |  |  | 1 |
| QED128 |  | CVR LBR Cylinder Dog |  |  |  |  |  |  |  | 7FT |  |  | 1 |
| QED129 |  | CVR LBR Fire-Rated |  |  |  |  |  |  |  | 7FT |  |  | 1 |
|  |  |  |  |  |  | Other Options |  |  |  |  |  |
|  |  |  |  |  |  |  | 8FT |  | Vertical rod kit for 8FT door application |  |
| NOTES: All Less Bottom Rod (LBR) fire-rated devices |  |  | 48" |  | 48" Device (Consult factory for lead-time) |  |
|  |  |  | HC |  | Hurricane Compliant |  |  |  |
| include a bottom fire latch. |  |  |  |  |  |  |  |  |  |  |

- Full Line Catalog STANLEY Commercial Hardware

QED 100 Series: Grade 1 Heavy-Duty Exit Devices

Electrified Options (Consult Factory For Lead Times)

| Model # | Description |
| --- | --- |
| QED___LR | Electrified Latch Retraction (LR) allows for the remote unlatching of exit devices. Continuous duty solenoids retract latches momentarily or for |
|  | extended periods of time. Requires the use of Stanley Commercial Hardware power supply 8Q00312 or 8Q00313. |
| QED___ED | Electrified Dogging (ED) allows continuous latch retraction and dogging simultaneously. ED requires first-time mechanical activation after which the |
|  | push bar will continuously hold the push bar and latch retracted. When power is removed or interrupted from the device, the latch bolt will extend |
|  | and push bar will release. Uses power supply 8Q00314 (see p. 20). |
| QED___X | Request to Exit (X) is an SPDT (Single Pole Double Throw) switch which monitors the push bar of the exit device. The X switch can be used to |
|  | activate a door alarm, control a magnetic locking device, shunt a door alarm or signal a control console when the push bar is depressed. |
| QED___LRX | Electrified Latch Retraction (LR) device with a Request to Exit (X) switch. Requires the use of Stanley Commercial Hardware power supply 8Q00312 |
|  | or 8Q00313. |  |  |
| QED___EDX | Electrified Dogging (ED) device with a Request to Exit (X) switch. Uses power supply 8Q00314 (see p. 20). |

Power Supply Options (Consult Factory For Lead Times)

| Model # | Description |
| --- | --- |
| 8Q00312 | Power supply for Electronic Latch Retraction Devices (LR/LRX). |
| 8Q00313 | Power supply with day/night mode for Electronic Latch Retraction Devices (LR/LRX). |

EXIT DEVICES

Electrified Product Specifications

- Consult factory for lead times.

- Electrification prices should be added to price of device.

- Continuous duty solenoids.

- Ties into alarm systems and electromagnetic locks.

- 24V AC/DC with .150 amp current.

- Lifetime warranty on exit device; 1-year warranty on electronic components.

- LR or LRX require power supply 8Q00312 or 8Q00313.

- Minimum door width 36."

- LR and ED require the removal of mechanical dogging mechanism.

- Options can be used in any Hex Dog or Fire-Rated QED100 Series Device (How to order example: QED111LR 36" 626).

Power Supply Specifications (10" x 10" x 4.25")

8Q00312

- Provides power for up to two LR or LRX devices.

- Supplied with wiring diagram in detailed instructions.

- Automatic door operator interface.

- Independent control of single exit devices (one or two single-doors) or sequential operation of two devices (pair of doors).

- Field adjustable latch retraction time delay.

- 24V DC or 12V DC auxiliary power, unfiltered and unregulated.

8Q00313

- Same as 8Q00312 with the addition of a day/night mode.

- Provides separate input for retracting one exit device or two exit devices sequentially without activating the auto door operator. While the latches are held retracted, auto operator can be activated independently from a different output.

Full Line Catalog STANLEY Commercial Hardware	41

How to Order

QED 100 Series: Grade 1 Heavy-Duty Exit Devices

EXIT DEVICES

Example

If you ordered: QED115 LR 36" 7FT 313AN KW KD

You would get: Grade 1 Heavy-Duty Architectural Surface Vertical Rod Exit Device with Cylinder Dogging for a 7' Door, in Anodized Duranodic Bronze, Kwikset Keyway, Keyed Different.

|  |  |  |  |  |  |  |  | KD | Keyed Different |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  | KA | Keyed Alike |
| 11 | Rim Hex Dog | 24 | CVR Hex Dog |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  | CK | Construction Keyed |
| 12 | Rim Cylinder Dog | 25 | CVR Cylinder Dog |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  | CMK | Construction Master |
| 13 | Rim Fire-Rated | 26 | CVR Fire-Rated |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  | Keyed |
| 14 | SVR Hex Dog | 27 | CVR LBR – Hex Dog |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  | MAIS | Maison Keyed |
| 15 | SVR Cylinder Dog | 28 | CVR LBR – Cylinder Dog |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  | MK | Master Keyed |
|  |  |  |  |  | 605 | Bright Brass |  |  |  |
| 16 | SVR Fire-Rated | 29 | CVR LBR – Fire-Rated |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  | GMK | Grand Master Keyed |
| 17 | SVR LBR – Hex Dog |  |  |  |  | Anodized |  |  |  |
|  |  |  |  |  | 313AN |  |  | GGMK | Great Grand Master |
|  |  |  |  |  |  | Duranodic Bronze |  |  |  |
| 18 | SVR LBR – Cylinder Dog |  |  |  |  |  |  |  | Keyed |
| 19 | SVR LBR – Fire-Rated |  |  |  | 626 | Satin Chrome |  | ZB | Zero Bitted |

|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Base Part Number |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | Series |  | Function |  | Options |  |  |  | Size |  |  | Height |  | Finish |  | Keyway |  | Keying |  | Notes |
|  |  | QED1 |  | 15 |  | LR |  |  | 36" |  |  |  | 7FT |  | 313AN |  | KW |  | KD |  | XXXX |
|  |  | Grade 1 Architectural |  |  |  |  |  |  | 36" | 36" Device |  |  |  |  |  |  |  | KW | Kwikset “KW” |  |
| QED1xx |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  | 48" | 48" Device |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  | Exit Device |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | WE | Weiser “E” |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | SC | Schlage “C” |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | GA | Yale “GA” |  |
|  |  |  |  | LR | Electrified Latch Retraction |  |  |  |  |  | 7FT |  | 7 ft Rod |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | LA | Sargent “LA” |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 8FT |  | 8 ft Rod |  |  |  |  |  |  |
|  |  |  |  |  |  | Electrified Latch Retraction |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  | LRX |  |  |  |  |  |  |  |  |  |  |  |  | BF | SFIC “F” |  |
|  |  |  |  |  | with Request to Exit |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | LC | Less Cylinder |  |
|  |  |  |  | ED | Electrified Dogging |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  | EDX | Electrified Dogging |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  | with Request to Exit |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  | X | Request to Exit |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  | HC | Hurricane Compliant |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

- Full Line Catalog STANLEY Commercial Hardware

QRM 100 Series: Mullions

Performance Features

- 2" x 3" steel mullion tube. 1/8" wall thickness.

- Hurricane – 2" x 3" steel mullion tube. 5/16" wall thickness.

- Head cap, bottom sill & hurricane mullion adapters – investment cast steel.

- Size – Standard for openings 8' high, field sizable for openings less than 8.' 9', 10', 11' & 12' also available and are field sizable.

- Mullion is pre-prepped for QED100 Series Exit Devices.

- Fire and Hurricane Rating 8' high max.

- Available finishes – Primer (600), Aluminum (689) and Dark Bronze (695).

Keyed Removable Mullions (Consult Factory For Mullion Lead Times)

Order	Description

Cylinder not included. Keyed removable mullions utilize standard rim cylinders. Reference cylinders, keys & keying section for more details.

| QRM111 KR | Keyed Removable Mullion. Includes: Mullion tube, cap, base, fasteners & strike. |
| --- | --- |

QRM111 HC KR	Hurricane Compliant, Keyed Removable Mullion. Includes: Mullion tube, cap, base, fasteners & strike interlock.

| QRM113 KR | Fire-Rated, Keyed Removable Mullion. Includes: Mullion tube, cap, base, fasteners & strike interlock. |
| --- | --- |

QRM113 HC KR	Fire-Rated, Hurricane Compliant, Keyed Removable Mullion. Includes: Mullion tube, cap, base, fasteners & strike interlock.

Removable Mullions (Consult Factory For Mullion Lead Times)

| Order | Description |
| --- | --- |
| QRM111 | Removable Mullion. Includes: Mullion tube, cap, base, fasteners & strike. |
| QRM111 HC | Hurricane Compliant, Removable Mullion. Includes: Mullion tube, cap, base, fasteners & strike interlock. |
| QRM113 | Fire-Rated, Removable Mullion. Includes: Mullion tube, cap, base, fasteners & strike interlock. |
| QRM113 HC | Fire-Rated, Hurricane Compliant, Removable Mullion. Includes: Mullion tube, cap, base, fasteners & strike interlock. |

EXIT DEVICES

Full Line Catalog STANLEY Commercial Hardware	43

How to Order

QRM 100 Series: Mullions

Example

If you ordered: QRM111 HC KR 8FT 600

You would get: Keyed Removable, Hurricane Compliant mullion, 8' height, with

Primer finish. Prepped for QED100 Series strike.

|  |  |  |  |  |  | 600 | Primer |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | HC | Hurricane Compliant |  |  |  |
|  |  |  |  |  |  | 689 | Aluminum |
| QRM1 | Mullion Prepped for |  |  |  |  |  |  |
|  | QED100 Series |  | KR | Keyed Removable |  | 695 | Dark Bronze |

Base Part Number

| Series | Function | Options | Height | Finish |
| --- | --- | --- | --- | --- |
| QRM1 | 11 | HC KR | 8FT | 600 |

EXIT DEVICES

- Standard

- Fire-Rated

| 8FT | Standard Height |
| --- | --- |
| 9FT |  |
| 10FT | Not Available in Fire- |
|  | Rated or Hurricane- |
| 11FT | Compliant Options |
| 12FT |  |

- Full Line Catalog STANLEY Commercial Hardware

QET 100 Series: Grade 1 Heavy-Duty Exit Trims

Escutcheon Trims Sierra (E)	Escutcheon Trims Summit (M)	Escutcheon Trims Slate (A)

• Available in: 605, 613*, 626	• Available in: 605, 613*,, 626	• Available in: 605, 613*, 626

| Model/Series | Functions | Style | Cylinder Type | Qty |
| --- | --- | --- | --- | --- |
| QET120 | Dummy Lever Escutcheon | E/M/A | — | 6 |
| QET130 | Passage Lever Escutcheon | E/M/A | — | 6 |
| QET160 | Keyed Lever Escutcheon (Classroom) | E/M/A | Mortise | 6 |
| QET170 | Night Latch Lever Escutcheon (Storeroom) | E/M/A | Rim | 6 |

NOTES: Cylinders ordered separately.

*613 Finish trims match 313 finish exit devices.

Escutcheon Trims Pull & Flat Plates

- Available in: 605, 626, 690

EXIT DEVICES

| Dummy Pull | Thumbpiece | Dummy Thumbpiece | Night Latch Pull | Flat Plate |
| --- | --- | --- | --- | --- |
| QET125 | QET165 | QET167 | QET175 | QET190 |

| Model/Series | Functions |  | Style | Cylinder Type |  | Qty |
| --- | --- | --- | --- | --- | --- | --- |
| QET125 | Dummy Pull Escutcheon |  | L | — |  | 6 |
| QET165 | Thumbpiece Pull Escutcheon |  | L | Mortise |  | 6 |
| QET167 | Dummy Thumbpiece Pull Escutcheon |  | L | — |  | 6 |
| QET175 | Night Latch Pull Escutcheon |  | L | Rim |  | 6 |
| QET190 | Flat Plate Escutcheon |  | L | — |  | 6 |
| NOTES: Cylinders ordered separately. |  |  |  |  |  |
|  |  | Full Line Catalog STANLEY Commercial Hardware | 45 |

QET 100 Series: Grade 1 Heavy-Duty Exit Trims

EXIT DEVICES

B

A

C

|  |  |  |  |  |  | Dimensions |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | A | B | C | D |  |
|  |  |  |  |  | 9.78" | 3.28" | 14" | 3" |  |
|  |  |  | D |  |  |  |  |  |
|  |  |  |  | 248.60mm | 83.31mm | 355.60mm | 76.20mm |  |
| Functions | Description |  |  |  |  |  |  |  |  |
| QET120 | Dummy Lever Escutcheon | Used for door pull when device is dogged or as matching inactive trim. |  |  |  |
|  |  | No mechanical operation. |  |  |  |  |  |
| QET125 | Dummy Pull Escutcheon | Used for door pull when device is dogged or as matching inactive trim. |  |  |  |
|  |  | No mechanical operation. |  |  |  |  |  |
| QET130 | Passage Lever Escutcheon | Levers always unlocked and always free for immediate ingress. |  |  |  |
| QET160 | Keyed Lever Escutcheon | Key locks & unlocks lever (operates same as classroom function). |  |  |  |
| QET165 | Thumbpiece Pull Escutcheon | Key locks & unlocks thumbpiece (operates same as classroom function). |  |  |  |
| QET167 | Dummy Thumbpiece | Used for door pull when device is dogged or as matching inactive trim. No mechanical operation. |  |
|  | Pull Escutcheon | Matches QET165. |  |  |  |  |  |
| QET170 | Night Latch Lever Escutcheon | Lever always locked, key retracts latch for entrance (operates same as |  |  |  |
|  |  | storeroom function). |  |  |  |  |  |
| QET175 | Night Latch Pull Escutcheon | Outside always locked, key retracts latch for entrance (operates same as |  |  |  |
|  |  | storeroom function). |  |  |  |  |  |
| QET190 | Flat Plate Escutcheon | Blank trim plate—used to cover existing door prep for an exit-only application. |  |  |

- Full Line Catalog STANLEY Commercial Hardware

How to Order

QET 100 Series: Grade 1 Heavy-Duty Exit Trims

Example

If you ordered: QET160 M 626 KW KD

You would get: Grade 1 Escutcheon Trim Lever, Summit design, Satin Chrome, Kwikset

Keyway, Keyed Different. This trim matches to the QED100 Series Exit Devices.

| 20 | DL – Dummy Trim Lever |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 25 | DP – Dummy Trim Pull |  |  |  |  |  |  |
|  |  |  |  |  |  | KD | Keyed Different |
| 30 | PL – Passage Lever |  |  |  |  | KA | Keyed Alike |
| 60 | KL – Keyed Lever |  |  |  |  | CK | Construction Keyed |
|  |  |  |  |  |  | CMK | Construction Master Keyed |
| 65 | TP – Thumbpiece Escutcheon |  |  |  |  |  |  |
|  |  |  |  |  |  | MAIS | Maison Keyed |
| 67 | DT – Dummy Thumbpiece Escutcheon |  | 605 | Bright Brass |  |  |  |
|  |  |  |  |  |  | MK | Master Keyed |
| 70 | NL – Night Latch Lever Escutcheon |  | 613† | Oil Rubbed Bronze |  |  |  |
|  |  |  |  |  |  | GMK | Grand Master Keyed |
| 75 | NL – Night Latch Pull Escutcheon |  | 626 | Satin Chrome |  |  |  |
|  |  |  |  |  |  | GGMK | Great Grand Master Keyed |
| 90 | Flat Plate |  | 690† | Painted Duranodic Bronze |  |  |  |
|  |  |  |  |  |  | ZB | Zero Bitted |

|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | DEVICES |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  |  |  | Base Part Number |  |  |  |  |  |  |  |  |
|  |  | Series |  | Function |  | Design |  | Finish |  | Keyway |  | Keying |  | Notes | EXIT |
|  |  | QET1 |  | 60 |  | M |  | 626 |  |  | KW |  | KD |  | XXXX |  |
| QET1xx | Grade 1 Architectural |  |  |  |  | E | Sierra |  |  | KW | Kwikset “KW”* |  |  |
|  | Exit Trim |  |  |  |  | M | Summit |  |  |  | WE | Weiser “E”* |  |  |
|  |  |  |  |  |  |  |  | A | Slate |  |  | SC | Schlage “C”* |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | GA | Yale “GA” |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | LA | Sargent “LA” |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | BF | Best “F” (SFIC) |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | LC | Less Cylinder |  |  |

NOTES: †613 finish available for lever escutcheon trims; 690 finish available for escutcheon pull trims.

*Available in 6-pin and 5-pin. 6-pin is standard.

Full Line Catalog STANLEY Commercial Hardware	47

QED 200 Series: Grade 1 Heavy-Duty Narrow Stile Exit Devices

Rim Type

EXIT DEVICES

Performance Features

- Consistent styling allows for harmonization with other STANLEY Commercial Hardware products.

- Thru-bolt trim design for increased security and durability.

- Wide variety of trim options to fit any job.

Certifications

- ANSI/BHMA A156.3 – Grade 1

- UL/cUL listed (3 hours) for “A” label doors (8' x 8') when used with HMS strike

- ANSI A117.1 Section 404.2.6 Accessibility Code (ADA Compliant)

Product Specifications

- Handing – All QED200 Series Exit Devices are non-handed.

- Door thickness – 1 3⁄4" standard (44.5mm).

- Latch bolt – Stainless steel 3⁄4" standard (19mm).

- Fasteners – Wood screws, machine screws and sex bolts standard.

- Head cover & end cap – Zinc die-cast.

- Trims – Sierra, Summit and Slate styles available. Escutcheon offering – Dummy, passage, keyed, night latch. Pull plate offering – Dummy, night latch, flat plate.

- Stile width – 2" minimum (50.8 mm) for ALS strike; 3 1⁄2" minimum (88.9 mm) for HMS strike option.

- Dogging – Hex key dogging and cylinder dogging available.

- 36" field sizeable to 26" door. 48" field sizeable to 36" door.

Keying

- Offered with the following keyway options: BEST 'F' SFIC, KW-Kwikset, WE-Weiser, SC-Schlage, GA-Yale, LA-Sargent and LC-Less Cylinder. Consult factory for details on Mortise and Rim Cylinder requirements.

Warranty

- Lifetime Mechanical and 3-year finish

NOTES: *QED213 available with HMS strike only.

- Full Line Catalog STANLEY Commercial Hardware

QED211

Sierra (E)	Summit (M)	Slate (A)	Pull Plate (L)

Functions

| Series | Description |
| --- | --- |
| QED211 | Rim Hex Dog |
| QED212 | Rim Cylinder Dog |
| QED213 | Rim Fire-Rated* |

Exit Trim Offerings

| ANSI | Series | Description |
| --- | --- | --- |
| 02 | QET220 | Dummy Lever Escutcheon |
| 02 | QET225 | Dummy Pull Plate |
| 14 | QET230 | Passage Lever Escutcheon |
| 08 | QET260 | Keyed Lever Escutcheon |
| 03 | QET270 | Night Latch Lever Escutcheon |
| 03 | QET275 | Night Latch Pull |
| 09 | QET280 | Night Latch Lever Escutcheon |
| 01 | QET290 | Flat Plate |

Finishes

| BHMA | Description |
| --- | --- |
| 605 | Bright Brass |
| 313AN | Anodized Duranodic Bronze |
| 626 | Satin Chrome |

QED 200 Series: Grade 1 Heavy-Duty Narrow Stile Exit Devices

Surface Vertical Rod (SVR) Type

Performance Features

- Consistent styling allows for harmonization with other STANLEY Commercial Hardware products.

- Thru-bolt trim design for increased security and durability.

- Wide variety of trim options to fit any job.

Certifications

- ANSI/BHMA A156.3 – Grade 1

- UL/cUL listed (3 hours) for “A” label for 8' x 8' opening

- ANSI A117.1 Section 404.2.6 Accessibility Code (ADA Compliant)

Product Specifications

- Handing – All QED200 Series Exit Devices are non-handed.

- Door thickness – 1 3⁄4" standard (44.5mm).

- Door height – 7' standard with 84" rods; 8' with 96" rods.

- Latch bolt – Stainless steel 1⁄2" throw (12.7mm).

- Fasteners – Wood screws, machine screws and sex bolts standard.

- Head cover & end cap – Zinc die-cast.

- Trims – Sierra, Summit and Slate styles available. Escutcheon offering – Dummy, passage, keyed, night latch. Pull plate offering – Dummy, night latch, flat plate.

- Stile width – 2" minimum (50.8 mm).

- Dogging – Hex key dogging and cylinder dogging available.

- 36" field sizeable to 26" door. 48" field sizeable to 36" door.

- QED219 includes bottom fire bolt.

Keying

- Offered with the following keyway options: BEST 'F' SFIC, KW-Kwikset, WE-Weiser, SC-Schlage, GA-Yale, LA-Sargent and LC-Less Cylinder. Consult factory for other cylinder options and for details on Mortise and Rim Cylinder requirements.

Sierra (E)	Summit (M)	Slate (A)	Pull Plate (L)

QED215

Functions

| Series | Description |
| --- | --- |
| QED214 | SVR Hex Dog |
| QED215 | SVR Cylinder Dog |
| QED216 | SVR Fire-Rated |
| QED217 | SVR Less Bottom Rod – Hex Dog |
| QED218 | SVR Less Bottom Rod – Cylinder Dog |
| QED219 | SVR Less Bottom Rod – Fire-Rated |

Exit Trim Offerings

| ANSI | Series | Description |
| --- | --- | --- |
| 02 | QET220 | Dummy Lever Escutcheon |
| 02 | QET225 | Dummy Pull Plate |
| 14 | QET230 | Passage Lever Escutcheon |
| 08 | QET260 | Keyed Lever Escutcheon |
| 09 | QET280 | Night Latch Escutcheon |
| 01 | QET290 | Flat Plate |

EXIT DEVICES

| Warranty | Finishes |  |
| --- | --- | --- |
| • Lifetime Mechanical and 3-year finish | BHMA | Description |
|  | 605 | Bright Brass |
|  | 313AN | Anodized Duranodic Bronze |
|  | 626 | Satin Chrome |

Full Line Catalog STANLEY Commercial Hardware	49

QED 200 Series: Grade 1 Heavy-Duty Narrow Stile Exit Devices

Concealed Vertical Rod (CVR) Type

Performance Features

- Consistent styling allows for harmonization with other STANLEY Commercial Hardware products.

- Thru-bolt trim design for increased security and durability.

- Wide variety of trim options to fit any job.

Certifications

- ANSI/BHMA A156.3 – Grade 1

- UL/cUL listed (3 hours) for “A” label for 8' x 8' opening

- ANSI A117.1 Section 404.2.6 Accessibility Code (ADA Compliant)

Sierra (E)	Summit (M)	Slate (A)	Pull Plate (L)

QED224

EXIT DEVICES

Product Specifications

- Handing – All QED200 Series Exit Devices are non-handed.

- Door thickness – 1 3⁄4" standard (44.5mm).

- Door height – 7' standard with 84" rods; 8' with 96" rods.

- Latch bolt – Stainless steel 1⁄2" throw (12.7mm).

- Fasteners – Wood screws, machine screws and sex bolts standard.

- Head cover & end cap – Zinc die-cast.

- Trims – Sierra, Summit and Slate styles available. Escutcheon offering – Dummy, passage, keyed, night latch. Pull plate offering – Dummy, night latch, flat plate.

- Stile width – 3 1⁄2" minimum (50.8 mm).

- Dogging – Hex key dogging and cylinder dogging available.

- 36" field sizeable to 26" door. 48" field sizeable to 36" door.

- QED229 includes bottom fire bolt.

Keying

- Offered with the following keyway options: BEST 'F' SFIC, KW-Kwikset, WE-Weiser, SC-Schlage, GA-Yale, LA-Sargent and LC-Less Cylinder. Consult factory for details on Mortise and Rim Cylinder requirements.

Functions

Series	Description

QED224	CVR Hex Dog

QED225	CVR Cylinder Dog

QED226	CVR Fire-Rated

QED227	CVR Less Bottom Rod – Hex Dog

QED228	CVR Less Bottom Rod – Cylinder Dog

QED229	CVR Less Bottom Rod – Fire-Rated

Exit Trim Offerings

| ANSI | Series | Description |
| --- | --- | --- |
| 02 | QET220 | Dummy Lever Escutcheon |
| 02 | QET226 | Dummy Pull Plate |
| 14 | QET230 | Passage Lever Escutcheon |
| 08 | QET260 | Keyed Lever Escutcheon |
| 09 | QET280 | Night Latch Escutcheon |
| 01 | QET291 | Flat Plate |

Warranty

- Lifetime Mechanical and 3-year finish

Finishes

BHMA	Description

| 605 | Bright Brass |
| --- | --- |

313AN	Anodized Duranodic Bronze

| 626 | Satin Chrome |
| --- | --- |

- Full Line Catalog STANLEY Commercial Hardware

QED 200 Series: Grade 1 Heavy-Duty Narrow Stile Exit Devices

C

|  | D |  |  |  |  |  |  | B |  |  |  |  |  |  |  | E |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  |  | A |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  | 36" Device |  |  |  |  |  |  | 48" Device |  |  |  |  |
|  | QED200 Series |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  | Minimum |  | Device | Pushpad | Minimum |  |  | Device | Pushpad | Head Cover |  | Head Cover |  | End Cap |
|  |  |  |  |  |  | Door Width |  | Length | Length | Door Width |  |  | Length | Length | Length |  | Width |  | Width |
|  | Measurement |  |  |  | A | B |  |  |  |  | A | B |  | C |  | D |  | E |
|  | Panic-Rated |  | 30" |  | 34 11/16" | 20" | 36" |  |  | 46 3/4" | 24 1/2" | 1.5" |  | 8 5/16" |  | 2.5" |
|  | (with Dogging) |  | 762 mm |  | 881 mm | 508 mm | 914.4 mm |  |  | 1187.5 mm | 622.3 mm | 38.1 mm |  | 211.1 mm |  | 63.5 mm |
|  | Fire-Rated or Panic |  | 26" |  | 34 11/16" | 20" | 33" |  |  | 46 3/4" | 24 1/2" | 1.5" |  | 8 5/16" |  | 2.5" |
|  | (with Dogging |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | Removed) |  | 660.4 mm |  | 881 mm | 508 mm | 838.2 mm |  |  | 1187.5 mm | 622.3 mm | 38.1 mm |  | 211.1 mm |  | 63.5 mm |
|  | Model/Series | Functions |  |  |  |  |  |  |  |  |  |  | Style |  | Case Qty |
|  | QED211 | Rim Hex Dog |  |  |  |  |  |  |  |  |  |  | — |  |  | 1 |
|  | QED212 | Rim Cylinder Dog |  |  |  |  |  |  |  |  |  | — |  |  | 1 |
|  | QED213 | Rim Fire-Rated* |  |  |  |  |  |  |  |  |  | — |  |  | 1 |
|  | QED214 | SVR Hex Dog |  |  |  |  |  |  |  |  |  |  | 7FT |  |  | 1 |
|  | QED215 | SVR Cylinder Dog |  |  |  |  |  |  |  |  |  | 7FT |  |  | 1 |
|  | QED216 | SVR Fire-Rated |  |  |  |  |  |  |  |  |  |  | 7FT |  |  | 1 |
|  | QED217 | SVR Less Bottom Rod (LBR) Hex Dog |  |  |  |  |  |  |  |  | 7FT |  |  | 1 |
|  | QED218 | SVR LBR Cylinder Dog |  |  |  |  |  |  |  |  |  | 7FT |  |  | 1 |
|  | QED219 | SVR LBR Fire-Rated |  |  |  |  |  |  |  |  |  | 7FT |  |  | 1 |
|  | QED224 | CVR Hex Dog |  |  |  |  |  |  |  |  |  |  | 7FT |  |  | 1 |
|  | QED225 | CVR Cylinder Dog |  |  |  |  |  |  |  |  |  | 7FT |  |  | 1 |
|  | QED226 | CVR Fire-Rated |  |  |  |  |  |  |  |  |  |  | 7FT |  |  | 1 |
|  | QED227 | CVR LBR Hex Dog |  |  |  |  |  |  |  |  |  | 7FT |  |  | 1 |
|  | QED228 | CVR LBR Cylinder Dog |  |  |  |  |  |  |  |  |  | 7FT |  |  | 1 |
|  | QED229 | CVR LBR Fire-Rated |  |  |  |  |  |  |  |  |  | 7FT |  |  | 1 |
|  |  |  |  |  |  |  |  |  |  |  | Other Options |  |  |  |  |  |  |  |
|  | NOTES: All Less Bottom Rod (LBR) fire-rated devices |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  | 8FT | Vertical rod kit for 8FT door application |  |  |
|  | include a bottom fire bolt. |  |  |  |  |  |  |  |  |
|  | *QED213 available with HMS strike only. |  |  |  | 48" | 48" Device (Consult factory for lead-time) |  |  |

EXIT DEVICES

Full Line Catalog STANLEY Commercial Hardware	51

How to Order

QED 200 Series: Grade 1 Heavy-Duty Narrow Stile Exit Devices

Example

If you ordered: QED215 36" 7FT 626 BF KD

You would get: Grade 1 Heavy-Duty Narrow Stile Surface Vertical Rod Exit Device with

Cylinder Dogging for a 7' Door, in Brushed Chrome Finish, SFIC "F" Keyway, Keyed Different.

|  |  |  |  |  |  |  |  | KD | Keyed Different |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 11 | Rim Hex Dog | 24 | CVR Hex Dog |  |  |  |  |  |
|  |  |  |  |  |  |  |  | KA | Keyed Alike |
| 12 | Rim Cylinder Dog | 25 | CVR Cylinder Dog |  |  |  |  |  |
|  |  |  |  |  |  |  |  | SK | Special Keying |
| 13 | Rim Fire-Rated* | 26 | CVR Fire-Rated |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  | -Construction Keyed |
| 14 | SVR Hex Dog | 27 | CVR LBR – Hex Dog |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  | -Construction Master Keyed |
| 15 | SVR Cylinder Dog | 28 | CVR LBR – Cylinder Dog |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  | -Maison Keyed |
| 16 | SVR Fire-Rated | 29 | CVR LBR – Fire-Rated |  |  |  |  |  |  |
| 17 | SVR LBR – Hex Dog |  |  |  | 605 | Bright Brass |  |  | -Master Keyed |
|  |  |  |  |  | 313AN | Anodized |  |  | -Grand Master Keyed |
| 18 | SVR LBR – Cylinder Dog |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  | Duranodic Bronze |  |  |  |
|  |  |  |  |  |  |  |  |  | -Great Grand Master Keyed |
| 19 | SVR LBR – Fire-Rated |  |  |  |  |  |  |  |  |
|  |  |  |  |  | 626 | Satin Chrome |  | ZB | Zero Bitted |

| EXITDEVICES |  |  |  |  |  |  |  |  |  |  |  |  |  | Base Part Number |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | Series | Function |  |  | Size |  | Height |  | Finish | Keyway |  | Keying |  | Strike** |  | Notes |  |
|  |  |  | QED2 | 15 |  |  |  | 36" |  |  | 7FT |  | 313AN | BF |  | KD |  | ALS |  | XXXX |  |
|  | QED2xx |  | Narrow Stile Exit Device |  | 36" | 36" Device |  |  |  |  | BF |  | BEST “F” SFIC |  |  | ALS |  | Aluminum Door Strike |
|  |  |  |  |  |  |  | 48" | 48" Device |  |  |  |  | KW |  | Kwikset “KW” |  |  | HMS |  | Hollow Metal Door Strike |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | WE |  | Weiser “E” |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | SC |  | Schlage “C” |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  |  | 7FT | 7 ft Rod |  |  | GA |  | Yale “GA” |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  |  | 8FT | 8 ft Rod |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | LA |  | Sargent “LA” |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | LC |  | Less Cylinder |  |  |  |  |  |  |  |  |

NOTES: *QED213 available with HMS strike only.

**Only for Rim devices.

- Full Line Catalog STANLEY Commercial Hardware

QET 200 Series: Grade 1 Heavy-Duty Narrow Stile Exit Trims

Escutcheon Trims Sierra (E)	Escutcheon Trims Summit (M)	Escutcheon Trims Slate (A)

• Available in: 605, 613, 626	• Available in: 605, 613,, 626	• Available in: 605, 613, 626

| Model/Series | Functions | Style | Cylinder Type | Qty |
| --- | --- | --- | --- | --- |
| QET220 | Dummy Lever Escutcheon (ANSI 02) | E/M/A | — | 6 |
| QET230 | Passage Lever Escutcheon (ANSI 14) | E/M/A | — | 6 |
| QET260 | Keyed Lever Escutcheon (Classroom, ANSI 08) | E/M/A | Mortise | 6 |
| QET270* | Night Latch Lever Escutcheon (Storeroom, ANSI 03) | E/M/A | Rim | 6 |
| QET280 | Night Latch Lever Escutcheon (Storeroom, ANSI 09) | E/M/A | Mortise | 6 |

NOTES: 613 Finish trims match 313AN finish exit devices.

* Not recommended for use on exit devices with vertical rods.

Escutcheon Trims Pull & Flat Plates

- Available in: 605, 613, 626

EXIT DEVICES

| Dummy Pull | Night Latch Pull | Flat Plate |
| --- | --- | --- |
| QET225 / QET226 | QET275 | QET290 / QET291 |

|  | Model/Series | Functions |  | Style | Cylinder Type |  | Qty |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | QET225 | Dummy Pull Escutcheon (ANSI 02) for Rim and SVR |  | L | — |  | 6 |
|  | QET226 | Dummy Pull Escutcheon (ANSI 02) for CVR |  | L | — |  | 6 |
|  | QET275* | Night Latch Pull Escutcheon (ANSI 03) |  | L | Rim |  | 6 |
|  | QET290 | Flat Plate Escutcheon (ANSI 01) for Rim and SVR |  | L | — |  | 6 |
|  | QET291 | Flat Plate Escutcheon (ANSI 01) for CVR |  | L | — |  | 6 |
| NOTES: * Not recommended for use on exit devices with vertical rods. |  |  |  |  |  |
|  |  |  | Full Line Catalog STANLEY Commercial Hardware | 53 |

How to Order

QET 200 Series: Grade 1 Heavy-Duty Narrow Stile Exit Trims

EXIT DEVICES

A

C

|  |  |  |  |  |  | Dimensions |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | A | B | C | D |
|  |  |  |  |  | 7.83" | 1.69" | 13.88" | 1.76" |
|  |  |  |  |  | 198.88mm | 42.93mm | 352.55mm | 44.70mm |
|  |  |  | D |  |  |  |  |
| Functions | Description |  |  |  |  |  |  |  |
| QET220 | Dummy Lever Escutcheon | Used for door pull when device is dogged or as matching inactive trim. |  |
|  |  | No mechanical operation. (ANSI 02) |  |  |  |
| QET225 / QET226 | Dummy Pull Escutcheon | Used for door pull when device is dogged or as matching inactive trim. |  |
|  |  | No mechanical operation. (ANSI 02) |  |  |  |
| QET230 | Passage Lever Escutcheon | Levers always unlocked and always free for immediate ingress. (ANSI 14) |  |
| QET260 | Keyed Lever Escutcheon | Key locks & unlocks lever (operates same as classroom function). (ANSI 08) |  |
| QET270* | Night Latch Lever Escutcheon | Lever always locked, key retracts latch for entrance (operates same as |  |
|  |  | storeroom function). (ANSI 03) |  |  |  |
| QET275* | Night Latch Pull Escutcheon | Outside always locked, key retracts latch for entrance (operates same as |  |
|  |  | storeroom function). (ANSI 03) |  |  |  |
| QET280 | Night Latch Lever Escutcheon | Key locks & unlocks lever. Device is locked when key is removed. (ANSI 09) |  |
| QET290 / QET291 | Flat Plate Escutcheon | Blank trim plate—used to cover existing door prep for an exit-only application. (ANSI 01) |

NOTES: * Not recommended for use on exit devices with vertical rods.

- Full Line Catalog STANLEY Commercial Hardware

How to Order

QET 200 Series: Grade 1 Heavy-Duty Narrow Stile Exit Trims

Example

If you ordered: QET230 E 626

You would get: Grade 1 Escutcheon Passage Trim Lever, Sierra Design, Satin Chrome.

This trim matches to the QED200 Series Exit Devices.

| 20 | DL – Dummy Trim Lever (ANSI 02) |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 25 | DP – Dummy Trim Pull (ANSI 02) Rim/SVR |  |  |  |  | KD | Keyed Different |
|  |  |  |  |  |  | KA | Keyed Alike |
| 26 | DP – Dummy Trim Pull (ANSI 02) CVR |  |  |  |  |  |  |
|  |  |  |  |  |  | SK | Special Keying |
| 30 | PL – Passage Lever (ANSI 14) |  |  |  |  |  |  |
|  |  |  |  |  |  |  | -Construction Keyed |
| 60 | KL – Keyed Lever (ANSI 08) |  |  |  |  |  |  |
|  |  |  |  |  |  |  | -Construction Master Keyed |
| 70 | NL – Night Latch Lever Escutcheon (ANSI 03) |  |  |  |  |  |  |
|  |  |  |  |  |  |  | -Maison Keyed |
| 75 | NL – Night Latch Pull Escutcheon (ANSI 03) |  |  |  |  |  |  |
|  |  |  |  |  |  |  | -Master Keyed |
| 80 | NL – Night Latch Lever Escutcheon (ANSI 09) |  | 605 | Bright Brass |  |  | -Grand Master Keyed |
|  |  |  | 613 | Oil Rubbed Bronze |  |  |  |
| 90 | Flat Plate (ANSI 01) Rim/SVR |  |  |  |  |  |  |
|  |  |  |  |  |  |  | -Great Grand Master Keyed |
|  |  |  | 626 | Satin Chrome |  |  |  |
| 91 | Flat Plate (ANSI 01) CVR |  |  |  |  |  |  |
|  |  |  |  |  |  | ZB | Zero Bitted |

|  |  |  |  |  |  |  |  |  | Base Part Number |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | Series |  | Function |  | Design |  | Finish |  | Keyway* |  | Keying** | Notes |
|  |  | QET2 |  | 60 |  | M |  | 626 |  | BF |  | KD | XXXX |
| QET2xx | Narrow Stile Exit Trim |  |  |  | L | Pull |  | BF | BEST “F” SFIC |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  | KW | Kwikset “KW” |  |  |
|  |  |  |  |  |  |  | E | Sierra |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  | WE | Weiser “E” |  |  |
|  |  |  |  |  |  |  | M | Summit |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  | SC | Schlage “C” |  |  |
|  |  |  |  |  |  |  | A | Slate |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  | GA | Yale “GA” |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  | LA | Sargent “LA” |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  | LC | Less Cylinder |  |  |

EXIT DEVICES

NOTES: * Applies to Surface Vertical Rods only

** Applies to Cylinder Dogged only

| Full Line Catalog STANLEY Commercial Hardware | 55 |
| --- | --- |

QED 300 Series: Grade 1 Standard-Duty Exit Devices

Rim Type

Performance Features

- Tested and certified to significantly exceed 500,000 cycles required for Grade 1 certification.

- Field sizeable. 36" to 32" door application (91.44cm-81.28cm).

- Consistent styling allows for harmonization with other STANLEY Commercial Hardware products.

Certifications

- ANSI/BHMA A156.3 – Grade 1.

- UL/cUL listed (3 hours) for “A” label door applications (8' x 8')

- ANSI A117.1 Section 404.2.6 Accessibility Code (ADA Compliant)

QED311

Sierra (E)	Summit (M)	Slate (A)	Thumbpiece

Plate (L)

QRT360 M	QRT320 E

EXIT DEVICES

Product Specifications

- Handing – All QED300 Series Exit Devices are non-handed.

- Door thickness – 1 3⁄4" standard (44.5mm).

- Latch bolt – Stainless steel 3⁄4" throw (19mm).

- Strike – Stainless steel body with plated steel roller standard fire-rated stainless steel strike, with stainless steel roller standard on QED313.

- Fasteners – Wood and machine screws standard. Sex bolts optional. (Standard on fire-rated device).

- Head cap & end cap – Zinc die-cast.

- Trims – Sierra, Summit and Slate styles available. Escutcheon offering – Dummy, passage, keyed, night latch. Pull plate offering – Dummy, thumbpiece, night latch, flat plate.

- Stile width – 3 7⁄8" minimum (98mm).

- Dogging – Hex key dogging and cylinder dogging available.

- Standard backset – 2 1⁄4" (57mm) to face of doorstop.

Keying

- Offered with the following keyway options: BF-SFIC “F”, KW-Kwikset, WE-Weiser, SC-Schlage, GA-Yale, LA-Sargent & LC-Less Cylinder.

Consult factory for other cylinder options and for details on Mortise and Rim Cylinder requirements.

Warranty

- Lifetime Mechanical and 3-year finish

Functions

| Series | Description |
| --- | --- |
| QED311 | Rim Hex Dog |
| QED312 | Rim Cylinder Dog |
| QED313 | Rim Fire-Rated |

Exit Trim Offerings

| ANSI | Series | Description |
| --- | --- | --- |
| 02 | QET320 | Dummy Lever Escutcheon |
| 02 | QET325 | Dummy Pull Plate |
| 14 | QET330 | Passage Lever Escutcheon |

- QET360   Keyed Lever Escutcheon

- QET365   Thumbpiece

| 02 | QET367 Dummy Thumbpiece Pull Escutcheon |
| --- | --- |
| 03 | QET370 | Night Latch Lever Escutcheon |
| 03 | QET375 | Night Latch Pull |

—QET377   Gull Wing Pull Escutcheon

| 01 | QET390 | Flat Plate |
| --- | --- | --- |
| 02 | QRT320 | Dummy Round Rose Lever |
| 14 | QRT330 | Passage Round Rose Lever |
| 08 | QRT360 | Keyed Round Rose Lever |
| 03 | QRT370 | Night Latch Round Rose Lever |

Finishes

BHMA	Description

- Painted Aluminum

- Painted Duranodic Bronze

- Full Line Catalog STANLEY Commercial Hardware

QED 300 Series: Grade 1 Standard-Duty Exit Devices

Surface Vertical Rod (SVR) Type

Performance Features

- Tested and certified to significantly exceed 500,000 cycles required for Grade 1 certification.

- Field sizeable. 36" to 32" door application (91.44cm-81.28cm).

- Thru-bolt trim design for increased security and durability.

- Consistent styling allows for harmonization with other STANLEY Commercial Hardware products.

Certifications

- ANSI/BHMA A156.3 – Grade 1.

- UL/cUL listed (1.5 hours) for “A” label door applications (8' x 8')

- ANSI A117.1 Section 404.2.6 Accessibility Code (ADA Compliant)

Product Specifications

- Handing – All QED300 Series Exit Devices are non-handed.

- Door thickness – 1 3⁄4" standard (44.5mm).

- Door height – 7' standard with 84" rods; 8' optional with 96" rods (2.1336m x 2.438m).

- Latch bolt – 1⁄2" (12.7mm) throw on top latch; 3⁄8" (9.53mm) on bottom latch.

- Fasteners – Wood and machine screws standard. Sex bolts optional. (Standard on fire-rated device).

- Head cap & end cap – Zinc die-cast.

- Trims – Sierra, Summit and Slate styles available. Escutcheon offering – Dummy, passage, keyed, night latch. Pull plate offering – Dummy, thumbpiece, night latch, flat plate.

- Stile width – 3 1⁄2" minimum (89mm).

- Dogging – Hex key dogging and cylinder dogging available.

- Standard backset – 2 1⁄4" (57mm) to face of doorstop.

- QED319 includes bottom fire latch.

Keying

- Offered with the following keyway options: BF-SFIC “F”, KW-Kwikset, WE-Weiser, SC-Schlage, GA-Yale, LA-Sargent & LC-Less Cylinder. Consult factory for other cylinder options and for details on Mortise and Rim Cylinder requirements.

Warranty

- Lifetime Mechanical and 3-year finish

Sierra (E)	Summit (M)	Slate (A)	Thumbpiece

Plate (L)

QRT360 M	QRT320 E

QED314

Exit Device Functions

| Series | Description |
| --- | --- |
| QED314 | SVR Hex Dog |
| QED315 | SVR Cylinder Dog |
| QED316 | SVR Fire-Rated |
| QED317 | SVR Less Bottom Rod – Hex Dog |
| QED318 | SVR Less Bottom Rod – Cylinder Dog |
| QED319 | SVR Less Bottom Rod – Fire-Rated |

Exit Trim Offerings

| ANSI | Series | Description |
| --- | --- | --- |
| 02 | QET320 | Dummy Lever Escutcheon |
| 02 | QET325 | Dummy Pull Plate |
| 14 | QET330 | Passage Lever Escutcheon |

- QET360   Keyed Lever Escutcheon

- QET365   Thumbpiece

| 02 | QET367 | Dummy Thumbpiece Pull Escutcheon |
| --- | --- | --- |
| 03 | QET370 | Night Latch Lever Escutcheon |
| 03 | QET375 | Night Latch Pull |
| 01 | QET390 | Flat Plate |
| 02 | QRT320 | Dummy Round Rose Lever |
| 14 | QRT330 | Passage Round Rose Lever |
| 08 | QRT360 | Keyed Round Rose Lever |
| 03 | QRT370 | Night Latch Round Rose Lever |

Finishes

BHMA	Description

- Painted Aluminum

- Painted Duranodic Bronze

EXIT DEVICES

Full Line Catalog STANLEY Commercial Hardware	57

EXIT DEVICES

QED 300 Series: Grade 1 Standard-Duty Exit Devices

|  |  |  |  |  | C |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | D |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| E |  | F |  |  |  |  |  | B |  |  |  |  |  |  |  |  | G |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  | A |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 36" Device |  |  |  |  |  |  |  |  |  |
| QED300 Series |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  | Minimum | Device |  | Pushpad | Head Cap | Head Cap | Head Cap | Head Cap |  | End Cap |
|  |  |  |  |  |  |  |  |  |  |  | Door Width | Length |  | Length | Length | Length | Width | Width |  | Length |
| Measurement |  |  | A |  | B | C | D |  | E | F |  | G |
| Panic Rated |  | 30" | 27" |  | 19" | 2.75" | 1.75" | 6.25" | 3" |  |  | 2" |
| (with Dogging) |  | 762mm | 685.80mm |  | 482.60mm | 69.90mm | 44.50mm | 158.80mm | 76.20mm |  | 50.80mm |
| Fire-Rated or Panic |  | 28" | 25" |  | 19" | 2.75" | 1.75" | 6.25" | 3" |  |  | 2" |
| with Dogging |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Removed |  | 711.20mm | 635mm |  | 482.60mm | 69.90mm | 44.50mm | 158.80mm | 76.20mm |  | 50.80mm |
| Model/Series |  | Functions |  |  |  |  |  |  |  |  |  |  |  |  |  | Case Qty |
| QED311 |  | Rim Hex Dog |  |  |  |  |  |  |  |  |  |  |  |  |  | 4 |
| QED312 |  | Rim Cylinder Dog |  |  |  |  |  |  |  |  |  |  |  |  |  | 4 |
| QED313 |  | Rim Fire-Rated |  |  |  |  |  |  |  |  |  |  |  |  |  | 4 |
| QED314 |  | SVR Hex Dog |  |  |  |  |  |  |  |  |  |  |  |  |  | 4 |
| QED315 |  | SVR Cylinder Dog |  |  |  |  |  |  |  |  |  |  |  |  |  | 4 |
| QED316 |  | SVR Fire-Rated |  |  |  |  |  |  |  |  |  |  |  |  |  | 4 |
| QED317 |  | SVR Less Bottom Rod – Hex Dog |  |  |  |  |  |  |  |  |  |  |  | 4 |
| QED318 |  | SVR Less Bottom Rod – Cylinder Dog |  |  |  |  |  |  |  |  |  |  |  | 4 |
| QED319 |  | SVR Less Bottom Rod – Fire-Rated (Includes Auxiliary Bottom Fire Latch) |  |  |  |  |  |  |  | 4 |

Other Options

| 8FT | Vertical rod kit for 8FT door application |
| --- | --- |
| 48" | 48" Device |

- Full Line Catalog STANLEY Commercial Hardware

How to Order

QED 300 Series: Grade 1 Standard-Duty Exit Devices

Example

If you ordered: QED315 36" 7FT 689 KW KD

You would get: Grade 1 Standard-Duty Surface Vertical Rod Exit Device 36," with Cylinder Dogging, for a 7' height, in Painted Aluminum finish. Kwikset Keyway, Keyed Different.

- Rim Hex Dog

- Rim Cylinder Dog

| 13 | Rim Fire-Rated |  |  |  |  | KW | Kwikset “KW” |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 14 | SVR Hex Dog |  |  |  |  | WE | Weiser “E” |
| 15 | SVR Cylinder Dog |  |  |  |  | SC | Schlage “C” |
| 16 | SVR Fire-Rated |  |  |  |  | GA | Yale “GA” |
| 17 | SVR LBR – Hex Dog |  |  |  |  | LA | Sargent “LA” |
| 18 | SVR LBR – Cylinder Dog |  |  |  |  | BF | SFIC “F” |
|  |  |  | 7FT | 7 ft Rod |  |  |  |
| 19 | SVR LBR – Fire-Rated |  | 8FT | 8 ft Rod |  | LC | Less Cylinder |

|  |  |  |  |  |  |  |  |  |  |  | Base Part Number |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | Series |  | Function |  | Size |  |  | Height |  | Finish | Keyway |  |  | Keying |  | Notes |  |
|  |  | QED3 |  | 15 | 36" |  |  | 7FT |  | 689 | KW |  |  | KD |  | XXXX |  |
| QED3xx | Grade 1 Standard-Duty |  | 36" |  | 36" Device |  |  | 689 | Painted Aluminum |  |  |  | KD |  | Keyed Different |
|  | Exit Device |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  | 48" |  | 48" Device |  |  |  |  |  |  |  |  |  | KA |  | Keyed Alike |
|  |  |  |  |  |  |  |  | 690 | Painted Duranodic Bronze |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | CK |  | Construction Keyed |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | CMK |  | Construction Master Keyed |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | MAIS |  | Maison Keyed |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | MK |  | Master Keyed |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | GMK |  | Grand Master Keyed |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | GGMK |  | Great Grand Master Keyed |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | ZB |  | Zero Bitted |

EXIT DEVICES

Full Line Catalog STANLEY Commercial Hardware	59

EXIT DEVICES

QRM 300 Series: Mullions

Performance Features

- 2" x 3" steel mullion tube. 1⁄8" wall thickness.

- Size – Standard for openings 8' high, field sizeable for openings less than 8'. 9', 10', 11' & 12' also available and are field sizable.

- Mullion is pre-prepped for QED300 Series Exit Devices.

- Fire Rating 8' high max.

- Available finishes – Primer (600), Aluminum (689) & Dark Bronze (695).

Keyed Removable Mullions (Consult Factory For Mullion Lead Times)

Order	Description

Cylinder not included. Keyed removable mullions utilize standard rim cylinders. Reference cylinders, keys & keying section for more details.

| QRM311 KR | Keyed Removable Mullion. Includes: Mullion tube, cap, base, fasteners & strike. |
| --- | --- |
| QRM313 KR | Fire-Rated, Keyed Removable Mullion. Includes: Mullion tube, cap, base, fasteners & strike interlock. |

Removable Mullions (Consult Factory For Mullion Lead Times)

| Order | Description |
| --- | --- |
| QRM311 | Removable Mullion. Includes: Mullion tube, cap, base, fasteners & strike. |
| QRM313 | Fire-Rated, Removable Mullion. Includes: Mullion tube, cap, base, fasteners & strike interlock. |

- Full Line Catalog STANLEY Commercial Hardware

How to Order

QRM 300 Series: Mullions

Example

If you ordered: QRM313 KR 8FT 689

You would get: Keyed Removable, Fire-Rated Mullion, 8' Height, with

Aluminum finish. Prepped for QED300 Series strike.

|  |  |  |  |  |  | 600 | Primer |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | 689 | Aluminum |
| QRM3 | Mullion Prepped for |  |  |  |  |  |  |
|  | QED300 Series |  | KR | Keyed Removable |  | 695 | Dark Bronze |

Base Part Number

| Series | Function | Options | Height | Finish |
| --- | --- | --- | --- | --- |
| QRM3 | 13 | KR | 8FT | 689 |

- Standard

- Fire-Rated

| 8FT | Standard Height |
| --- | --- |
| 9FT |  |
| 10FT | Not Available in |
| 11FT | Fire-Rated Option |
| 12FT |  |

EXIT DEVICES

Full Line Catalog STANLEY Commercial Hardware	61

QET 300 Series: Grade 1 Standard-Duty Exit Escutcheon Trims

Escutcheon Trims Sierra (E)	Escutcheon Trims Summit (M)	Escutcheon Trims Slate (A)

• Available in: 689, 690	• Available in: 689, 690	• Available in: 689, 690

EXIT DEVICES

| Model/Series | Functions | Style | Cylinder Type | Qty |
| --- | --- | --- | --- | --- |
| QET320 | Dummy Lever Escutcheon | E/M/A | — | 12 |
| QET330 | Passage Lever Escutcheon | E/M/A | — | 12 |
| QET360 | Keyed Lever Escutcheon (Classroom) | E/M/A | Mortise | 12 |
| QET370 | Night Latch Lever Escutcheon (Storeroom) | E/M/A | Mortise | 12 |

NOTES: Cylinders ordered separately.

Escutcheon Trims Pull & Flat Plates

- Available in: 689, 690

Dummy Pull	Thumbpiece	Dummy Thumbpiece	Night Latch Pull	Gull Wing Pull	Flat Plate

QET325	QET365	QET367	QET375	QET377	QET390

| Model/Series | Functions | Style | Cylinder Type | Qty |
| --- | --- | --- | --- | --- |
| QET325 | Dummy Pull Escutcheon | L | — | 12 |
| QET365 | Thumbpiece Pull Escutcheon | L | Mortise | 12 |
| QET367 | Dummy Thumbpiece Pull Escutcheon | L | — | 12 |
| QET375 | Night Latch Pull Escutcheon | L | Rim | 12 |
| QET377 | Gull Wing Pull Escutcheon | Gull Wing | Rim | 12 |
| QET390 | Flat Plate Escutcheon | N/A | — | 12 |

NOTES: Cylinders ordered separately.

- Full Line Catalog STANLEY Commercial Hardware

QET 300 Series: Grade 1 Standard-Duty Exit Escutcheon Trims

B

A

C

|  |  |  |  |  |  | Dimensions |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | A | B | C | D |  |
|  |  |  |  | 8.0625" | 2.625" | 14" | 3" |  |
|  |  |  |  |  | 204.79mm | 66.675mm | 355.60mm | 76.70mm |  |
|  |  |  | D |  |  |  |  |
| Model/Series | Functions |  | Description |  |  |  |  |
| QET320 | Dummy Lever Escutcheon |  | Used for door pull when device is dogged or as matching inactive trim. |  |  |  |
|  |  |  | No mechanical operation. |  |  |  |  |
| QET325 | Dummy Pull Escutcheon |  | Used for door pull when device is dogged or as matching inactive trim. |  |  |  |
|  |  |  | No mechanical operation. |  |  |  |  |
| QET330 | Passage Lever Escutcheon |  | Lever is always unlocked and always free for immediate ingress. |  |  |  |
| QET360 | Keyed Lever Escutcheon |  | Key locks & unlocks lever (operates same as classroom function). |  |  |  |
| QET365 | Thumbpiece Pull Escutcheon |  | Key locks & unlocks thumbpiece (operates same as classroom function). |  |  |  |
| QET367 | Dummy Thumbpiece |  | Used for door pull when device is dogged or as matching inactive trim. |  |  |  |
|  | Pull Escutcheon |  | No mechanical operation. Matches QET365. |  |  |  |  |
| QET370 | Night Latch Escutcheon |  | Lever always locked, key retracts latch for entrance (operates same as |  |  |  |
|  |  |  | storeroom function). |  |  |  |  |
| QET375 | Night Latch Pull Escutcheon |  | Outside always locked, key retracts latch for entrance (operates same as |  |  |  |
|  |  |  | storeroom function). |  |  |  |  |
| QET377 | Gull Wing Pull Escutcheon |  | Outside always locked, key retracts latch for entrance (operates same as |  |  |  |
|  |  |  | storeroom function). |  |  |  |  |
| QET390 | Flat Plate Escutcheon |  | Blank trim plate—used to cover existing door prep for an exit-only application. |  |  |

EXIT DEVICES

Full Line Catalog STANLEY Commercial Hardware	63

How to Order

QET 300 Series: Grade 1 Standard-Duty Exit Escutcheon Trims

Example

If you ordered: QET360 E 689 KW KD

You would get: Grade 1 Escutcheon Keyed Lever, Sierra design, Painted Aluminum finish, Kwikset Keyway, Keyed Different. This trim matches the QED300 Series Exit Devices.

EXIT DEVICES

| 20 | DL – Dummy Trim Lever |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 25 | DP – Dummy Trim Pull |  |  |  |  |  |  |
|  |  |  |  |  |  | KD | Keyed Different |
| 30 | PL – Passage Lever |  |  |  |  |  |  |
|  |  |  |  |  |  | KA | Keyed Alike |
| 60 | KL – Keyed Lever |  |  |  |  |  |  |
|  |  |  |  |  |  | CK | Construction Keyed |
| 65 | TP – Thumbpiece Escutcheon |  |  |  |  |  |  |
|  |  |  |  |  |  | CMK | Construction Master Keyed |
| 67 | DT – Dummy Thumbpiece Escutcheon |  |  |  |  |  |  |
|  |  |  |  |  |  | MAIS | Maison Keyed |
|  |  |  |  | Painted |  |  |  |
| 70 | NL – Night Latch Lever Escutcheon |  | 689 |  |  |  |  |
|  |  |  |  |  |  | MK | Master Keyed |
|  |  |  |  | Aluminum |  |  |  |
| 75 | NL – Night Latch Pull |  |  |  |  |  |  |
|  |  |  |  |  |  | GMK | Grand Master Keyed |
| 77 | GW – Gull Wing |  |  | Painted |  |  |  |
|  |  |  |  |  |  | GGMK | Great Grand Master Keyed |
|  |  |  | 690 | Duranodic |  |  |  |
| 90 | Flat Plate |  |  | Bronze |  |  |  |
|  |  |  |  |  |  | ZB | Zero Bitted |

|  |  |  |  |  |  |  |  |  |  |  | Base Part Number |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | Series |  | Function | Design |  | Finish | Keyway |  | Keying |  | Notes |
|  |  | QET3 |  | 60 |  | E |  | 689 |  | KW |  | KD |  | XXXX |
| QET3xx | Grade 1 Standard- |  |  | E |  | Sierra |  |  |  | KW |  | Kwikset “KW” |  |  |
|  | Duty Exit Trim |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  | M |  | Summit |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  | WE |  | Weiser “E” |  |  |  |
|  |  |  |  |  |  | A |  | Slate |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  | SC |  | Schlage “C” |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  | GA |  | Yale “GA” |  |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  | LA |  | Sargent “LA” |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  | BF |  | SFIC “F” |  |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  | LC |  | Less Cylinder |  |  |

- Full Line Catalog STANLEY Commercial Hardware

QRT 300 Series: Grade 1 Standard-Duty Exit Rose Trims

Round Rose Trims Sierra (E)	Round Rose Trims Summit (M)

• Available in: 626, 689, 690	• Available in: 626, 689, 690

A

B

D

C

|  |  | Dimensions |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  | A | B | C | D | DEVICES |
| Summit | 4.95" | 3.45" | 3.12" | .52" |  |
| Sierra | 4.98" | 3.15" | 3.12" | .52" |  |
|  | 126.49mm | 80.01mm | 79.25mm | 13.21mm |  |
|  |  |  |  |  | EXIT |
|  | 125.73mm | 87.63mm | 79.25mm | 13.21mm |  |

| Model/Series | Functions | Description | Style | Case |
| --- | --- | --- | --- | --- |
|  |  |  |  | Qty |
| QRT320 | Dummy Lever | Used for door pull when device is dogged or as matching inactive trim. | E/M | 12 |
|  |  | No mechanical operation. |  |  |
| QRT330 | Passage Lever | Levers always unlocked and always free for immediate ingress. | E/M | 12 |
| QRT360/361 | Keyed Lever | Key locks & unlocks lever (operates same as classroom function). Clutch feature disengages | E/M | 12 |
|  | (Classroom) | outside lever from latch when locked to prevent vandalism. |  |  |
| QRT370/371 | Keyed Lever | Lever always locked, key retracts latch for entrance (operates same as storeroom function). | E/M | 12 |
|  | (Storeroom) | Clutch feature disengages outside lever from latch when locked to prevent vandalism. |  |  |

Full Line Catalog STANLEY Commercial Hardware	65

EXIT DEVICES

How to Order

QRT 300 Series: Grade 1 Standard-Duty Exit Rose Trims

Example

If you ordered: QRT360 E 689 KW KD

You would get: Standard-Duty Keyed Lever Round Rose Trim, Sierra design, Painted Aluminum finish, Kwikset Keyway, Keyed Different. This trim matches the QED300 Series Exit Devices.

|  |  |  |  |  |  | KD | Keyed Different |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | KA | Keyed Alike |
|  |  |  |  |  |  | CK | Construction Keyed |
| 20 | DL – Dummy Lever |  |  |  |  |  |  |
|  |  |  |  |  |  | CMK | Construction Master Keyed |
| 30 | PL – Passage Lever |  |  |  |  |  |  |
|  |  |  |  |  |  | MAIS | Maison Keyed |
| 60 | KL – Keyed Lever |  |  |  |  |  |  |
|  |  |  |  |  |  | MK | Master Keyed |
| 61 | KL – Keyed Lever SFIC |  | 626 | Satin Chrome |  |  |  |
|  |  |  |  |  |  | GMK | Grand Master Keyed |
|  |  |  | 689 | Painted Aluminum |  |  |  |
| 70 | NL – Night Latch Lever |  |  |  |  |  |  |
|  |  |  |  |  |  | GGMK | Great Grand Master Keyed |
|  |  |  | 690 | Painted Duranodic Bronze |  |  |  |
| 71 | NL – Night Latch Lever SFIC |  |  |  |  |  |  |
|  |  |  |  |  |  | ZB | Zero Bitted |

|  |  |  |  |  |  |  |  |  |  | Base Part Number |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | Series |  | Function |  | Design |  |  | Finish |  | Keyway |  | Keying |  | Notes |
|  |  | QRT3 |  | 60 |  |  | E |  | 689 |  | KW |  | KD |  | XXXX |
| QRT3xx | Standard-Duty Rose |  |  | E |  | Sierra |  |  |  |  | KW |  | Kwikset “KW” |  |
|  | Exit Trim |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  | M |  | Summit |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  |  | WE |  | Weiser “E” |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  | SC |  | Schlage “C” |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  | GA |  | Yale “GA” |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  | LA |  | Sargent “LA” |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  | BF |  | SFIC “F” |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  | LC |  | Less Cylinder |  |

- Full Line Catalog STANLEY Commercial Hardware

Door Closers

QDC 100 Series: Grade 1 Extra Heavy-Duty Door Closers

DOOR CLOSERS

Performance Features

- Fully adjustable from 1 - 6 allowing for maximum flexibility.

- All-weather fluid ensures optimal operational performance in multiple climate conditions.

- Delayed action and backcheck are standard in the same door closer body.

Certifications

- ANSI/BHMA A156.4 Series – Grade 1

- ANSI A117.1 Accessibility Code (ADA Compliant)

- UL/cUL listed (3 hour) for self closing

- UL10C Positive Pressure Rated

- UL10B Pressure Rated

Product Specifications

- Handing – All QDC100 Series Closers are non-handed (QDC116 arms & metal covers are handed).

- Cast-iron closer body.

- All-weather fluid.

- Stacked valves prevent oil leaks from screws being backed out too far.

- Cover – metal and plastic covers available.

- Arms & brackets – Tri-pack standard, additional arms optional.

- Arm material – Heat-treated carbon steel.

- Springs – High-impact hand-drawn steel wires.

- Pinions – Heat-treated chrome molybdenum steel.

- Cylinder construction – Heat-treated free-cutting carbon steel.

- Fasteners – Wood and machine screws standard; sex nuts and self-reaming, self-tapping screws shipped standard.

- Door weights & sizes:

|  |  |  |  |  | Door Width Ranges |
| --- | --- | --- | --- | --- | --- |
| Size | Applicable Door Weight | Interior | Exterior |
| 1 | 33 | – 55 LBS (15 – 30 Kg) | 32" (0.81m) | 28" (0.71m) |
| 2 | 56 | – 99 LBS (30 – 45 Kg) | 36" (0.91m) | 32" (0.81m) |
| 3 | 99 | – 143 LBS (45 – 65 Kg) | 42" (1.07m) | 36" (0.91m) |
| 4 | 143 | – 187 LBS (65 | – 85 Kg) | 48" (1.22m) | 42" (1.07m) |
| 5 | 187 | – 264 LBS (85 | – 120 Kg) | 54" (1.37m) | 48" (1.22m) |
| 6* | 264 | – 330 LBS (120 – 150 Kg) | 58" (1.47m) | 54" (1.32m) |

*50% spring power adjustment over size 6.

Warranty

- Lifetime Mechanical and 3-year finish

QDC111

Rounded Plastic Cover (R)

(Ships Standard)

Metal Cover (M)

(Left hand shown)

Door Closer Functions

| Series | Description |
| --- | --- |
| QDC111 | Tri-Pack Arm |
| QDC112 | Tri-Pack Arm with Hold-Open |
| QDC113 | Extra Duty Arm with Compression Stop |
| QDC114 | Extra Duty Arm with Hold-Open and |
|  | Compression Stop |
| QDC115 | Extra Duty Arm |
| QDC116 | Extra Duty Arm with Hold-Open (handed) |
| QDC117 | Extra Duty Arm with Stop |
| QDC118 | Extra Duty Arm with Hold-Open and Stop |
| QDC119 | Extra Duty Arm with Spring Stop |
| QDC120 | Extra Duty Arm with Hold Open and Spring |
|  | Stop |

Finishes

BHMA	Description

- Painted Aluminum

- Painted Dark Bronze

| 696 | Painted Satin Brass |
| --- | --- |

- Full Line Catalog STANLEY Commercial Hardware

QDC 100 Series: Grade 1 Extra Heavy-Duty Door Closers

|  |  |  |  |  |  |  |  |  | Dimensions |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | A |  |  | A | B | C |  |
|  |  |  |  |  |  |  | C | 3.50" | 2.25" | 12.1875" |  |
|  |  |  |  |  |  |  |  | 88.90mm | 57.15mm | 309.56mm |  |
|  |  |  |  |  |  | B |  |  |  |  |  |  |
| Model/Series |  | Functions |  |  |  |  |  |  |  | Case Qty |
| QDC111 |  | Tri-Pack Arm |  |  |  |  |  |  |  | 3 |
| QDC112 |  | Tri-Pack Arm with Hold-Open |  |  |  |  |  | 1 |
| QDC113 |  | Extra Duty Arm with Compression Stop |  |  |  |  |  | 1 |
| QDC114 |  | Extra Duty Arm with Hold-Open and Compression Stop |  |  |  |  | 1 |
| QDC115 |  | Extra Duty Arm |  |  |  |  |  |  |  | 1 |
| QDC116 |  | Extra Duty Arm with Hold-Open (handed) |  |  |  |  |  | 1 |
| QDC117 |  | Extra Duty Arm with Stop |  |  |  |  |  | 1 |
| QDC118 |  | Extra Duty Arm with Hold-Open and Stop |  |  |  |  |  | 1 |
| QDC119 |  | Extra Duty Arm with Spring Stop |  |  |  |  |  | 1 |
| QDC120 |  | Extra Duty Arm with Hold Open and Spring Stop |  |  |  |  |  | 1 |
| Order with Closer |  |  | Description |  |  |  | Service Part # |
|  |  |  |  |  | Sex nuts (Qty 4) (specify finish) |  |  |  | 8Q00097 |
|  |  |  |  |  | Self-reaming, self-tapping screws (specify finish) |  |  | 8Q00547 |
|  |  |  | M |  | QDC100 Series Metal Cover - RH |  |  |  | 8Q01140 |
|  |  |  | M |  | QDC100 Series Metal Cover - LH |  |  |  | 8Q01141 |

DOOR CLOSERS

Full Line Catalog STANLEY Commercial Hardware	69

How to Order

QDC 100 Series: Grade 1 Extra Heavy-Duty Door Closers

Example

If you ordered: QDC111R 689 BF RH

You would get: Grade 1 Extra Duty Door Closer – Full Adjustable

(Sized 1-6), Tri-Pack Arm, Rounded Plastic Cover, Barrier Free, Painted

Aluminum Finish

CLOSERS

- Tri-Pack Arm

- Tri-Pack Arm with Hold-Open

- Extra Duty Arm with Compression Stop

- Extra Duty Arm with Hold-Open and Compression Stop

- Extra Duty Arm

- Extra Duty Arm with Hold-Open

- Extra Duty Arm with Stop

- Extra Duty Arm with Hold-Open and Stop

- Extra Duty Arm with Spring Stop

- Extra Duty Arm with Hold Open and Spring Stop

- Painted Aluminum

- Painted Dark Bronze

- Painted Satin Brass

QDC 116 HEDA Arm and Metal Cover Only

| LH | Left Hand |
| --- | --- |
| RH | Right Hand |

DOOR

|  |  |  |  |  |  |  |  | Base Part Number |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | Series | Function |  | Trim | Finish |  | Options |  | Handing |  |
|  |  | QDC1 | 11 |  | R | 689 |  | BF |  |  |  |
| QDC1xx | Grade 1 Extra Heavy- |  |  | R |  | Full-Size Rounded Plastic Cover |  | BF |  | Barrier Free |  |
|  | Duty Architectural |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  | M |  | Full-Size Metal Cover |  |  |  |  |  |

- Full Line Catalog STANLEY Commercial Hardware

QDC 200 Series: Grade 1 Heavy-Duty Door Closers

Performance Features

- Fully adjustable from 1 - 6 allowing for maximum flexibility.

- Delayed action and backcheck are standard in the same door closer body.

- All-weather fluid ensures optimal operational performance in multiple climate conditions.

Certifications

- ANSI/BHMA A156.4 Series – Grade 1

- ANSI A117.1 Accessibility Code (ADA Compliant)

- UL/cUL listed (3 hour) for self-closing doors without hold open

- UL10C Positive Pressure Rated

- UL10B Pressure Rated

Product Specifications

- Handing – All QDC200 Series Closers are non-handed.

- Material – Cast aluminum closer body.

- All-weather fluid.

- Cover – Slim-line plastic cover standard. Full, architectural plastic cover also available.

- Arms & brackets – Tri-pack standard (regular, top jamb, parallel configurations). Hold open and dead stop arms also available.

- Arm material – Heat-treated carbon steel.

- Springs – High-impact hand-drawn steel wires.

- Pinions – Heat-treated chrome molybdenum steel.

- Cylinder construction – Heat-treated free-cutting carbon steel.

- Fasteners – Wood and machine screws standard; sex nuts and self-reaming, self-tapping screws shipped standard.

- Door weights & sizes:

|  |  |  |  |  | Door Width Ranges |
| --- | --- | --- | --- | --- | --- |
| Size | Applicable Door Weight | Interior | Exterior |
| 1 | 33 | – 55 LBS (15 – 30 Kg) | 32" (0.81m) | 28" (0.71m) |
| 2 | 56 | – 99 LBS (30 – 45 Kg) | 36" (0.91m) | 32" (0.81m) |
| 3 | 99 | – 143 LBS (45 – 65 Kg) | 42" (1.07m) | 36" (0.91m) |
| 4 | 143 | – 187 LBS (65 | – 85 Kg) | 48" (1.22m) | 42" (1.07m) |
| 5 | 187 | – 264 LBS (85 | – 120 Kg) | 54" (1.37m) | 48" (1.22m) |
| 6 | 264 | – 330 LBS (120 – 150 Kg) | 58" (1.47m) | 54" (1.32m) |

Tri-Pack Arm	Tri-Pack Arm with

Hold-Open

Heavy Duty Arm with	Heavy Duty Arm

Compression Stop	with Hold-Open and

Compression Stop

Door Closer Functions

| Series | Description |
| --- | --- |
| QDC211 | Tri-Pack Arm |
| QDC212 | Tri-Pack Arm with Hold-Open |
| QDC213 | Heavy Duty Arm with Compression Stop |
| QDC214 | Heavy Duty Arm with Hold-Open and |
|  | Compression Stop |

Finishes

BHMA	Description

- Painted Aluminum

- Painted Dark Bronze

| 696 | Painted Satin Brass |
| --- | --- |

DOOR CLOSERS

Warranty

- Lifetime Mechanical and 3-year finish

Full Line Catalog STANLEY Commercial Hardware	71

How to Order

QDC 200 Series: Grade 1 Heavy-Duty Door Closers

DOOR CLOSERS

| A |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  | B |  |  |  |  |
|  |  |  |  | DIMENSIONS |  |
|  |  | A |  | B | C |
|  |  | 2.05" | 3.18" | 12" |
|  |  | 52.20mm | 80.70mm | 305mm |
|  |  | C |  |  |  |
| Model/Series | Functions |  |  | Qty |
| QDC211 | Tri-Pack Arm |  |  | 6 |
| QDC212 | Tri-Pack Arm with Hold-Open |  |  | 6 |
| QDC213 | Heavy Duty Arm with Compression Stop |  |  | 3 |
| QDC214 | Heavy Duty Arm with Hold-Open and Compression Stop |  |  | 3 |
| Order with Closer |  | Description | Service Part # |  |
|  | F | Full-size cover (specify finish) | 8Q00094 |  |
|  | S | Slim-line cover (specify finish) | 8Q00096 |  |
|  |  | Sex nuts (Qty 4) (specify finish) | 8Q00097 |  |
|  |  | Self-reaming, self-tapping screws (Qty 8) (specify finish) | 8Q00436 |  |

- Full Line Catalog STANLEY Commercial Hardware

How to Order

QDC 200 Series: Grade 1 Heavy-Duty Door Closers

Example

If you ordered: QDC211 F 689

You would get: Grade 1 Heavy-Duty Slim-Line Non-Hold Open Door Closer – Full Adjustable (Sized 1-6), Tri-Packed Arms with both Delayed Action & Backcheck Standard, full-size cover, Painted Aluminum finish.

| 11 | Tri-Pack Arm |  |  |  |
| --- | --- | --- | --- | --- |
| 12 | Tri-Pack Arm with Hold-Open |  | 689 | Painted Aluminum |
| 13 | Heavy Duty Arm with Compression Stop |  | 690 | Painted Dark Bronze |
| 14 | Heavy Duty Arm with Hold-Open and Compression Stop |  | 696 | Painted Brass |

|  |  |  |  |  | Base Part Number |  |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | Series | Function |  | Trim |  | Finish |
|  |  | QDC2 | 11 |  |  | F |  | 689 |
| QDC2xx | Grade 1 Heavy-Duty |  |  | F |  | Full-Size Cover |  |
|  | Architectural |  |  |  |  |  |  |  |  |
|  |  |  |  | S |  | Slim-Line Cover |  |

DOOR CLOSERS

Full Line Catalog STANLEY Commercial Hardware	73

QDC 300 Series: Grade 1 Standard-Duty Door Closers

Performance Features

- Fully adjustable from 1 - 6 allowing for maximum flexibility.

- Delayed action and backcheck are standard in the same door closer body.

- All-weather fluid ensures optimal operational performance in multiple climate conditions.

Certifications

- ANSI/BHMA A156.4 Series – Grade 1

- ANSI A117.1 Accessibility Code (ADA Compliant)

| • UL/cUL listed (3 hour) for self-closing doors without hold open | Tri-Pack Arm | Tri-Pack Arm with |
| --- | --- | --- |
|  |  | Hold-Open |
| • | UL10C Positive Pressure Rated |  |  |
| • | UL10B Pressure Rated |  |  |

DOOR CLOSERS

Product Specifications

- Handing – All QDC300 Series Closers are non-handed.

- Material – Cast aluminum closer body.

- All-weather fluid.

- Cover – Full, architectural plastic cover also available.

- Arms & brackets – Tri-pack standard (regular, top jamb, parallel configurations). Hold open and dead stop arms also available.

- Arm material – Heat-treated carbon steel.

- Springs – High-impact hand-drawn steel wires.

- Pinions – Heat-treated chrome molybdenum steel.

- Cylinder construction – Heat-treated free-cutting carbon steel.

- Fasteners – Wood and machine screws standard; sex nuts and self-tapping screws shipped standard.

- Door weights & sizes:

|  |  |  |  |  | Door Width Ranges |
| --- | --- | --- | --- | --- | --- |
| Size | Applicable Door Weight | Interior | Exterior |
| 1 | 33 | – 55 LBS (15 – 30 Kg) | 32" (0.81m) | 28" (0.71m) |
| 2 | 56 | – 99 LBS (30 – 45 Kg) | 36" (0.91m) | 32" (0.81m) |
| 3 | 99 | – 143 LBS (45 – 65 Kg) | 42" (1.07m) | 36" (0.91m) |
| 4 | 143 | – 187 LBS (65 | – 85 Kg) | 48" (1.22m) | 42" (1.07m) |
| 5 | 187 | – 264 LBS (85 | – 120 Kg) | 54" (1.37m) | 48" (1.22m) |
| 6 | 264 | – 330 LBS (120 – 150 Kg) | 58" (1.47m) | 54" (1.32m) |

Warranty

- Lifetime Mechanical and 3-year finish

Heavy Duty Arm with	Heavy Duty Arm

Compression Stop	with Hold-Open and

Compression Stop

Door Closer Functions

| Series | Description |
| --- | --- |
| QDC311 | Tri-Pack Arm |
| QDC312 | Tri-Pack Arm with Hold-Open |
| QDC313 | Heavy Duty Arm with Compression Stop |
| QDC314 | Heavy Duty Arm with Hold-Open and |
|  | Compression Stop |

Finishes

BHMA	Description

- Painted Aluminum

- Painted Dark Bronze

| 696 | Painted Satin Brass |
| --- | --- |

- Full Line Catalog STANLEY Commercial Hardware

QDC 300 Series: Grade 1 Standard-Duty Door Closers

A

B

C

|  |  |  |  | CLOSERS |
| --- | --- | --- | --- | --- |
|  |  |  |  | DOOR |
|  | Dimensions |  |  |  |
| A | B | C |  |  |
| 2.62" | 3.08" | 9.80" |  |  |
| 66.50mm | 78.10mm | 249mm |  |  |

| Model/Series | Functions | Qty |
| --- | --- | --- |
| QDC311 | Tri-Pack Arm | 6 |
| QDC312 | Tri-Pack Arm with Hold-Open | 6 |
| QDC313 | Heavy Duty Arm with Compression Stop | 3 |
| QDC314 | Heavy Duty Arm with Hold-Open and Compression Stop | 3 |

| Order with Closer | Description | Service Part # |
| --- | --- | --- |
|  | F | Full-size cover (specify finish) | 8Q00094 |
|  | S | Slim-line cover (specify finish) | 8Q00096 |
|  |  | Sex nuts (Qty 4) (specify finish) | 8Q00097 |
|  |  | Self-tapping screws (Qty 8) (specify finish) | 8Q00436 |

Full Line Catalog STANLEY Commercial Hardware	75

How to Order

QDC 300 Series: Grade 1 Standard-Duty Door Closers

DOOR CLOSERS

Example

If you ordered: QDC311 F 689 BF

You would get: Grade 1 Standard-Duty Non-Hold Open Door Closer – Full Adjustable (Sized 1-6), Tri-Packed Arms with Both Delayed Action & Backcheck Standard, full-size cover, Painted Aluminum finish, and Barrier Free.

| 11 | Tri-Pack Arm |  |  |  |
| --- | --- | --- | --- | --- |
| 12 | Tri-Pack Arm with Hold-Open |  |  |  |
|  |  |  | 689 | Painted Aluminum |
| 13 | Heavy Duty Arm with Compression Stop |  | 690 | Painted Duranodic Bronze |
| 14 | Heavy Duty Arm with Hold-Open and Compression Stop |  | 696 | Painted Satin Brass |

|  |  |  |  |  |  | Base Part Number |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | Series | Function |  | Trim |  | Finish |  | Options |  |  |
|  |  | QDC3 | 11 |  | F |  | 689 |  | BF |  |  |
| QDC3xx | Grade 1 Standard- |  |  | F |  | Full-Size Cover |  |  |  | BF | Barrier Free |
|  | Duty |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  | S |  | Slim-Line Cover |  |  |  |  |  |  |  |
|  |  |  |  |  |  | NC |  | No Cover |  |  |  |  |  |  |  |

- Full Line Catalog STANLEY Commercial Hardware

Miscellaneous Information

Windstorm- & Hurricane- Compliant Hardware Tests

MISCELLANEOUS

Windstorm- and Hurricane-Compliant Hardware have passed structural tests as per South Florida Building Code Protocol. These tests are designed to provide sufficient resistance to high-wind forces and windborne debris. The hardware provides a high level of security for door openings even if hurricane-rated door components are not required. A brief description of the test is provided below.

Static Air Pressure Test

Test simulates wind loading by evenly distributing air pressure to the face of the door assembly in positive and negative directions.

The door assembly must not have excessive deflection or deformation and must remain secure in the chamber.

Missile Impact Test

Test simulates impacts created by wind driven debris by impacting the exterior face of the doors with a 2" x 4" x 9' board at 50 feet per second. The board must not pass through the doors and the doors must remain secure in the chamber.

Cyclic Wind Pressure Test

Test simulates wind gusts by repeating cycles of positive and negative air pressure to determine that the integrity of the door assembly is not compromised with the Missile Impact Test. The door assembly must not have excessive deflection or deformation and must remain secure in the chamber.

Component Approval

The hardware listed is approved as components to be used with any 18-gauge single or pair of hollow metal doors with 16-gauge frames holding a current Notice of Acceptance (NOA). The lowest Design Pressure Rating of the doors or components shall apply.

Notice of Acceptance (NOA)

The Miami-Dade County Product Control Division has approved these devices to be used in Miami-Dade County and other areas where allowed by the Authority Having Jurisdiction (AHJ). Product Control NOA Numbers 11-0325.04 (locking products) and 11-0606.02 (exit devices) have been issued and expire on August 18, 2016.

To see the NOA documentation online, visit: http://www.miamidade.gov/building/pc-search.app.asp and type in the NOA numbers referenced above under the Product Search Application link.

- Full Line Catalog STANLEY Commercial Hardware

Windstorm- & Hurricane- Compliant Hardware Charts

|  | Locks & Deadbolts |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  | Single Door |  |  |  | Pair of Doors with Mullion |  |  | Pair of Doors with SVR |
|  |  |  |  |  |  |  |  |  | Max |  |  |  |  |  |  | Max |  |  |  |  |  |  |  |  | Max |
|  | Product |  | Opening |  |  |  | Design | Opening |  |  |  | Design |  |  | Opening |  |  |  |  |  | Design |
|  |  |  |  |  | Model #* | Pressure |  | Model # |  | Pressure |  |  |  |  |  | Model # |  | Pressure |
|  |  |  | Size |  |  |  |  | Size |  |  |  |  |  |  | Size |  |  |  |  |  |
|  |  |  |  |  |  |  |  | Rating |  |  |  |  |  | Rating |  |  |  |  |  |  |  |  | Rating |
|  |  |  |  |  |  |  |  |  | (PSF) |  |  |  |  |  |  | (PSF) |  |  |  |  |  |  |  |  | (PSF) |
|  | Grade 1 |  |  |  |  |  | QCL100 with |  |  |  |  | QCL100 with |  |  |  |  |  |  |  | QCL100 with |  |  |
|  | Cylindrical |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  | QDB100/200 & |  |  |  |  |  |  | QDB100/200 & |  |  |
|  | with |  |  |  |  |  | QDB100/200 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  | QED111/112/113 |  |  |  |  | QED114/115/116 |  |  |
|  | Deadbolt |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | Grade 2 |  | 4' 0" x |  |  | QCL200 with |  | 8' 0" x |  | QCL200 with |  |  |  |  | 8' 0" x |  |  | QCL200 with |  |  |
|  | Cylindrical |  |  |  |  |  | 75 |  |  |  |  | 75 |  |  |  |  |  |  |  | 68 |
|  |  |  | 8' 0" |  |  |  |  | 8' 0" |  | QDB100/200 & |  |  |  | 8' 0" |  | QDB100/200 & |  |  |
|  | with |  |  |  |  | QDB100/200 |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  | QED111/112/113 |  |  |  |  | QED114/115/116 |  |  |
|  | Deadbolt |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | Grade 2 |  |  |  |  |  | QTL200 with |  |  |  |  | QTL200 with |  |  |  |  |  |  |  | QTL200 with |  |  |
|  | Tubular with |  |  |  |  |  |  |  |  |  |  | QDB100/200 & |  |  |  |  |  |  | QDB100/200 & |  |  |
|  |  |  |  |  |  |  | QDB100/200 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | Deadbolt |  |  |  |  |  |  |  |  |  |  | QED111/112/113 |  |  |  |  | QED114/115/116 |  |  |
| * Dummy functions not included. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | Exit Devices |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  | Single Door |  |  |  |  |  | Pair of Doors with Mullion |  |  |
|  | Product |  |  | Opening Size |  | Model # |  |  | Max Design |  | Opening Size |  |  | Model # |  | Max Design |
|  |  |  |  |  |  |  |  |  | Pressure Rating |  |  |  |  |  |  | Pressure Rating |
|  |  |  |  |  |  |  |  |  |  |  |  |  | (PSF) |  |  |  |  |  |  |  |  |  |  | (PSF) |
|  |  |  |  |  |  |  |  |  | QED111 |  |  |  |  |  |  |  |  |  | QED111 |  |  |  |  |  |
|  |  |  |  |  |  | 4' 0" x 8' 0" |  | QED112 |  |  |  | 75 |  | 8' 0" x 8' 0" |  |  | QED112 |  |  |  | 75 |
|  |  |  |  |  |  |  |  |  | QED113 |  |  |  |  |  |  |  |  |  | QED113 |  |  |  |  |  |
|  | Grade 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Pair of Doors with SVR |  |  |
|  | Heavy-Duty |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | QED114 |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 8' 0" x 8' 0" |  |  | QED115 |  |  |  | 68 |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | QED116 |  |  |  |  |  |

MISCELLANEOUS

Full Line Catalog STANLEY Commercial Hardware	79

Competitive Cross-Reference

MISCELLANEOUS

Auxiliary Deadbolts

|  |  | Arrow | Corbin | Sargent | Yale | Marks | Schlage | Falcon | Hager | Dorma | Cal |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | Russwin |  |  |  |  |  |  |  | Royal |
| Grade 1 | QDB100 | DC60 | DL3100 | 480 | 3600 | 140 | B600 | D100 | 3100 | DB800 | CRB800 |
| Deadbolt | Series | Series | Series | Series | Series | Series | Series | Series | Series | Series | Series |
| Grade 2 | QDB200 | E60 | DL2100 | 470 | 3500 | — | BC100 | D200 | 3200 | DB600 | T300 |
| Deadbolt | Series | Series | Series | Series | Series |  | Series | Series | Series | Series | Series |

Mechanical Locksets

|  |  | Arrow | Corbin | Sargent | Yale | Marks | Schlage | Falcon | Hager | Dorma | Cal |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | Russwin |  |  |  |  |  |  |  | Royal |
| Grade 1 | QML100 | BW | ML2000 | 8200 | 8800 | — | L | MA | 3800 | M9000 | NM |
| Mortise | Series | Series | Series | Series | Series |  | Series | Series | Series | Series | Series |
| Grade 1 | QCL100 |  |  |  |  |  |  |  |  |  | Genesys |
|  |  | Q Series | CL3300 | 10 Line | 5400LN | 95 Line | ND | T | 3400 | CL800 | Series/ |
| Cylindrical | Series | W Series | Series | Series | Series | Series | Series | Series | Series | Series | Calypso |
|  |  |  |  |  |  |  |  |  |  |  | Series |
| Grade 2 | QCL200 | ML | CL3800 | 7 Line | 5300LN | 70 Line | AL | B Series | 3500 | CL700 | SL |
| Cylindrical | Series | Series | Series | Series | Series | Series | Series | W Series | Series | Series | Series |
| Grade 2 | QTL200 | C Series | CL3700 | DL | 4300LN | — | S Series | Y Series | 3600 | CL600 | SG |
| Tubular | Series |  | Series | Series | Series |  |  |  | Series | Series | Series |

Exit Devices

| Arrow | Corbin | Sargent Yale Marks | Von | Falcon Hager Dorma | Cal |
| --- | --- | --- | --- | --- | --- |
|  | Russwin |  | Duprin |  | Royal |

| Grade 1 |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Heavy-Duty | QED100 | 3000 | ED5000 | 80 | 7000 | — | 98/99 | 24 Series | 4500 | 9000 | 7700 |
| Architectural | Series | Series | Series | Series | Series |  | Series | 25 Series | Series | Series | Series |
| Push Bar |  |  |  |  |  |  |  |  |  |  |  |
| Grade 1 |  |  |  |  |  |  |  |  |  |  |  |
| Economy | QED300 | 1000 | ED8000 | 30 | 2100 | — | 22 | 19 | 4700 | 8000 | 2200 |
| Standard | Series | Series | Series | Series | Series |  | Series | Series | Series | Series | Series |
| Push Bar |  |  |  |  |  |  |  |  |  |  |  |

Door Closers

| Arrow | Corbin | Sargent Yale Norton | LCN | Falcon Hager Dorma | Cal |
| --- | --- | --- | --- | --- | --- |
|  | Russwin |  |  |  | Royal |

| Grade 1 | QDC100 | DC500 | DC6200 |  | 4400 | 7500 | 4040 | SC70 | 5100 | 8900 | CR441 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Extra |  |  |  | 281 Series |  |  |  |  |  |  |  |
|  | Series | Series | Series |  | Series | Series | Series | Series | Series | Series | Series |
| Heavy-Duty |  |  |  |  |  |  |  |  |  |  |  |
| Grade 1 | QDC200 | 5000N | DC3000 | 1331 | 3000 | 8000 | 1460 | SC80 | 5200 | 8600 | CR801 |
| Heavy-Duty |  |  |  |  |  |  |  |  |  |  | Series 900 |
|  | Series | Series | Series | Series | Series | Series | Series | Series | Series | Series |  |
| (Slim-Line) |  |  |  |  |  |  |  |  |  |  | Series |
| Grade 1 | QDC300 | 900N | DC4600 | 1130 | 51 | 1601 | 1070 | SC60 | 5300 | 7400 |  |
| Standard- |  |  |  |  |  |  |  |  |  |  | 300 Series |
|  | Series | Series | Series | Series | Series | Series | Series | Series | Series | Series |  |
| Duty |  |  |  |  |  |  |  |  |  |  |  |

- Full Line Catalog STANLEY Commercial Hardware

Notes

___________________________________________________________________________________________________________________________

___________________________________________________________________________________________________________________________

___________________________________________________________________________________________________________________________

___________________________________________________________________________________________________________________________

___________________________________________________________________________________________________________________________

___________________________________________________________________________________________________________________________

___________________________________________________________________________________________________________________________

___________________________________________________________________________________________________________________________

___________________________________________________________________________________________________________________________

___________________________________________________________________________________________________________________________

___________________________________________________________________________________________________________________________

___________________________________________________________________________________________________________________________

___________________________________________________________________________________________________________________________

___________________________________________________________________________________________________________________________

___________________________________________________________________________________________________________________________

___________________________________________________________________________________________________________________________

___________________________________________________________________________________________________________________________

___________________________________________________________________________________________________________________________

___________________________________________________________________________________________________________________________

___________________________________________________________________________________________________________________________

NOTES

Full Line Catalog STANLEY Commercial Hardware	81

NOTES

Notes

___________________________________________________________________________________________________________________________

___________________________________________________________________________________________________________________________

___________________________________________________________________________________________________________________________

___________________________________________________________________________________________________________________________

___________________________________________________________________________________________________________________________

___________________________________________________________________________________________________________________________

___________________________________________________________________________________________________________________________

___________________________________________________________________________________________________________________________

___________________________________________________________________________________________________________________________

___________________________________________________________________________________________________________________________

___________________________________________________________________________________________________________________________

___________________________________________________________________________________________________________________________

___________________________________________________________________________________________________________________________

___________________________________________________________________________________________________________________________

___________________________________________________________________________________________________________________________

___________________________________________________________________________________________________________________________

___________________________________________________________________________________________________________________________

___________________________________________________________________________________________________________________________

___________________________________________________________________________________________________________________________

___________________________________________________________________________________________________________________________

___________________________________________________________________________________________________________________________

___________________________________________________________________________________________________________________________

- Full Line Catalog STANLEY Commercial Hardware

6161 East 75th Street

Indianapolis, IN 46250 USA

Phone 855-365-2407

stanleyhardwarefordoors.com

ST-CH-0005 Rev. 7/14/2018

© 2018 dormakaba Holding. All rights reserved.

| © 2018 Stanley Black & Decker, Inc. STANLEY® and the STANLEY® Notched Rectangle logo are | dormakaba.com |
| --- | --- |
| registered trademarks of Stanley Black & Decker Inc. or one of its affiliates, and are used under license |  |