Concealed

closer series

Product selection guide

The concealed LCN closers feature a modern design for concealment in either the head frame or top rail of the door. This guide is based on the desired mounting of the closer.

EXTERIOR

DOOR

|  |  | CONCEALED |  |  |  |  |  | CONCEALED IN |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | IN FRAME |  |  |  |  |  | TUBE FRAME |  |  |  |
|  | DOUBLE |  |  |  |  | SINGLE |  |  | DOUBLE |  |  |  | SINGLE |
|  | LEVER ARM |  |  |  | LEVER ARM |  |  | LEVER ARM |  |  |  | LEVER ARM |
| 5010 |  |  |  |  | 2010 2210** |  | 5030 |  |  |  |  | 2030 | 6030 |

INTERIOR

DOOR

|  |  | CONCEALED |  |  |  |  |  | CONCEALED IN |  |  |  |  |  |  | CONCEALED |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | IN FRAME |  |  |  |  | TUBE FRAME |  |  |  |  |  |  | IN DOOR |  |  |  |
|  | DOUBLE |  |  |  |  | SINGLE |  |  | DOUBLE |  |  |  | SINGLE |  |  | DOUBLE |  |  |  | SINGLE |
|  | LEVER ARM |  |  |  | LEVER ARM |  |  | LEVER ARM |  |  |  | LEVER ARM |  |  | LEVER ARM |  |  |  | LEVER ARM |
| 5010 |  |  |  |  | 2010 2210** |  |  | 5030 |  |  |  |  | 2030 | 6030 |  | 3030 |  |  |  |  | 3130 | 3130SE*** |

- INDICATES HIGH SECURITY CLOSER, DOOR POSITION SWITCH OPTIONAL. REFER TO HIGH SECURITY SECTION OF THE CATALOG.

- INDICATES FIRE LIFE SAFETY CLOSER. REFER TO FIRE LIFE SAFETY SECTION.

Product comparison

This chart shows a basic comparison of LCN concealed closers. Refer to the specific closer chapter for complete details.

|  |  |  |  |  |  |  | CONCEALED |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  | MOUNTING | FINISH | CYLINDER |  | ARM | *ARM FUNCTION |
|  |  |  |  | -3/4˝ | TUBE | COAT |  |  | ACTION |  |  | (SINGLE) |
| CLOSER |  | FRAME |  |  |  | DOOR | POWDERPLATED | HANDEDSIZED | DELAYED |  | EXPOSED | STANDARD | -OPEN |
|  | IN |  |  |  | IN |  |  |  |  |  |  |  | HOLD |
|  |  | IN |  |  |  |  |  |  |  |  |  |  |
| SERIES |  |  | 1 |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  | 180° | 110° |
| 2010 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 2030 |  |  |  |  |  |  |  |  |  |  |  |  | 180° | 110° |
| 3030 |  |  |  |  |  |  |  |  |  |  |  |  | 180° | 140° |
| 3130 |  |  |  |  |  |  |  |  |  |  |  |  | 140° | 100° |
| 5010 |  |  |  |  |  |  |  |  |  |  |  |  | 180° | 100° |
| 5030 |  |  |  |  |  |  |  |  |  |  |  |  | 180° | 100° |
| 6030 |  |  |  |  |  |  |  |  |  |  |  |  | 95° | 95° |

| AVAILABLE | Closer available with less than 5.0 lbs. opening force on 36˝ door. |  |
| --- | --- | --- |
| NOT AVAILABLE |  |  |
|  | * Maximum opening/hold-open point with standard template. See individual closer series for degrees of opening per |  |
|  | installation. |  |
|  |  | D1 |
|  | LCN Door Control Catalog |  |

phone: 877-671-7011	n	fax: 800-248-1460	n	www.allegion.com/us	n	009426	rev. 11/16

Concealed

closer series

APPLICATIONS

- For aluminum, hollow metal, or wood doors and frames.

- Can be used with hinge or pivot mounted door.

- Closers for 4˝ or minimum 1-3/4˝ head frame or 4˝ top rail.

- Mounting clips for wood frames and other installation accessories available for unusual conditions.

- For concealed in door closers consult factory for installations with pivots.

FEATURES COMMON TO CONCEALED CLOSERS

- Mountings for head frame or door top rail.

- Handed for right or left swinging doors. (except 6030)

- Closers to meet ADA reduced opening force requirements.

- Adjustable hydraulic backcheck cushions opening swing prior to 90°.

- Separate regulation of general closing speed and latching speed.

- Joints in arm and shoe adapt to uneven trim. (for double lever arms)

DESIGN ASSISTANCE

LCN has been providing reliable solutions to unique door control problems since 1925. Design and specification assistance are only a phone call away. Contact LCN for assistance or technical information at 877-671-7011

or FAX 800-248-1460 (Order Entry), Fax 815-879-1495 for Product Support.

WARRANTY

15 year limited warranty. See General Information Section for complete warranty details.

SPECIFICATIONS

Refer to “SPECIFICATIONS”section for suggested architectural specifications.

MATERIALS

(Closers concealed in the door or frame)

- High strength cast iron cylinder.

- Forged steel main arms (except 6030).

- One piece forged steel piston.

- All weather fluid in overhead concealed models performs to temperature ranges from 120°F (49°C) to -30°F (-35°C) without any seasonal adjustment.

- High efficiency, full complement, low friction bearings.

- Tamper resistant regulating screws.

- Full rack and pinion hydraulic action.

- Quiet, low friction track and roller combination for all single lever (standard) arm closers.

FINISHES

- Available in six standard or a wide selection of optional custom powder coat finishes to blend with door and frame.

- LCN’s powder coat finishes surpass 100 hours of salt spray which is over four times the ANSI standard for corrosion resistance.

- For installations where a higher level of corrosive resistance is required, LCN offers an optional special rust inhibiting (SRI) pre-treatment. Closers that combine the exclusive LCN powder coat finish and the SRI pre-treatment exceed the ANSI standard for corrosion resistance even further.

- Plated finishes are available as an option to accent door and frame. (SRI not available with plated finishes)

LISTINGS & APPROVALS

UL listed for self-closing doors without hold-open under “SWINGING DOOR CLOSERS” (GVEV) file R 1943.

Tested and certified under ANSI Standard A156.4. Consult factory for details.

Consult factory for other listings such as; cUL, California State Fire Marshal, Bureau of Standards and Appeals.

POSITIVE PRESSURE

LCN closers have been certified for three hours by UL to be in compliance with UL 10 C. Contact LCN for specific details on door closer fire ratings.

FASTENERS

Standard WOOD and MACHINE SCREW (WMS) pack contains phillips head wood and machine screws to install the closer. TORX machine screws are available for some closers.

Note 1: Phillips head, metric machine screws are available, please specify.

MAINTENANCE

Closers mounted according to LCN installation instructions require no periodic maintenance or adjustments.

D2	LCN Door Control Catalog

phone: 877-671-7011	n	fax: 800-248-1460	n	www.allegion.com/us	n	009426	rev. 11/16

2010

Series

Features

The concealed 2010 Series is a heavy duty closer designed to provide complete concealment. The single lever arm and roller assembly provide smooth, quiet door control and the choice of finishes and track functions meet virtually all architectural requirements.

| Certifications | Grade 1 - ANSI A156.4, UL 10 C, ADA, 100 Hour |
| --- | --- |
|  | Salt Spray, Meets BAA - Buy American Act |
| Body Construction | n | Cast Iron Body |
|  | n | Full Complement Bearing |
|  | n | 1-1/2˝ Diameter Piston |
|  | n | 11/16˝ Diameter Double Heat Treated |
|  |  | Pinion Journal |
| Fluid | All Weather Fluid |
| Handing | Handed |
| Size | Sized 1-6 |
| Warranty | 15 years |

| Fasteners | Wood and Machine Screw Pack |
| --- | --- |
| Mounting | Concealed (in frame); aluminum frame |
|  | requires minimum 4˝ x 4˝ (102 mm) tube |
| Arms | Standard arm and track |
| Finishes/Colors/ | n | Aluminum (689) |
| Powder Coat | n | Statuary Bronze (690) |
|  | n | Light Bronze (691) |
|  | n | Black (693) |
|  | n | Dark Bronze (695) |
|  | n | Brass (696) |
|  | n | Custom colors optional |
|  | n | Optional SRI primer - powder coat only |
|  | n | Optional plated finishes |

Special	Customized installation templates or products may be available to solve unusual applications.

Templates	Contact LCN Product Support for assistance.

|  |  |  |  | CONCEALED |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | MOUNTING | FINISH | CYLINDER |  | ARM | *ARM FUNCTION |
|  | -3/4˝ | TUBE | COAT |  |  | ACTION |  |  | (SINGLE) |
|  |  |  | DOOR |  |  |  |  |  |  | -OPEN |
| IN | FRAME 1 | IN |  | POWDERPLATED | HANDEDSIZED | DELAYED |  | EXPOSED | STANDARD | HOLD |
|  | IN |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  | 180° | 110° |

| AVAILABLE | Closer available with less than 5.0 lbs. opening force on 36˝ door. |  |
| --- | --- | --- |
| NOT AVAILABLE |  |  |
|  | * Maximum opening/hold-open point with standard template. See individual closer series for |  |
|  | degrees of opening per installation. |  |
|  |  | D3 |
|  | LCN Door Control Catalog |  |

phone: 877-671-7011	n	fax: 800-248-1460	n	www.allegion.com/us	n	009426	rev. 11/16

2010

Series

Mounting details

Concealed

Mounting

|  |  | 5-5/16" | 14" |  | 3-5/8" |
| --- | --- | --- | --- | --- | --- |
|  |  | 135 mm |  |  | 92 mm |
|  |  |  | 356 mm |  |  |
|  |  |  |  |  | 3/8" |
|  |  |  |  |  | 10 mm |
|  |  | 10" |  | 1-1/16" |  |
|  |  | 254 mm |  | 27 mm | 1-3/8" |
|  |  |  | 22-1/2" |  | 35 mm |
|  |  | 1" | 572 mm |  |  |
| 2-1/16" | 1-1/4" | 25 mm |  |  |  |
| 52 mm | 32mm |  |  |  |  |

1/4"

6mm

of Track

to of Closer

| Butt Hinges | Should not exceed 5˝ (127 mm) in width |
| --- | --- |
| Auxiliary Stop | n | Recommended where a door cannot swing 180° |
|  | n | Optional track bumper assembly assists backcheck in cushioning the opening swing of the door (not intended to |
|  |  | replace an auxiliary stop). |
| Top Rail | n | 1-3/8˝ (35 mm) mortise required |
|  | n | With Fire Shield, 1-13/32˝ (36 mm) mortise required |
|  | n | 5/16˝ (8 mm) cutout required at top of the door, stop face only |
| Door Thickness | 1-3/4˝ (44 mm) minimum |
| Hollow Metal Frame | Consult factory for installation instructions |
| Maximum opening | n | Butt hinge template allows 180°, trim permitting |
|  | n | Limited to 110° when optional bumper is installed |
|  | n | Adjustable hold-open points from 85° to 110°, with hold-open track |
|  | n | Offset pivot template allows 110°, trim permitting |
|  | n | Limited to 95° when optional bumper is installed |
|  | n | Adjustable hold-open points from 75° to 95°, with hold-open track |
|  | n | Center pivot template allows 120°, trim permitting |
|  | n | Limited to 95° when optional bumper is installed |
|  | n | Adjustable hold-open points from 75° to 95°, with hold-open track |

Notes:

- For interior or exterior doors

- Single acting cylinder in head frame

- Concealed arm and track in door top rail

D4

LCN Door Control Catalog

phone: 877-671-7011

n	fax: 800-248-1460

n	www.allegion.com/us

n	009426	rev. 11/16

2010

Series

Accessories

Cylinders

Arm

Installation Accessories

2011(3)(4)(5)(6)-3071 Cast Iron Cylinder Assembly

- Handed

- With mounting plate

- Standard

2010-3077T

Standard Arm

- Handed

- Track roller not included with arm

2010-420

Fire Shield

- 22 gauge steel liner mounts in the track mortise of the door’s top rail for 20 minute labeled wood doors

2010-169

Track Bumper

- Mounts in track to assist backcheck

- Limits maximum opening

- Consists of bumper, bumper post, and mounting screw

NOTE: Track bumper does not replace auxiliary stop.

Tracks

2010-3038

Standard Track

- Non-handed

- Non hold-open

- Will accept hold-open clip and/or bumper assembly.

- Standard

2010-3038H

Hold-Open Track

- Non-handed

- Will accept bumper assembly

- Optional

2010-3038B

Standard Track with Bumper

- Non-handed

- Non hold-open

- Will accept hold-open clip

- Optional

2010-3038HB

Hold-Open Track with Bumper

- Non-handed

- Optional

2010-3054

Hold-Open Clip

- Mounts in track to provide hold-open function

- Hold-open point controlled by clip location

- Requires 2010-3034H

2010-3034H

Hold-Open Track Roller

- Quiet, low friction roller assembly

- Shoulder dimension “X” = 1/16˝ (2mm)

2010-3034

Track Roller

- Quiet, low friction roller assembly

- Shoulder dimension “X” = 1/16˝ (2mm)

| LCN Door Control Catalog | D5 |
| --- | --- |
| phone: 877-671-7011 n fax: 800-248-1460 n www.allegion.com/us n 009426 | rev. 11/16 |

2010

Series

Ordering Information

| How-to-order 2010 Series closers |  |  |  |
| --- | --- | --- | --- |
|  |  | Closer will be shipped with: |  |
| Table of sizes | - Standard cylinder with finish plate |  |
| n | Select closer based on width of door. | - Standard arm |  |
| n | 2010 Series cylinders available in size 1, 3, 4, 5, or 6. | - Standard track |  |
| n | Closing power of all 2010 Series closers may be increased 15%. | - Wood and machine screw pack |  |
| n | Specify next higher size closer where strong drafts exist. | unless options listed below are selected. |  |

| Select cylinder size | Select hand |
| --- | --- |
| 2011 | RH |
| 2013 | LH |
| 2014 | Specify finish |
| 2015 |  |
| 2016 | Standard Powder Coat __________ |
|  | Aluminum, Dark Bronze, Statuary, Light Bronze, Black, Brass. |
| Closer options |  |
| Tracks | Installation accessories |
| Standard with Bumper (BUMPER) | Fire Shield, 2010-420 |
| Hold-open (H) |  |
| Hold-open with Bumper (HBUMPER) |  |
| Finishes |  |
| Custom Powder Coat (RAL)_____________ |  |
| Plated Finish, US ______________ |  |

SRI primer (use with powder coat finishes only)

| Screw pack | Special template |
| --- | --- |
| TORX Machine Screw (TORX) | ST- ________ |

Exterior (and Vestibule) door width	Interior door width

| 28˝ | 30˝ | 36˝ |  | 42˝ | 48˝ | 28˝ | 34˝ | 38˝ | 48˝ | 54˝ | 60˝ |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 711mm | 762mm | 914mm | 1067mm | 1219mm | 711mm | 864mm | 965mm | 1219mm | 1372mm | 1524mm |
| 2013 | size 3 | size 4 | size 5 | size 6 |  | 2013 | size 3 | size 4 | size 5 | size 6 |  |
| 2014 |  |  |  |  |  | 2014 |  |  |  |  |  |
| 2015 |  |  |  |  |  | 2015 |  |  |  |  |  |
| 2016 |  |  |  |  |  | 2016 |  |  |  |  |  |

| Minimum door width |  | Minimum door width |
| --- | --- | --- |
|  |  | Indicates recommended range of door width for closer size. |

Reduced opening force 2010 Series closers

CAUTION ! Any manual door closer, including those certified by BHMA to conform to ANSI Standard A156.4, that is selected, installed and adjusted based on ADA or other reduced opening force requirements may not provide sufficient power to reliably close and latch a door.

Refer to POWER OPERATORS section for information on systems that meet reduced opening force requirements without affecting closing power.

* Maximum opening force.

| DOOR WIDTH | 36˝ | 42˝ | 48˝ |
| --- | --- | --- | --- |
| 8.5* lbs. | 2014 | 2014 | 2015 |
| 5.0* lbs. | 2011 | 2011 | 2013 |

D6	LCN Door Control Catalog

phone: 877-671-7011	n	fax: 800-248-1460	n	www.allegion.com/us	n	009426	rev. 11/16

2030 Series

Features

The concealed 2030 Series PACER® is a heavy duty closer designed to fit in a narrow, minimum 1-3/4˝ aluminum transom. The single lever arm and roller assembly provide smooth, quiet door control and the choice of finishes and track functions meet virtually all architectural requirements.

| Certifications | Grade 1 - ANSI A156.4, UL 10 C, ADA, 100 Hour |
| --- | --- |
|  | Salt Spray, Meets BAA - Buy American Act |
| Body Construction | n | Cast Iron Body |
|  | n | Full Complement Bearing |
|  | n | 1 1/8˝ Diameter Piston |
|  | n | 11/16˝ Diameter Double Heat Treated |
|  |  | Pinion Journal |
| Fluid | All Weather Fluid |
| Handing | Handed |
| Size | Sized 1-5 |
| Warranty | 15 years |

| Fasteners | Wood and Machine Screw Pack |
| --- | --- |
| Mounting | Concealed (in tube); aluminum frame |
|  | requires minimum 1-3/4˝ (44 mm) x |
|  | 4˝ (102) mm) tube |
| Arms | Standard arm and track |
| Finishes/Colors/ | n | Aluminum (689) |
| Powder Coat | n | Statuary Bronze (690) |
|  | n | Light Bronze (691) |
|  | n | Black (693) |
|  | n | Dark Bronze (695) |
|  | n | Brass (696) |
|  | n | Custom colors optional |
|  | n | Optional SRI primer - powder coat only |
|  | n | Optional plated finishes |

Special	Customized installation templates or products may be available to solve unusual applications.

Templates	Contact LCN Product Support for assistance.

|  |  |  |  | CONCEALED |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | MOUNTING | FINISH | CYLINDER |  | ARM | *ARM FUNCTION |
|  | -3/4˝ | TUBE | COAT |  |  | ACTION |  |  | (SINGLE) |
|  |  |  | DOOR |  |  |  |  |  |  | -OPEN |
| IN | FRAME 1 | IN |  | POWDERPLATED | HANDEDSIZED | DELAYED |  | EXPOSED | STANDARD | HOLD |
|  | IN |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  | 180° | 110° |

| AVAILABLE | Closer available with less than 5.0 lbs. opening force on 36˝ door. |  |
| --- | --- | --- |
| NOT AVAILABLE | * Maximum opening/hold-open point with standard template. See individual closer series for degrees of opening per |  |
|  | installation. |  |
|  |  | D7 |
|  | LCN Door Control Catalog |  |

phone: 877-671-7011	n	fax: 800-248-1460	n	www.allegion.com/us	n	009426	rev. 11/16

2030

Series

Mounting details

Concealed

Mounting

| 5-13/16" |  | 21-7/8" |  |  |  |
| --- | --- | --- | --- | --- | --- |
| 148 mm |  | 556 mm | 1-5/8" |  |
|  |  |  |  | 41 mm |  |

|  | 10" | 1-1/16" | 1-3/8" |
| --- | --- | --- | --- |
|  | 254 mm | 27 mm | 35 mm |
|  |  | 22-1/2" |  |
| 1-1/4" | 1" | 572 mm |  |
| 32 mm |  |  |  |
|  | 25 mm |  |  |
| 3-23/32" |  |  |  |
| 94 mm |  |  |  |

9/64"

4 mm

| Butt Hinges | Should not exceed 5˝ (127 mm) in width |
| --- | --- |
| Auxiliary Stop | n | Recommended where a door cannot swing 180° |
|  | n | Optional track bumper assembly assists backcheck in cushioning the opening swing of the door (not intended to |
|  |  | replace an auxiliary stop). |
| Top Rail | n | 1-3/8˝ (35 mm) mortise required |
|  | n | With Fire Shield, 1-13/32˝ (36 mm) mortise required |
|  | n | 5/16˝ (8 mm) cutout required at top of the door, stop face only |
| Door Thickness | 1-3/4˝ (44 mm) minimum |
| Hollow Metal Frame | Consult factory for installation instructions |
| Wood Frame | Installation simplified by WOOD MOUNTING CLIP SET 2030-416 for center pivoted or 2030-417 for offset pivoted and |
|  | butt hung installations. Consult factory for preparation details. |
| Maximum opening | n | Butt hinge template allows 180°, trim permitting |
|  | n | Limited to 110° when optional bumper is installed |
|  | n | Adjustable hold-open points from 85° to 110°, with hold-open track |
|  | n | Consult factory if door will be held open at 180° |
|  | n | Offset pivot template allows 115°, trim permitting. Limited to 95° when optional bumper is installed |
|  | n | Hold-open point from 85°, with hold-open track |
|  | n | Center pivot template allows 120°, trim permitting |
|  | n | Limited to 100° when optional bumper is installed |
|  | n | Adjustable hold-open points from 85° to 100°, with hold-open track |

Notes:

- For interior or exterior doors

- Single acting cylinder in head frame

- Concealed arm and track in door top rail

D8

LCN Door Control Catalog

phone: 877-671-7011

n	fax: 800-248-1460

n	www.allegion.com/us

n	009426	rev. 11/16

2030

Series

Accessories

Cylinders	Arm

| 2031(2)(3)(4)(5)-3071 | 2030-3077T |
| --- | --- |
| Cast Iron Cylinder Assembly | Standard Arm |
| n | Handed | n | Handed |
| n | With mounting plate | n | Track roller not included with arm |

- Standard

TracksCylinders

2030-3038

Standard Track

- Non-handed

- Non hold-open

- Will accept hold-open clip and/or bumper assembly

- Standard

| 2030-3038B | 2030-3038H | 2030-3038HB |
| --- | --- | --- |
| Standard Track with Bumper | Hold-Open Track | Hold-Open Track with Bumper |
| n | Non-handed | n | Non-handed | n | Non-handed |
| n | Non hold-open | n | Will accept bumper assembly | n | Optional |
| n | Will accept hold-open clip | n | Optional |  |  |

- Optional

| LCN Door Control Catalog | D9 |
| --- | --- |
| phone: 877-671-7011 n fax: 800-248-1460 n www.allegion.com/us n 009426 | rev. 11/16 |

2030

Series

Accessories

Installation Accessories

2030-420

Fire Shield

- 22 gauge steel liner mounts in the track mortise of the door’s top rail for 20 minute labeled wood doors

2030-3054

Hold-Open Clip

- Mounts in track to provide hold-open function

- Hold-open point controlled by clip location

- Requires 2030-3034H Hold-Open Track Roller

2030-416

Wood Mounting Clip Set

- Simplifies mounting center pivoted 2030 closer in wood frame

- Includes latch stile clip, hinge stile clip, and cover

- For use with Ives Series center pivots

- Consult factory for special template

2030-3034

Track Roller

- Quiet, low friction roller assembly

- Shoulder dimension “X” = 1/16˝ (2mm)

2030-417

Wood Mounting Clip Set

- Simplifies mounting offset pivoted or butt hung 2030 closer in wood frame

- Includes two clips

- For use with offset pivots

- Consult factory for special template

2030-3034H Hold-Open Track Roller

- Quiet, low friction roller assembly

- Shoulder dimension “X” = 1/16˝ (2mm)

2030-169

Track Bumper

- Mounts in track to assist backcheck. Limits maximum opening.

- Consists of bumper, bumper post, and mounting screw

NOTE: Track bumper does not replace auxiliary stop

D10	LCN Door Control Catalog

phone: 877-671-7011	n	fax: 800-248-1460	n	www.allegion.com/us	n	009426	rev. 11/16

| How-to-order 2030 Series closers |  |  |  |
| --- | --- | --- | --- |
|  |  | Closer will be shipped with: |  |
| Select cylinder size | Specify finish | - Standard cylinder with mounting plate |  |
| 2031 | Standard Powder Coat __________ | - Standard arm |  |
| 2032 | Aluminum, Dark Bronze, Statuary, | - Standard track |  |
| 2033 | Light Bronze, Black, Brass | - Wood and machine screw pack |  |
| 2034 |  |  | unless options listed below are selected. |  |
| 2035 |  |  |  |  |

Select hand

RH

LH

2030

Series

Ordering Information

| Closer options |  |
| --- | --- |
| Tracks | Installation accessories |
| Standard with Bumper (BUMPER) | Fire Shield, 2030-420 |
| Hold-open (H) | Wood Clip Set, 2030-416 |
| Hold-open with Bumper (HBUMPER) | Wood Clip Set, 2030-417 |
| Finishes |  |
| Custom Powder Coat (RAL)_____________ |  |
| Plated Finish, US ______________ |  |
| SRI primer (use with powder coat finishes only) |  |

| Screw pack | Special template |
| --- | --- |
| TORX Machine Screw (TORX) | ST- ________ |

Table of sizes

- Select closer based on width of door.

- 2030 Series cylinders available in size 1, 2, 3, 4, or 5.

- Closing power of all 2030 Series closers may be increased 35%.

- Specify next higher size closer where strong drafts exist

Exterior (and Vestibule) door width

| 28˝ | 30˝ | 36˝ | 42˝ |
| --- | --- | --- | --- |
| 711mm | 762mm | 914mm | 1067mm |
| 2033 | size 3 | size 4 | size 5 |
| 2034 |  |  |  |
| 2035 |  |  |  |

Minimum door width

Interior door width

| 28˝ | 34˝ | 38˝ |  | 48˝ | 54˝ |
| --- | --- | --- | --- | --- | --- |
| 711mm | 864mm | 965mm |  | 1219mm | 1372mm |
| size 2 | size 3 |  | size 4 | size 5 |  |
| 2032 |  |  |  |  |  |
| 2033 |  |  |  |  |  |
| 2034 |  |  |  |  |  |
| 2035 |  |  |  |  |  |

Minimum door width

Indicates recommended range of door width for closer size.

Reduced opening force 2030 Series closers

CAUTION ! Any manual door closer, including those certified by BHMA to conform to ANSI Standard A156.4, that is selected, installed and adjusted based on ADA or other reduced opening force requirements may not provide sufficient power to reliably close and latch a door.

Refer to POWER OPERATORS section for information on systems that meet reduced opening force requirements without affecting closing power.

* Maximum opening force.

| DOOR WIDTH | 36˝ | 42˝ | 48˝ |
| --- | --- | --- | --- |
| 8.5* lbs. | 2033 | 2033 | 2034 |
| 5.0* lbs. | 2031 | 2032 | 2032 |

| LCN Door Control Catalog | D11 |
| --- | --- |
| phone: 877-671-7011 n fax: 800-248-1460 n www.allegion.com/us n 009426 | rev. 11/16 |

Notes

__________________________________________________________________________________________________________________________________________________________________________________

__________________________________________________________________________________________________________________________________________________________________________________

__________________________________________________________________________________________________________________________________________________________________________________

__________________________________________________________________________________________________________________________________________________________________________________

__________________________________________________________________________________________________________________________________________________________________________________

__________________________________________________________________________________________________________________________________________________________________________________

__________________________________________________________________________________________________________________________________________________________________________________

__________________________________________________________________________________________________________________________________________________________________________________

__________________________________________________________________________________________________________________________________________________________________________________

__________________________________________________________________________________________________________________________________________________________________________________

__________________________________________________________________________________________________________________________________________________________________________________

__________________________________________________________________________________________________________________________________________________________________________________

__________________________________________________________________________________________________________________________________________________________________________________

__________________________________________________________________________________________________________________________________________________________________________________

__________________________________________________________________________________________________________________________________________________________________________________

__________________________________________________________________________________________________________________________________________________________________________________

__________________________________________________________________________________________________________________________________________________________________________________

__________________________________________________________________________________________________________________________________________________________________________________

__________________________________________________________________________________________________________________________________________________________________________________

__________________________________________________________________________________________________________________________________________________________________________________

__________________________________________________________________________________________________________________________________________________________________________________

__________________________________________________________________________________________________________________________________________________________________________________

__________________________________________________________________________________________________________________________________________________________________________________

__________________________________________________________________________________________________________________________________________________________________________________

__________________________________________________________________________________________________________________________________________________________________________________

__________________________________________________________________________________________________________________________________________________________________________________

D12

LCN Door Control Catalog

phone: 877-671-7011

n	fax: 800-248-1460

n	www.allegion.com/us

n	009426	rev. 11/16

3030

Series

Features

The concealed 3030 Series is designed to mount in a 1-3/4˝ interior door. The double lever arm provides superior door control and the choice of finishes and arm functions meet virtually all architectural requirements.

| Certifications | Grade 1 - ANSI A156.4, UL 10 C, ADA, 100 Hour |
| --- | --- |
|  | Salt Spray, Meets BAA - Buy American Act |
| Body Construction | n | Cast Iron Body |
|  | n | Full Complement Bearing |
|  | n | 1 -1/8˝ Diameter Piston |
|  | n | 1/2˝ Diameter Double Heat Treated |
|  |  | Pinion Journal |
| Fluid | All Weather Fluid |
| Handing | Handed |
| Size | Sized 1-4 |
| Warranty | 15 years |

| Fasteners | Wood Screws and Torx Security Screws |
| --- | --- |
|  | (optional) |
| Mounting | Concealed (in door); consult factory for |
|  | installations with pivots |
| Arms | Regular arm |
| Finishes/Colors/ | n | Aluminum (689) |
| Powder Coat | n | Statuary Bronze (690) |
|  | n | Light Bronze (691) |
|  | n | Black (693) |
|  | n | Dark Bronze (695) |
|  | n | Brass (696) |
|  | n | Custom colors optional |
|  | n | Optional SRI primer - powder coat only |
|  | n | Optional plated finishes |

Special	Customized installation templates or products may be available to solve unusual applications.

Templates	Contact LCN Product Support for assistance.

CONCEALED

MOUNTING	FINISH	CYLINDER	ARM	*ARM FUNCTION

|  |  |  | TUBE | COAT |  |  | ACTION |  |  | (SINGLE) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| IN | -3/4˝ |  | DOOR | POWDER PLATED | HANDEDSIZED | DELAYED |  | EXPOSED | STANDARD | -OPEN |
|  | IN | IN |  |  |  |  |  |  |  | HOLD |
|  | FRAME 1 |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  | 180° | 140° |

| AVAILABLE | Closer available with less than 5.0 lbs. opening force on 36˝ door. |  |
| --- | --- | --- |
| NOT AVAILABLE | * Maximum opening/hold-open point with standard template. See individual closer series for |  |
|  | degrees of opening per installation. |  |
|  |  | D13 |
|  | LCN Door Control Catalog |  |

phone: 877-671-7011	n	fax: 800-248-1460	n	www.allegion.com/us	n	009426	rev. 11/16

3030

Series

Mounting details

Concealed

Mounting

A

|  |  | B | 2-11/16" | 3/4" | 15/16" |  |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  | 68 mm |  | 24 mm |  |
|  |  |  |  | 19 mm |  |  |
|  | 1-3/8" | 3" |  |  |  |  |
|  |  | 76 mm |  |  |  |  |
|  | 35 mm |  |  |  |  |  |
| 8-3/4" |  | 5/16" | 3-3/4" |  |  |  |
| 222 mm |  | 8 mm | 95 mm |  |  |  |
| 11-3/4" |  | 4-7/8" |  |  | 2-15/16" |  |
| 298 mm |  | 124 mm | 1-1/4" dia. |  |  | 3-3/16" |
|  |  |  | 32 mm | 9/16" | 75 mm | 81 mm |
|  |  | 1-1/2" | 8-3/4" | 14 mm |  |  |
|  |  | 38 mm | 222 mm |  |  |  |

C

| Butt Hinges | Should not exceed 5˝ (127 mm) in width |
| --- | --- |
| Auxiliary Stop | Recommended at hold-open point or where a door cannot swing 180° |
| Top Rail | Minimum 4˝ (102 mm) required |
| Door Thickness | n | 1-3/4˝ (44 mm) minimum |
|  | n | Please consult the door manufacturer to assure that the door integrity and warranty is maintained after installing |
|  |  | the 3030 Series door closer in a 1-3/4˝ thick wood door |
| Maximum opening | Can be templated for |
|  | 100°: | A = 3-5/8˝ (92 mm) |
|  |  |  | B = 10-1/4˝ (260 mm) |
|  | 130°: | A = 2-5/8˝ (67 mm) |
|  |  |  | B = 9-1/4˝ (235 mm) |
|  | 180°: | A = 1-5/8˝ (41 mm) |
|  |  |  | B = 8-1/4˝ (210 mm) |

- Hold-open points up to maximum opening or 140°, whichever is less, with hold-open arm.

Arm clearance above door

C = 1-1/4˝ (32 mm) minimum

Notes:

- For interior or exterior doors

- Single acting cylinder in top rail of door

- Exposed arm on hinge side of door

D14	LCN Door Control Catalog

phone: 877-671-7011	n	fax: 800-248-1460	n	www.allegion.com/us	n	009426	rev. 11/16

3030

Series

Accessories

Cylinder	Arms

| 3031(2)(3)(4)-3071 | 3030-3077 | 3030-3049 |
| --- | --- | --- |
| Cast Iron Cylinder Assembly | Regular arm | Hold-open arm |
| n | Handed | n Non-handed | n | Handed |
| n | With mounting plate |  | n | Provides hold-open function, |
| n | Standard |  |  | adjustable at elbow |
|  |  |  | n | Optional |

| LCN Door Control Catalog | D15 |
| --- | --- |
| phone: 877-671-7011 n fax: 800-248-1460 n www.allegion.com/us n 009426 | rev. 11/16 |

3030

Series

Ordering Information

| How-to-order 3030 Series closers |  |  |  |
| --- | --- | --- | --- |
|  |  | Closer will be shipped with: |  |
| Select cylinder size | - Standard cylinder with mounting bracket |  |
| 3031 |  | - Regular arm |  |
| 3032 |  | - Wood and machine screw pack |  |
| 3033 |  | unless options listed below are selected. |  |
| 3034 |  |  |  |
| Select hand |  |  |
| RH |  |  |
| LH |  |  |

Specify finish

Standard Powder Coat __________

Aluminum, Dark Bronze, Statuary, Light Bronze, Black, Brass.

| Closer options |  | Screw pack |
| --- | --- | --- |
| Arm |  |  |
| Hold-open (H) |  | TORX Machine Screw (TORX) |
| Finishes |  |  |
| Custom Powder Coat (RAL)___________ |  | Special template |
| Plated Finish, US ______________ |  | ST- ________ |
| SRI primer (use with powder coat finishes only) |  |  |

Table of sizes

- Select closer based on width of door

- 3030 Series cylinders available in size 1, 2, 3, or 4

- Closing power of all 3030 Series closers may be increased 15%

Interior door width

| 24˝ | 34˝ | 38˝ | 48˝ |
| --- | --- | --- | --- |
| 610mm | 864mm | 965mm | 1219mm |
| 3032 | size 2 | size 3 | size 4 |
| 3033 |  |  |  |
| 3034 |  |  |  |

Minimum door width

Indicates recommended range of door width for closer size.

Reduced opening force 3030 Series closers

CAUTION ! Any manual door closer, including those certified by BHMA to conform to ANSI Standard A156.4, that is selected, installed and adjusted based on ADA or other reduced opening force requirements may not provide sufficient power to reliably close and latch a door.

Refer to POWER OPERATORS section for information on systems that meet reduced opening force requirements without affecting closing power.

* Maximum opening force.

| DOOR WIDTH | 36˝ | 42˝ | 48˝ |
| --- | --- | --- | --- |
| 8.5* lbs. | N/A | N/A | N/A |
| 5.0* lbs. | 3031 | 3031 | 3032 |

D16	LCN Door Control Catalog

phone: 877-671-7011	n	fax: 800-248-1460	n	www.allegion.com/us	n	009426	rev. 11/16

3130

Series

Features

The concealed 3130 Series is designed to mount in a 1-3/4˝ interior door. The single lever arm and roller assembly provides complete concealment and the choice of finishes and track functions meet virtually all architectural requirements.

| Certifications | Grade 1 - ANSI A156.4, UL 10 C, ADA, 100 Hour |
| --- | --- |
|  | Salt Spray, Meets BAA - Buy American Act |
| Body Construction | n | Cast Iron Body |
|  | n | Full Complement Bearing |
|  | n | 1-1/8˝ Diameter Piston |
|  | n | 1/2˝ Diameter Double Heat Treated |
|  |  | Pinion Journal |
| Fluid | All Weather Fluid |
| Handing | Handed |
| Size | Sized 1-3 |
| Warranty | 15 years |

| Fasteners | Wood Screws and Torx Security Screws |
| --- | --- |
|  | (optional) |
| Mounting | Concealed (in door); consult factory for |
|  | installation with pivots |
| Arms | Standard arm and track |
| Finishes/Colors/ | n | Aluminum (689) |
| Powder Coat | n | Statuary Bronze (690) |
|  | n | Light Bronze (691) |
|  | n | Black (693) |
|  | n | Dark Bronze (695) |
|  | n | Brass (696) |
|  | n | Custom colors optional |
|  | n | Optional SRI primer - powder coat only |
|  | n | Optional plated finishes |

Special	Customized installation templates or products may be available to solve unusual applications.

Templates	Contact LCN Product Support for assistance.

CONCEALED

MOUNTING	FINISH	CYLINDER	ARM	*ARM FUNCTION

|  |  |  | TUBE | COAT |  |  | ACTION |  |  | (SINGLE) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| IN | -3/4˝ |  | DOOR | POWDER PLATED | HANDEDSIZED | DELAYED |  | EXPOSED | STANDARD | -OPEN |
|  | IN | IN |  |  |  |  |  |  |  | HOLD |
|  | FRAME 1 |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  | 140° | 100° |

| AVAILABLE | Closer available with less than 5.0 lbs. opening force on 36˝ door. |  |
| --- | --- | --- |
| NOT AVAILABLE | * Maximum opening/hold-open point with standard template. See individual closer series for |  |
|  | degrees of opening per installation. |  |
|  |  | D17 |
|  | LCN Door Control Catalog |  |

phone: 877-671-7011	n	fax: 800-248-1460	n	www.allegion.com/us	n	009426	rev. 11/16

3130

Series

Mounting details

Concealed

Mounting

11-3/4"

298 mm

| 1-3/8" | 1-1/4" |
| --- | --- |
| 35 mm | 32 mm |

|  |  |  | 2" | 1-1/16" |
| --- | --- | --- | --- | --- |
|  |  |  | 50 mm | 22-1/2" | 27 mm |
|  |  |  |  | 572 mm |

| 3/8" |  |  |  |  |
| --- | --- | --- | --- | --- |
| 10 mm |  |  |  |  |
| 4-7/8" | 1-1/4" dia. | 5/8" |  | 3-1/4" |
| 124 mm |  |  |  |  |
| 1-1/2" | 32 mm | 16 mm | 3" | 83 mm |
|  | 8-3/4" |  |  |  |
| 38 mm |  |  | 76 mm |  |
|  | 222 mm |  |  |  |
| 4-3/8" |  |  |  |  |
| 110 mm |  |  |  |  |

| Butt Hinges | Should not exceed 5˝ (127 mm) in width |
| --- | --- |
| Auxiliary Stop | n | Recommended at hold-open point or where a door cannot swing 140° |
|  | n | Optional track bumper assembly assists backcheck in cushioning the opening swing of the door. It is not intended to |
|  |  | replace an auxiliary stop |
| Top Rail | Minimum 4˝ (102 mm) required |
| Door Thickness | n | 1-3/4˝ (44 mm) minimum. |
|  | n | Please consult the door manufacturer to assure that the door integrity and warranty is maintained after installing |
|  |  | the 3130 Series door closer in a 1-3/4˝ thick wood door |
| Door Width | 2´2˝ (660 mm) minimum |
| Maximum opening | n | Templating allows 140°, trim permitting. 100° with optional bumper installed |
|  | n | Adjustable hold-open points from 85° to 100°, with hold-open track |

Notes:

- For interior doors

- Single acting cylinder and standard arm in top rail of door

- Concealed track in head frame

- Consult factory for installations with pivots.

D18	LCN Door Control Catalog

phone: 877-671-7011	n	fax: 800-248-1460	n	www.allegion.com/us	n	009426	rev. 11/16

3130

Series

Accessories

Cylinder	Arm

| 3131(2)(3)-3071 | 3130-3077T |
| --- | --- |
| Cast Iron Cylinder Assembly | Standard Arm |
| n | Handed | n | Handed |
| n | With mounting plate | n | Track roller not included with arm |
| n | Standard | n | Standard |

Tracks

3130-3038

Track

- Non-handed

- Non hold-open

- Will accept hold-open clip and/ or bumper assembly

- Standard

| 3130-3038B | 3130-3038H | 3130-3038HB |
| --- | --- | --- |
| Standard Track with Bumper | Hold-Open track | Hold-Open Track with Bumper |
| n | Non-handed | n | Non-handed | n | Non-handed |
| n | Non hold-open | n | Will accept bumper assembly | n | Optional |
| n | Will accept hold-open clip | n | Optional |  |  |

- Optional

Installation Accessories

| 3130-169 | 3130-3054 | 3130-3034 |
| --- | --- | --- |
| Track Bumper | Hold-Open Clip | Track Roller |
| n | Mounts in track to assist | n | Mounts in track to provide hold- | n | Quiet, low friction roller |
|  | backcheck, does not replace |  | open function |  | assembly |
|  | auxiliary stop | n | Hold-open point controlled by | n | Shoulder dimension “X” = |
| n | Limits maximum opening |  | clip location |  | 1/8˝ (3mm) |
| n | Consists of bumper, bumper | n | Requires 3130-3034H Hold- |  |  |
|  | post, and mounting screw |  | Open Track Roller |  |  |

3130-3034H

Hold-Open Track Roller

- Quiet, low friction roller assembly

- Shoulder dimension “X” = 1/8˝ (3mm)

| LCN Door Control Catalog | D19 |
| --- | --- |
| phone: 877-671-7011 n fax: 800-248-1460 n www.allegion.com/us n 009426 | rev. 11/16 |

3130

Series

Ordering Information

| How-to-order 3130 Series closers | Closer will be shipped with: |
| --- | --- |
| Select cylinder size | - Standard cylinder with mounting bracket |
| 3131 | - Standard arm wtih finish plate |
| 3132 | - Standard track |
| 3133 | - Wood and machine screw pack |

| Select hand | unless options listed below are selected. |
| --- | --- |
| RH |  |
| LH |  |

Specify finish

Standard Powder Coat __________

Aluminum, Dark Bronze, Statuary, Light Bronze, Black, Brass.

| Closer options |  |
| --- | --- |
| Track | Screw pack |
| Standard with Bumper (BUMPER) | TORX Machine Screw (TORX) |
| Hold-open (H) |  |
| Hold-open with Bumper (HBUMPER) |  |
|  | Special template |
| Finishes | ST- ________ |
| Custom Powder Coat (RAL)___________ |  |
| Plated Finish, US ______________ |  |
| SRI primer (use with powder coat finishes only) |  |

Table of sizes

- Select closer based on width of door.

- 3130 Series cylinders available in size 1, 2, or 3.

- Closing power of 3130 Series closers is not adjustable

Interior door width

| 26˝ | 34˝ | 38˝ |
| --- | --- | --- |
| 660mm | 864mm | 965mm |
| 3132 | size 2 | size 3 |
| 3133 |  |  |

Minimum door width

Indicates recommended range of door width for closer size.

Reduced opening force 3130 Series closers

CAUTION ! Any manual door closer, including those certified by BHMA to conform to ANSI Standard A156.4, that is selected, installed and adjusted based on ADA or other reduced opening force requirements may not provide sufficient power to reliably close and latch a door.

Refer to POWER OPERATORS section for information on systems that meet reduced opening force requirements without affecting closing power.

* Maximum opening force.

| DOOR WIDTH | 36˝ | 42˝ | 48˝ |
| --- | --- | --- | --- |
| 8.5* lbs. | N/A | N/A | N/A |
| 5.0* lbs. | 3131 | 3131 | 3132 |

D20	LCN Door Control Catalog

phone: 877-671-7011	n	fax: 800-248-1460	n	www.allegion.com/us	n	009426	rev. 11/16

5010

Series

Features

The concealed 5010 Series is a heavy duty closer designed for institutional, high traffic, or other applications exposed to weather or abuse. The double lever arm provides superior door control and a choice of finishes, cylinder functions, and arm functions that meet virtually all architectural requirements.

| Certifications | Grade 1 - ANSI A156.4, UL 10 C, ADA, 100 Hour |
| --- | --- |
|  | Salt Spray, Meets BAA - Buy American Act |
| Body Construction | n | Cast Iron Body |
|  | n | Full Complement Bearing |
|  | n | 1-1/8˝ Diameter Piston |
|  | n | 11/16˝ Diameter Double Heat Treated |
|  |  | Pinion Journal |
| Fluid | All Weather Fluid |
| Handing | Handed |
| Size | Sized 1-6 |
| Warranty | 15 years |

| Fasteners | Wood Screws and Torx Security Screws |
| --- | --- |
|  | (optional) |
| Mounting | Concealed (in frame); aluminum frame |
|  | requires 4˝ (102 mm) x 4˝ tube |
| Arms | Regular Arm |
| Finishes/Colors/ | n | Aluminum (689) |
| Powder Coat | n | Statuary Bronze (690) |
|  | n | Light Bronze (691) |
|  | n | Black (693) |
|  | n | Dark Bronze (695) |
|  | n | Brass (696) |
|  | n | Custom colors optional |
|  | n | Optional SRI primer - powder coat only |
|  | n | Optional plated finishes |

Special	Customized installation templates or products may be available to solve unusual applications.

Templates	Contact LCN Product Support for assistance.

CONCEALED

MOUNTING	FINISH	CYLINDER	ARM	*ARM FUNCTION

|  |  |  | TUBE | COAT |  |  | ACTION |  |  | (SINGLE) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| IN | -3/4˝ |  | DOOR | POWDER PLATED | HANDEDSIZED | DELAYED |  | EXPOSED | STANDARD | -OPEN |
|  | IN | IN |  |  |  |  |  |  |  | HOLD |
|  | FRAME 1 |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  | 180° | 100° |

| AVAILABLE | Closer available with less than 5.0 lbs. opening force on 36˝ door. |  |
| --- | --- | --- |
| NOT AVAILABLE | * Maximum opening/hold-open point with standard template. See individual closer series for |  |
|  | degrees of opening per installation. |  |
|  |  | D21 |
|  | LCN Door Control Catalog |  |

phone: 877-671-7011	n	fax: 800-248-1460	n	www.allegion.com/us	n	009426	rev. 11/16

5010

Series

Mounting details

Concealed

Mounting

7/8"

22 mm

| 14" |  |  | 3-5/8" |
| --- | --- | --- | --- |
| 356 mm |  |  |  |
|  |  |  | 92 mm |
| 2-1/16" |  | 3/8" |  |
|  |  | 10 mm |
| 52 mm |  |  |
| 11-1/2" |  |  |  |
| 292 mm |  |  |  |
| A | 2-11/16" | 3/4" | 2-1/8" |
| B | 68 mm | 19 mm | 54 mm |
| 3/4" |  |  |  |
| 19 mm |  |  |  |
| 2" MAX |  |  |  |
| 51 mm |  |  |  |

| Butt Hinges | Should not exceed 6˝ (152 mm) in width |
| --- | --- |
| Auxiliary Stop | Recommended at hold-open point or where a door cannot swing 180° |
| Top Rail | Minimum 2-1/8˝ (54 mm) required |
| Delay Action | n | Add suffix “DEL” to selected cylinder (eg. 5014 DEL) (not available with 5016 cylinder) |
|  | n | Delays closing from maximum opening to approximately 70° |
|  | n | Delay time adjustable up to approximately 1 minute |
| Maximum opening | Butt hung doors can be templated for |
|  | 100°: | A = 10-3/16˝ (259 mm) |
|  |  |  | B = 12˝ (305 mm) |
|  | 180°: | A = 5-1/2˝ (140 mm) |
|  |  |  | B = 7-5/16˝ (186 mm) trim permitting |
|  | n | Hold-open points up to 100° only with hold-open arm |
|  | n | Center pivot mounting restricts opening to 140° |
|  | n | Offset pivot mounting allows up to 180°, trim permitting |

Notes:

- For interior or exterior doors

- Single acting cylinder in head frame

- Exposed arm on hinge side of door

D22

LCN Door Control Catalog

phone: 877-671-7011

n	fax: 800-248-1460

n	www.allegion.com/us

n	009426	rev. 11/16

5010

Series

Accessories

Cylinder	Arms

| 5011(2)(3)(4)(5)(6)-3071 | 5010-3077 | 5010-3049 |
| --- | --- | --- |
| Cast Iron Cylinder Assembly | Regular Arm | Hold-Open Arm |
| n | Handed | n Non-handed | n | Handed |
| n | With mounting plate |  | n | Provides hold-open function for |
| n | Standard |  |  | 100° Template, adjustment at |
|  |  |  |  | elbow |
|  |  |  | n | Optional |

| LCN Door Control Catalog | D23 |
| --- | --- |
| phone: 877-671-7011 n fax: 800-248-1460 n www.allegion.com/us n 009426 | rev. 11/16 |

5010

Series

| Ordering information |  |  |  |  |
| --- | --- | --- | --- | --- |
|  | How-to-order 5010 Series closers |  |  |  |
|  |  |  | Closer will be shipped with: |  |
|  | Select cylinder size | - Standard cylinder with finish plate |  |
|  | 5011 |  | - Standard arm |  |
|  | 5012 |  | - Regular arm |  |
|  | 5013 |  | - Wood and machine screw pack |  |
|  | 5014 |  | unless options listed below are selected. |  |
|  | 5015 |  |  |  |

5016 (DEL not available)

| Select hand | Specify finish |
| --- | --- |
| RH | Standard Powder Coat __________ |
| LH | Aluminum, Dark Bronze, Statuary, Light Bronze, Black, Brass |

| Closer options |  |
| --- | --- |
| Cylinder function | Screw pack |
| Delayed Action (DEL) | TORX Machine Screw (TORX) |
| Arm |  |
| Hold-Open (H) | Special template |
| Finishes | ST- ________ |
| Custom Powder Coat (RAL)_____________ |  |
| Plated Finish, US ______________ |  |

SRI primer (use with powder coat finishes only)

Table of sizes

- Select closer based on width of door

- Series cylinders available in size 1, 2, 3, 4, 5, or 6

- Closing power of all 5010 Series closers may be increased 50%

- Specify next higher size closer where strong drafts exist

- Delayed action not available with 5016 cylinder

Exterior (and Vestibule) door width	Interior door width

| 24˝ | 30˝ | 36˝ |  | 42˝ | 48˝ | 24˝ | 34˝ | 38˝ | 48˝ | 54˝ | 60˝ |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 610mm | 762mm | 914mm | 1067mm | 1219mm | 610mm | 864mm | 965mm | 1219mm | 1372mm | 1524mm |
|  | size 3 | size 4 | size 5 | size 6 |  | size 2 | size 3 | size 4 | size 5 | size 6 |  |
| 5013 |  |  |  |  |  | 5012 |  |  |  |  |  |
| 5014 |  |  |  |  |  | 5013 |  |  |  |  |  |
| 5015 |  |  |  |  |  | 5014 |  |  |  |  |  |
| 5016 |  |  |  |  |  | 5015 |  |  |  |  |  |
| Minimum door width |  |  |  |  | 5016 |  |  |  |  |  |
|  |  |  |  |  |  | Minimum door width |  |  |  |  |

Indicates recommended range of door width for closer size.

Reduced opening force 5010 Series closers

CAUTION ! Any manual door closer, including those certified by BHMA to conform to ANSI Standard A156.4, that is selected, installed and adjusted based on ADA or other reduced opening force requirements may not provide sufficient power to reliably close and latch a door.

Refer to POWER OPERATORS section for information on systems that meet reduced opening force requirements without affecting closing power.

* Maximum opening force.

| DOOR WIDTH | 36˝ | 42˝ | 48˝ |
| --- | --- | --- | --- |
| 8.5* lbs. | 5012 | 5013 | 5013 |
| 5.0* lbs. | 5011 | 5011 | 5012 |

D24	LCN Door Control Catalog

phone: 877-671-7011	n	fax: 800-248-1460	n	www.allegion.com/us	n	009426	rev. 11/16

5030

Series

Features

The concealed 5030 Series PACER® is a heavy duty closer designed to fit in a narrow, minimum 1-3/4˝ aluminum transom. The double lever arm provides superior door control and the choice of finishes and arm functions meet virtually all architectural requirements.

| Certifications | Grade 1 - ANSI A156.4, UL 10 C, ADA, 100 Hour |
| --- | --- |
|  | Salt Spray, Meets BAA - Buy American Act |
| Body Construction | n | Cast Iron Body |
|  | n | Full Complement Bearing |
|  | n | 1-1/8˝ Diameter Piston |
|  | n | 11/16˝ Diameter Double Heat Treated |
|  |  | Pinion Journal |
| Fluid | All Weather Fluid |
| Handing | Handed |
| Size | Sized 1; 3-6 |
| Warranty | 15 years |

| Fasteners | Wood Screws and Torx Security Screws |
| --- | --- |
|  | (optional) |
| Mounting | Concealed (in tube); aluminum frame |
|  | requires minimum 1-3/4˝ (44 mm) x |
|  | 4-1/2˝ (114 mm) tube |
| Arms | Regular Arm |
| Finishes/Colors/ | n | Aluminum (689) |
| Powder Coat | n | Statuary Bronze (690) |
|  | n | Light Bronze (691) |
|  | n | Black (693) |
|  | n | Dark Bronze (695) |
|  | n | Brass (696) |
|  | n | Custom colors optional |
|  | n | Optional SRI primer - powder coat only |
|  | n | Optional plated finishes |

Special	Customized installation templates or products may be available to solve unusual applications.

Templates	Contact LCN Product Support for assistance.

CONCEALED

MOUNTING	FINISH	CYLINDER	ARM	*ARM FUNCTION

|  | -3/4˝ | TUBE | COAT |  |  | ACTION |  |  | (SINGLE) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| IN |  |  | DOOR | POWDERPLATED | HANDEDSIZED | DELAYED |  | EXPOSED | STANDARD | -OPEN |
|  | IN | IN |  |  |  |  |  |  |  | HOLD |
|  | FRAME 1 |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  | 180° | 100° |

| AVAILABLE | Closer available with less than 5.0 lbs. opening force on 36˝ door. |  |
| --- | --- | --- |
| NOT AVAILABLE | * Maximum opening/hold-open point with standard template. See individual closer series for |  |
|  | degrees of opening per installation. |  |
|  |  | D25 |
|  | LCN Door Control Catalog |  |

phone: 877-671-7011	n	fax: 800-248-1460	n	www.allegion.com/us	n	009426	rev. 11/16

5030

Series

Mounting details

Concealed

Mounting

A

|  | 1-5/8" |  | 21-7/8" |  |
| --- | --- | --- | --- | --- |
|  | 41 mm |  | 556 mm |  |
| 3-23/32" | 11-1/4" |  |  |  |
| 94 mm |  |  |  |  |
|  | 286 mm |  |  |  |
|  | B | 2-11/16" | 3/4" | 2-1/8" |
|  |  |  |  | 54 mm |
|  |  |  | 19 mm |  |
|  |  | 68 mm |  |  |

19/32" dia.

15 mm

3/4" MIN.

19 mm

| Butt Hinges | Should not exceed 6˝ (152 mm) in width |
| --- | --- |
| Auxiliary Stop | Recommended at hold-open point or where the door cannot swing 180° |
| Wood Frame | n | Installation simplified by WOOD MOUNTING CLIP SET 5030-416 for center pivoted or 5030-417 for offset pivoted |
|  |  | and butt hung installations |
|  | n | Consult factory for preparation details |
| Top Rail | Minimum 2-1/8˝ (54 mm) required |
| Door Thickness | Maximum 1-3/4˝ (44 mm), for doors thicker than 1-3/4˝ consult factory |
| Maximum opening | Butt hung doors can be templated for |
|  | 100°: | A = 5-13/16˝ (148 mm) |
|  |  |  | B = 11-13/16˝ (300 mm) |
|  | 180°: | A = 2-1/16˝ (52 mm) |
|  |  |  | B = 8-1/16˝ (205 mm) |
|  |  |  | trim permitting |

- Hold-open points up to 100° only with hold-open arm

- Center pivot mounting restricts opening to 120°. Hold-open up to 120° with hold-open arm

- Offset pivot mounting allows up to 115°, trim permitting. Hold-open up to 115° with hold-open arm

Notes:

- For interior or exterior doors

- Single acting cylinder in head frame

- Exposed arm on push side of door

D26

LCN Door Control Catalog

phone: 877-671-7011

n	fax: 800-248-1460

n	www.allegion.com/us

n	009426	rev. 11/16

Cylinder	Arms

| 5031(3)(4)(5)(6)-3071 | 5030-3077 | 5030-3049 |
| --- | --- | --- |
| Cast Iron Cylinder Assembly | Regular Arm | Hold-Open Arm |
| n | Handed | n Non-handed | n | Handed |
| n | With mounting plate |  | n | Provides hold-open function for |
| n | Standard |  |  | 100° template, adjustable at |
|  |  |  |  | elbow |
|  |  |  | n | Optional |

5030

Series

Accessories

Installation Accessories

5030-416

Wood Mounting Clip Set

- Simplifies mounting center pivoted 5030 closer in wood frame

- Includes latch stile clip, hinge stile clip, and cover.

- For use with Ives Series center pivots

- Consult factory for special template

5030-417

Wood Mounting Clip Set

- Simplifies mounting offset pivoted or butt hung 5030 closer in wood frame.

- Includes two clips.

- For use with offset pivots.

- Consult factory for special template.

LCN Door Control Catalog

phone: 877-671-7011	n	fax: 800-248-1460	n	www.allegion.com/us	n	009426	rev. 11/16

D27

5030

Series

| Ordering information |  |  |  |  |
| --- | --- | --- | --- | --- |
|  | How-to-order 5030 Series closers |  |  |  |
|  |  |  | Closer will be shipped with: |  |
|  | Select cylinder size | - Standard cylinder with mounting plate |  |
|  | 5031 |  | - Regular arm |  |
|  | 5033 |  | - Wood and machine screw pack |  |
|  | 5034 |  | unless options listed below are selected. |  |
|  | 5035 |  |  |  |
|  | 5036 |  |  |  |

| Select hand | Specify finish |
| --- | --- |
| RH | Standard Powder Coat __________ |
| LH | Aluminum, Dark Bronze, Statuary, Light Bronze, Black, Brass |

| Closer options |  |
| --- | --- |
| Arm | Installation accessories |
| Hold-Open (H) | Wood Clip Set, 5030-416 |
| Finishes | Wood Clip Set, 5030-417 |
| Custom Powder Coat (RAL)_____________ |  |
| Plated Finish, US ______________ |  |

SRI primer (use with powder coat finishes only)

| Screw pack | Special template |
| --- | --- |
| TORX Machine Screw (TORX) | ST- ________ |

Table of sizes

- Select closer based on width of door

- 5030 Series cylinders available in size 1, 2, 3, 4, 5 or 6

- Closing power of all 5030 Series closers may be increased 50%

- Specify next higher size closer where strong drafts exist

Exterior (and Vestibule) door width	Interior door width

| 28˝ | 30˝ | 36˝ |  | 42˝ | 48˝ | 28˝ | 34˝ | 38˝ | 48˝ | 54˝ | 60˝ |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 711mm | 762mm | 914mm | 1067mm | 1219mm | 711mm | 864mm | 965mm | 1219mm | 1372mm | 1524mm |
| 5033 | size 3 | size 4 | size 5 | size 6 |  | 5033 | size 3 | size 4 | size 5 | size 6 |  |
| 5034 |  |  |  |  |  | 5034 |  |  |  |  |  |
| 5035 |  |  |  |  |  | 5035 |  |  |  |  |  |
| 5036 |  |  |  |  |  | 5036 |  |  |  |  |  |
| Minimum door width |  |  |  |  | Minimum door width |  |  |  |  |

Indicates recommended range of door width for closer size.

Note: Minimum door width 28˝ (711 mm).

Reduced opening force 5030 Series closers

CAUTION ! Any manual door closer, including those certified by BHMA to conform to ANSI Standard A156.4, that is selected, installed and adjusted based on ADA or other reduced opening force requirements may not provide sufficient power to reliably close and latch a door.

Refer to POWER OPERATORS section for information on systems that meet reduced opening force requirements without affecting closing power.

* Maximum opening force.

| DOOR WIDTH | 36˝ | 42˝ | 48˝ |
| --- | --- | --- | --- |
| 8.5* lbs. | 5033 | 5033 | 5033 |
| 5.0* lbs. | 5031 | 5031 | 5033 |

D28	LCN Door Control Catalog

phone: 877-671-7011	n	fax: 800-248-1460	n	www.allegion.com/us	n	009426	rev. 11/16

6030

Series

Features

The concealed 6030 Series PACER® is a heavy duty, double acting closer designed to fit in a narrow, minimum 1-3/4˝ header. The single lever arm and roller assembly provides smooth, quiet door control and the choice of finishes and track functions meet virtually all architectural requirements. Installation at left illustrated with center pivot set (not included).

| Certifications | Grade 1 - ANSI A156.4, UL 10 C, ADA, 100 Hour |
| --- | --- |
|  | Salt Spray, Meets BAA - Buy American Act |
| Body Construction | n | Cast Iron Body |
|  | n | Full Complement Bearing |
|  | n | 1-1/8˝ Diameter Piston |
|  | n | 11/16˝ Diameter Double Heat Treated |
|  |  | Pinion Journal |
| Fluid | All Weather Fluid |
| Handing | Non-Handed |
| Size | Sized 1-5 |
| Warranty | 15 years |

| Fasteners | Wood Screws and Torx Security Screws |
| --- | --- |
|  | (optional) |
| Mounting | Concealed (in tube); double acting |
| Arms | Standard arm with track |
| Finishes/Colors/ | n | Aluminum (689) |
| Powder Coat | n | Statuary Bronze (690) |
|  | n | Light Bronze (691) |
|  | n | Black (693) |
|  | n | Dark Bronze (695) |
|  | n | Brass (696) |
|  | n | Custom colors optional |
|  | n | Optional SRI primer - powder coat only |
|  | n | Optional plated finishes |

Special	Customized installation templates or products may be available to solve unusual applications.

Templates	Contact LCN Product Support for assistance.

CONCEALED

MOUNTING	FINISH	CYLINDER	ARM	*ARM FUNCTION

|  | FRAME1 |  | TUBE | COAT |  | DELAYED | ACTION | EXPOSED |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| IN |  | IN | DOOR | POWDER PLATED | HANDED SIZED |  |  |  |
|  | IN |  |  |  |  |  |  |  |
|  | -3/4˝ |  |  |  |  |  |  |  |

STANDARD

95°

(SINGLE)	OPEN

HOLD-

95°

| AVAILABLE | Closer available with less than 5.0 lbs. opening force on 36˝ door. |  |
| --- | --- | --- |
| NOT AVAILABLE | * Maximum opening/hold-open point with standard template. See individual closer series for |  |
|  | degrees of opening per installation. |  |
|  |  | D29 |
|  | LCN Door Control Catalog |  |

phone: 877-671-7011	n	fax: 800-248-1460	n	www.allegion.com/us	n	009426	rev. 11/16

6030

Series

Mounting details

Concealed

Mounting

|  |  | 1-5/8" | 4-1/2" | 18-1/4" | 1-5/8" |
| --- | --- | --- | --- | --- | --- |
|  |  | 41 mm | 115 mm | 464 mm | 41 mm |
| 1" |  |  |  |  |  |
| 25 mm |  |  |  |  |  |
|  |  |  | 1/2" |  | 1-7/16" |
|  |  |  | 13 mm |  |  |
|  |  |  |  |  | 37 mm |
|  |  |  |  | 22-1/2" |  |
|  | of Door | 3-23/32" |  | 572 mm |  |
| 5-1/4" |  |  |  |  |  |
|  |  | 95 mm |  |  |  |
| 133 mm | 23-5/8" |
|  | 600 mm |
|  | of Pivot |
|  | 1-1/4" |
|  | 32 mm |

| Auxiliary Stop | Recommended where a door cannot swing 95° |
| --- | --- |
| Center Pivot Set | Must be used but ordered separately |
| Door Width | 30˝ (762 mm) minimum with 1-3/4˝ (44 mm) pivot centers |
| Top Rail | n | 1-7/16˝ (36 mm) mortise required |
|  | n | 3/8˝ (10 mm) cutout required at top of the door, both sides. |
| Door Thickness | 1-3/4˝ (44 mm) minimum |
| Centering Adjustment | Centering is provided by rotating the track roller to center the door in the opening. |
| Wood Frame | n | Installation simplified by WOOD MOUNTING CLIP SET, 6030-416 |
|  | n | Consult product support for special template |
| Maximum opening | n | Center pivot template allows 95° |
|  | n | Adjustable hold-open points from 85° to 95°, with hold-open track |

Notes:

- For interior or exterior doors

- Double acting cylinder in cased frame

- Concealed arm and track in door top rail

- Center pivots only

D30

LCN Door Control Catalog

phone: 877-671-7011

n	fax: 800-248-1460

n	www.allegion.com/us

n	009426	rev. 11/16

6030

Series

Accessories

Cylinder

6031(2)(3)(4)(5)-3071 Cast Iron Cylinder Assembly

- Non-handed

- With mounting plate

- Standard

Arm

6030-3077T

Standard Arm

- Non-handed

- 5/16˝ (8 mm) thick arm

- Track roller not included with arm

Tracks

| 6030-3038B | 6030-3038HB |
| --- | --- |
| Standard Track with Bumper | Hold-Open Track with Bumper |
| n | Non-handed | n | Non-handed |
| n | Non hold-open | n | Optional |

- Will accept hold-open clip

- Standard

Installation Accessories

6030-416

Wood Mounting Clip Set

- Simplifies mounting closer in wood frame

- Includes latch stile clip, hinge stile clip, and cover

- For use with Ives Series center pivots

- Consult factory for special template

6030-3034H Hold-Open Track Roller

- Hold-open roller

- Quiet, low friction roller assembly

6030-169

Track Bumper

- Mounts in track to assist backcheck

- Limits maximum opening

- Consists of bumper, bumper post, and mounting screw

NOTE: Track bumper does not replace auxiliary stop.

6030-3054

Hold-Open Clip

- Mounts in track to provide hold-open function

- Hold-open point controlled by clip location

- Requires 6030-3034H Hold-Open Track Roller

6030-3034

Track Roller

- Quiet, low friction roller assembly includes eccentric with 3/4˝ (19 mm) adjustment to center 36˝ (914 mm) door

| LCN Door Control Catalog | D31 |
| --- | --- |
| phone: 877-671-7011 n fax: 800-248-1460 n www.allegion.com/us n 009426 | rev. 11/16 |

6030

Series

| Ordering information |  |  |  |  |
| --- | --- | --- | --- | --- |
|  | How-to-order 6030 Series closers |  |  |  |
|  |  |  | Closer will be shipped with: |  |
|  | Select cylinder size | - Standard cylinder with mounting plate |  |
|  | 6031 |  | - Standard arm |  |
|  | 6032 |  | - Standard track with bumper |  |
|  | 6033 |  | - Wood and machine screw pack |  |
|  | 6034 |  | unless options listed below are selected. |  |
|  | 6035 |  |  |  |
|  | Specify finish |  |  |
|  | Standard Powder Coat __________ |  |  |
|  | Aluminum, Dark Bronze, Statuary, Light Bronze, Black, Brass |  |  |
|  | Closer options |  |  |

| Track | Installation accessories |
| --- | --- |
| Hold-open with Bumper (HBUMPER) | Wood Clip Set, 6030-416 |
| Finishes |  |
| Custom Powder Coat (RAL)_____________ |  |
| Plated Finish, US ______________ |  |
| SRI primer (use with powder coat finishes only) |  |
| Screw pack | Special template |
| TORX Machine Screw (TORX) | ST- ________ |

Table of sizes

- Select closer based on width of door

- 6030 Series cylinders available in size 1, 2, 3, 4, or 5

- Closing power of all 6030 Series closers may be increased 35%

- Specify next higher size closer where strong drafts exist

Exterior (and Vestibule) door width

| 30˝ | 34˝ | 36˝ | 42˝ |
| --- | --- | --- | --- |
| 762mm | 864mm | 914mm | 1067mm |
| 6033 | size 3 | size 4 | size 5 |
| 6034 |  |  |  |
| 6035 |  |  |  |

Minimum door width

Interior door width

| 30˝ | 34˝ | 38˝ | 48˝ | 54˝ |
| --- | --- | --- | --- | --- |
| 762mm | 864mm | 965mm | 1219mm | 1372mm |
| size 2 | size 3 | size 4 | size 5 |  |
| 6032 |  |  |  |  |
| 6033 |  |  |  |  |
| 6034 |  |  |  |  |
| 6035 |  |  |  |  |

Minimum door width

Indicates recommended range of door width for closer size.

Note: Minimum door width 28˝ (711 mm).

Reduced opening force 6030 Series closers

CAUTION ! Any manual door closer, including those certified by BHMA to conform to ANSI Standard A156.4, that is selected, installed and adjusted based on ADA or other reduced opening force requirements may not provide sufficient power to reliably close and latch a door.

Refer to POWER OPERATORS section for information on systems that meet reduced opening force requirements without affecting closing power.

* Maximum opening force.

| DOOR WIDTH | 36˝ | 42˝ | 48˝ |
| --- | --- | --- | --- |
| 8.5* lbs. | 6033 | 6034 | 6035 |
| 5.0* lbs. | 6031 | 6032 | 6032 |

D32	LCN Door Control Catalog

phone: 877-671-7011	n	fax: 800-248-1460	n	www.allegion.com/us	n	009426	rev. 11/16