30117-05	Rev. 1.4/08-07

LIQUID MEASURING

CONVERSION FACTORS

| MULTIPLY | BY | TO OBTAIN |
| --- | --- | --- |
| Gallons | .1337 | Cubic Feet |
| " | .00000307 | Acre Feet |
| " | .001856 | * Miner's Inch (9 GPM) |
| " | .001481 | * Miner's Inch (11.25 GPM) |
| " | .83267 | Imperial Gallons |
| " | 3.785 | Liters |
| " | .003785 | Cubic Meters |
| " | .0238 | Barrels (42 Gallon) |
| " | .00003683 | Acre Inches |
| Cubic Feet | 7.48052 | Gallons |
| " | .000022956 | Acre Feet |
| " | .01388 | Miner's Inch Hours (9 GPM) |
| " | .01107 | Miner's Inch Hours (11.25 GPM) |
| " | 28.32 | Liters |
| " | .02832 | Cubic Meters |
| Acre Feet | 325,851 | Gallons |
| " | 43,560 | Cubic Feet |
| Acre Inch | 27,154 | Gallons |
| " | 3,630 | Cubic Feet |
| Imperial Gallons | 1.20095 | U.S. Gallons |
| * Miner's Inch | 540.2 | Gallons |
| (9 GPM) | .0016595 | Acre Feet |
| * Miner's Inch | 675 | Gallons |
| (11.25 GPM) | .002079 | Acre Feet |
| Miner's Inch Days | 12930 | Gallons |
| (9 GPM) | 1.729 | Cubic Feet |
|  | .039825 | Acre Feet |
| Liters | .2642 | Gallons |
| " | .03531 | Cubic Feet |
| " | .001 | Cubic Meters |
| Cubic Meters | 264.2 | Gallons |
| " | 35.31 | Cubic Feet |
| " | 1000 | Liters |
| Mega Liters | 264200 | Gallons |
| " | 35323 | Cubic Feet |
| Barrels (42 Gallon) | 42 | Gallons |
| Pound (Water) | .1198 | Gallons |
| " | .01602 | Cubic Feet |
| Tons (long 2240#) | 268.35 | Gallons |
| " | 35.88 | Cubic Feet |
| Tons (short 2000#) | 239.6 | Gallons |
| " | 32.04 | Cubic Feet |

* Miner's Inch (Hours) must multiply by 60.

3255 WEST STETSON AVENUE • HEMET, CALIFORNIA 92545 USA • TEL: 951-652-6811 • FAX: 951-652-3078 www.mccrometer.com

Copyright © 2000-2007 McCrometer. All printed material should not be changed or altered without permission of McCrometer. The published technical data and instructions are subject to change without notice. Contact your McCrometer representative for current technical data and instructions.