EML2322L Decision Matrix Example - Bad

| MOBILE PLAFTORM |  |  | Design 1 |  | Design 2 |  | Design 3 |  | Design 4 | Design 5 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Objective | Weighting | Parameter | Mag. |  | Score | Value | Mag. |  | Score | Value | Mag. |  | Score | Value | Mag. |  | Score | Value | Mag. | Score Value |
|  | Factor |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Speed |  | 0.20 |  | feet | 2.30 |  | 0.0 | 0.0 | 3.10 |  | 6.7 | 1.3 | 2.60 |  | 2.5 | 0.5 | 3.50 |  | 10.0 | 2.0 | 2.30 | 0.0 | 0.0 |
| Controllability |  | 0.30 |  | experience | fair |  | 4.0 | 1.2 | good |  | 8.0 | 2.4 | great |  | 9.0 | 2.7 | poor |  | 2.0 | 0.60 | great | 10.0 | 3.0 |
| Manufacturing Time |  | 0.20 |  | hours | 6.5 |  | 4.23 | 0.8 | 8.0 |  | 6.40 | 1.3 | 10.0 |  | 10.00 | 2.0 | 6.0 |  | 3.60 | 0.7 | 6.0 | 3.60 | 0.7 |
| Modularity |  | 0.20 |  | fasteners | 2 |  | 10 | 2.0 | 3 |  | 7 | 1.3 | 4 |  | 5 | 1.0 | 2 |  | 10 | 2.0 | 2 | 10 | 2.0 |
| Material Cost |  | 0.10 |  | experience | okay |  | 6 | 0.6 | okay |  | 6 | 0.6 | okay |  | 6 | 0.6 | okay |  | 6 | 0.6 | okay | 6 | 0.6 |
| Overall value |  |  |  |  | 4.65 |  |  |  | 6.9 |  |  |  | 6.8 |  |  |  | 5.9 |  |  | 6.3 |
| INSERT PAGE BREAK |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| BALL HOPPER / SORTER |  | Design 1 |  | Design 2 |  | Design 3 |  | Design 4 |  |  |  |
| Objective | Weighting | Parameter | Mag. |  | Score | Value | Mag. |  | Scoer | Value | Mag. |  | Score | Value | Mag. |  | Score | Value |  |  |  |
|  | Factor |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Spead |  | 0.30 |  | … | … |  | … | … | … |  | … | … | … |  | … | … | … |  | … | … |  |  |  |
| Controlability |  | 0.30 |  | … | … |  | … | … | … |  | … | … | … |  | … | … | … |  | … | … |  |  |  |
| Manufacturing Time |  | 0.30 |  | … | … |  | … | … | … |  | … | … | … |  | … | … | … |  | … | … |  |  |  |
| Overall value |  |  |  |  | … |  |  |  | … |  |  |  | … |  |  |  | … |  |  |  |
| Qualitative Score Assignments: |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| great | 10 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| good | 8.6 |  |  |  |  |  |  |  |  | k |  |  |  |  |  |  |  |  |  |  |  |  |
| okay | 6 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| fair | 4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| poor | 2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

Mobile Platform (bad)

Objective Definitinos & Weighting Factor Justifications:

Speed is how fast the robot goes.	Its important because we want our robot to fly through the coarse.

We gave it a score of 20%.

To make sure we can get the balls into the bucket, we need to control the robot with controllability.

If you are reading this circle here.	Other fluff…

Manufacturing Time …

Modularity …

Material Cost …

Score Assignments:

Design 1

Design 1 uses the 44 rpm Entstort right angle gearmotors and 12" diameter drive wheels, which result in a loaded vehicle speed of 2.3 ft/sec (as seen in Appendix A: Wheel Speed Calculations). Since design 1 travels at 66% of the fastest design’s speed (3.5 ft/sec), design 1 receives a score of 6.6 out of 10 using a linear score assignment. As for controllability, design 1 is slow enough that it can be controlled well from what our friends told us. But, since it has four wheels, it isn’t a great design so we gave it a rating of fair and a score of 4.0. Regarding manufacture time…

Design 2

…

.

.

.

Bucket Manipulator

Objective Definitions & Weighting Factor Justifications:

…

Score Assignments:

…

Ball Hopper / Sorter

Objective Definitions & Weighting Factor Justifications:

…

Score Assignments:

…

Appendix A: Decision Matrix Calculations / Summaries

Speeds:

Design 1: 2.3001, Design 2: 3.1015, Design 3: 2.5993, Design 4: 3.5030, and Design 5: 2.3001

.

.

.

Errors in the Decision Matrix Example – Bad

- Are separate matrices used for different parts of the design?

  - Two matrices (rather than the required 3+ matrices) are used.

- Does each matrix contain an appropriate number of objectives?

  - Matrix 2 does not contain sufficient objectives to compare ball hopper / sorter designs. Thus, matrix 2 does not contain an appropriate number of objectives.

- Are different objectives used for different matrices?

  - The objectives in matrix 2 are just copied from matrix one and where not thought through.

- Do weighting factors for each matrix sum to one (or 100%)?

  - Matrix 2 has weighting factors that sum to 0.9

  - Matrix 1 has speed parameterized by feet which is likely wrong.

- Does each objective have a clearly written definition?

  - Objective Definitions: Speed is ambiguously defined. What is the measure of how fast the robot goes? Do you measure the fastness while it is in free fall?

  - Objective Definitions: Controllability is ambiguously defined.

  - Objective Definitions: No discussion is provided for why each objective received its weighting factor.

- Do quantitative objectives use quantitative assessments?

  - Matrix 1 - Material Cost: Material cost will never be qualitative since a quantitative magnitude can be determined using the material cost sheets and online pricing.

- Do all quantitative assessments include clear calculations and results summaries in tabular format?

  - No clear calculations.

  - Result summaries are not in tabular format.

  - Significant figures are not used properly. Speeds are reported (without units) to four decimal places.

  - All information should be justified from material provided to the students (i.e. motor speeds, material costs, and manufacturing time estimates) or from reliable online sources (for example: McMaster-Carr).

- Do qualitative objectives use qualitative assessments?

  - Matrix 1 – Controllability: Design 3 and design 5 have the same magnitude but different scores. This should not be .

  - Matrix 1 – Material Cost: Since all magnitudes are the same, this objective is not contributing to the comparison of the designs and should not be included.

- Does every qualitative magnitude assessment have a clearly written justification?

  - Simply, NO!

- Does every magnitude assessment use linear score assignments?

  - Matrix 1 – Speed: Scores should be assigned as a linear ratio. For example, if design A is the fastest, then any design half the speed of A receives a score of 5. Alternatively, if 3.0 ft/sec is the target speed, any design that runs at 1.5 ft/sec receives a score of 5 and any design that runs at 6 ft/sec receives a 5.

  - Matrix 1 – Manufacturing Time: Score should be assigned as a linear ratio. This objective uses a quadratic score assignment.

- Are quantitative magnitude assessments correct?

  - Matrix 1 – Manufacturing Time: Here, the score assignment is inverted. The lowest magnitude should result in the highest score on objectives like material cost, manufacturing time, and modularity (as defined here).

- Is the design with the highest composite score selected?

  - Matrix 1 does not have the highest scoring design selected. Design 2 should be selected.

- Are new design ideas properly incorporated into the evaluation matrix?

  - Matrix 1: A new design is incorporated into the matrix, however, that design does not score higher than the existing designs and should not be shown.

- Are reasonable and consistent significant figures reported in the matrices?

  - Matrix 1 – Speed: Speed cannot be estimated with an accuracy of one-hundredth of a foot per second. Report speeds to a tenth of a foot per second.

  - Matrix 1 – Controllability: Qualitative evaluations should never be shown with a decimal place since doing so implies that there is a (distinguishable) difference between scores of 7.0 and 7.5. If this level of precision exists, then the objective should be evaluated quantitatively.

  - Matrix 1 – Design 4: The value column should contain consistent significant figures.

  - Matrix 1 – Manufacturing Time: Scores should be reported to one decimal place since the magnitudes are reported as such.

  - Matrix 1 – Overall value: In general, overall values should be reported to one decimal place unless reporting a second decimal place distinguishes two designs tied for first place.

  - Qualitative Score Assignments: A qualitative score assignment of 8.6 is wrong as it implies there is a difference between a score of 8.6 and 8.5. If this level of precision exists, then the objective should be evaluated quantitatively.

- Are grammar and formatting at a collegiate level?

  - Grammar & Spelling

    - Matrix 1: Mobile Platform is misspelled.

    - Matrix 2: Speed is misspelled.

    - Matrix 2: Controllability is misspelled.

    - Matrix 2 – Design 2: Score is misspelled.

    - Objective Definitions: Definitions is misspelled.

    - Objective Definitions: Sentence structure, word use and content are not at a collegiate level.

    - Objective Definitions – Speed: “Its” should be “It’s”.

    - Objective Definitions – Speed: “Coarse” should be “Course”.

    - Score Assignments: Sentence structure, word use and content are not at a collegiate level.

  - Formatting

- If possible, matrices should be printed on a single page.

- Matrix 1: Table boarders should be shown as in the template.

- Matrix 1 – Design 5: The ‘value’ column has been resized.

- Matrix 2: Winning design must be highlighted.

- Matrix 2: Manufacturing time is erroneously in bold.

- Matrix 2: Manufacturing time is too large to fit in the Objective column and is cut off.

- Page: Random ‘k’ should not be present.

- Objective Definitions: Formatting is unclear. It is difficult to see where each objective is defined or even which objective is being defined.

- Objective Definitions: Formatting is inconsistent. Speed is not bold. Modularity is bold.

- Score Assignments: All designs should be discussed relative to each objective, not the other way around (as shown here).

- The content in appendix A should not begin until the page following “Appendix A: Decision Matrix Calculations / Summaries.”