## FEASIBILITY TUDY ON INTELLIGENT MARINE TRAFFIC SYSTEM

Kazuhiko HASEGAWA, Yasuhiro SHIGEMORI and Yuuichiro ICHIYAMA

Osaka University, 2-1 Yamada-oka, Suita, Osaka, 565-0871 Japan

e-mail:hase@naoe.eng.osaka-u.ac.jp

Abstract: Feasibility study on ITS (Intelligent Traffic System) for Marine (Marine ITS) is discussed based on Marine Traffic Simulation System (SMARTS)

## Introduction

For safety of navigation in congested waterways, radar plays an important role. ARPA (Automated Radar Plotting Aids) or ECDIS (Electric Chart Display and Information System) are recently added as additional operational aids.  However, the number of ship casualties doesn't change drastically for these ten years, or number of big disasters such as oil spills rather increased.

On the other hand, rapid progress in Internet, GPS and satellite communication have brought us various changes in technology.  Combining these technologies, we came up to an idea [1].  In this paper, the idea was realized and evaluated through computer network simulation.  The idea was discussed several times at various symposia/conferences or at a journal [2,3,4].  In this paper authors would like to discuss about AIS(Universal ship-borne Automatic Identification System), one of  communication protocol which could realize V-VTS [1].  There are already a few standard protocol for ship management [5].  Now AIS is studied actively in some advanced countries for its introduction forward safe navigation fields.  To verify its roles and usefulness, simulation is conducted by using SAFES [6] and SMARTS [7]. The results of simulation would show follows item. 1) Verification of AIS to be implemented 2) Usefulness of SAFES and SMARTS and finally 3) the above 2 items will support the feasibility of V-VTS.

2. Universal AIS(Automatic Identification System)

Now IMO is trying to standardize criterion of Universal AIS.  As you know AIS is now studied and has been studied in many advanced country as a tools to exchange information in both ship-to-ship and ship-to-shore in congested waterways.  The intention of standardization is to improve safety of VIS management and to support effective navigation of ships. For example, avoiding of collision, tools of VTS, sending cargo information to ships and to local center, automatic flow of ship's information, etc.  Fig. 1 shows the concept of Universal AIS.  The AIS of ship A sends the message in one time slot. At the same it reserves another time slot for next position message. All other AIS-equipped ships repeat the same procedure. Here one time slot should contents available information required by IMO standard such as ship name, speed, etc.

2.1 Standard information

Even though the concept and intentions of AIS is very great, the process of standardization is required to utilize it more effectively in the world.  So IMO require that follows information should be included in AIS message.

1) Static information; IMO number, call sign, height and width, ship type, position of antenna. 2) Dynamic information; ship's position, standard time, heading angle, course on ground, speed, rate of turn, etc. 3) Navigation information; draft, type of cargo, departure and destination, waypoint etc. 4) Safety message.

All ship under AIS system should report above information to center at regular intervals.  The reporting time depends on the situations of navigation.  The details of information to be reported and interval are as follows. 1) Static information - every 6 minutes or when requested. 2) Dynamic information – it depends on ship’s speed and status; berthing - 3mins, below 14kts - 12secs, from 14 to 23kts of speed - 6secs, above 23kts - 3secs, below 14kts(when altering course) - 4secs, from 14 to 23kts(when altering course) - 2secs, 23kts(when altering course) - 2secs. 3) Navigation information - every 6 minutes or when requested. 4) Safety message - when requested.  These standardized data make it possible to get other ship’s information and to send it to shore side.

2.2 AIS and V-VTS

The V-VTS is regarded as a database accessible from the network.  Fig. [5] show concept of V-VTS.  Each ship will access the V-VTS through a web browser such as Netscape or Internet Explorer.  The own ship is displayed in the center and other ships are shown with their plan paths and present velocity vector.  It will be helpful to ship master to provide these data without any manual operation or communication.  The above idea is almost same to that of AIS of which purpose is to provide ship and shore with useful ship information.  AIS can be one of communication protocol in V-VTS. Each ship equipped with AIS should report their information via VHF to share　with each other.  When one or many virtual server is located in VIS to collect ship report and to re-send them by request of ship, it will be one type of V-VTS.  It is considered that AIS is useful tools in building up V-VTS.  In this paper simulation is conducted to check the feasibility of Intelligent Marine Traffic System using AIS.

- Simulation

The marine traffic simulation system (SMARTS) [6] was developed using ship auto-navigation fuzzy expert system (SAFES) [7]. It can automatically create marine traffic according to the statistical data etc. The statistical data of Osaka port is utilized. The data refered to various survey on marine traffic of long term Osaka bay by the Kobe Marine Accidents Inquiry Agencies. To realize traffic situation of Osaka bay, following procedure is used. 1) Set destination and departure port of every ship. 2) Determine time interval of ship's emerging 3) Set route on sea including waypoint 4) Set parameter of ship. 5) Navigation automatically.  In Osaka bay, there are many small ports. Author limited these ports to 6 categories for simplification.  The ship's emerging time interval refers to two report of "The report on ship's navigation status in osaka bay" and "The report on navigation status”.  Route and waypoint is obtained by "Information on sea traffic by Japan hydrography" and "Report by Japan captain association".  Fig [2] shows Osaka bay used in simulation and Fig [3] shows one of actual display of simulation.

4. Results of simulation

24 hours of time are simulated by marine traffic simulation system to check the number of AIS report in Osaka bay.  Fig [4] shows total number of report and ship under AIS.  We can find that 1) the report number has not so many relations with altering course. 2) Total report number is almost 5 times than the number of ship underway.  It has relations with the fact that report number at below 14kts is 5 per minute. 3) The most peak value of report is 1200 per minute.  It satisfies the IMO criterion, 2000 report per minute, at least on simulation with simulated circumstances.

5. Conclusions

Until now author has proposed new concept to realize intelligent marine traffic system using virtual vessel traffic service (V-VTS).  This paper will be one story of that flow.  In this paper AIS is simulated to estimate total report number in Osaka bay and to confirm whether its number satisfy IMO standard.  Originally AIS was started with both ship-to-ship and ship-to-shore mode.  But as mentioned in body, in virtual world ship-to-shore mode can be replaced with ship-to-virtual server mode.  It will be one example of V-VTS.  The main conclusions will be drawn as follows.

1) The number of AIS report in Osaka bay is estimated by simulations.

2) The number of AIS report in Osaka bay satisfied the IMO standard criterion.

3) Total report number is almost 5 times than that of ship on sea.

4) The concept of Internet radar and intelligent marine traffic system using virtual vessel traffic service (V-VTS) proposed by the author is realized by using AIS.

## References

[1] K. Hasegawa: A proposal of global ship information system and its application to automatic ship collision avoidance system, Proc. Of Eleventh Ship Control Systems Symposium, Vol2, pp. 197-210, Southampton, U.K., 1997

[2] K. Hasegawa and K. Taniguchi: Internet Radar and Virtual Vessel Traffic Service, Proc. Of 2nd Conference for New Ship & Marine Technology into the 21st Century, pp.336-339, Hong Kong, China, 1998.

[3] K. Hasegawa: Internet Radar and Intelligent Vessel Traffic Service, oral presentation at the Special Session of Intelligent Marine Systems, 14th IFAC World Congress, Beijing, China, 6-9, July, 1999.

[4] M. Endo and K. Hasegawa: Systemization of Ship Operation – For the Cooperation between Seamen, Ship and Environment (First and Second Report) (in Japanese), Sea and Safety, pp.8-15, No.483, pp.10-15, No.484, 1999.

[5] Mits:URL http://www.itk.ntnu.no:80/SINTEF/MITS/.

[6] K. Hasegawa : An intelligent marine traffic evaluation system for harbour and waterway designs, Proc. of 4th International Symposium on Marine Engineering Kobe ’90 (ISME KOBE ’90), Vol.2, G-1-7 ―14, Kobe, Japan, 1990.

[7] K. Hasegawa: Knowledge-based automatic navigation system for harbour manoeuvring, Proc. of Tenth Ship Control Systems Symposium, Vo.2, 67-90, Ottawa, Canada, 1993.

Fig. 1 Concept of universal AIS 		Fig.2 picture of Osaka bay used in simulation

Fig. 3 Real snap display of simulation 		Fig. 4 The number of AIS Report and ships

???????????????????????????????????????????????????????

Fig. 5 Concept of V-VTS