Engineering Requisition

for Equipment / Services Form

SECTION 1 – ADDITIONAL INFORMATION

1.1	SCOPE OF SUPPLY

Supply of Valves including required documentation, mandatory testing requirements and packaging for sea and road transport.

The Supplier is responsible to furnish equipment and accessories of a sound mechanical design in accordance with good working practices to meet the design conditions as specified.

Drawings and mechanical data sheets shall be submitted to the client for approval prior to commencement of valve manufacture.

It is preferable for Gearbox Housings to be made from Cast Steel (as opposed to Cast Iron).

Trunnion mounted ball valves shall be supplied with approved grease fittings in accordance with 0000-TS-L006 for seat injection and stem injection. 6” and 8” valves shall have 1 fitting per seat. 10” valves and above shall have 2 fittings per seat. 4” valves and above shall have a stem grease fitting for lubrication of the stem.

All ball valves shall be supplied with Fire Safe Certificates in accordance with 0000-TS-L006.

All materials for pressure components shall be supplied with material certificates in accordance with Type 3.1 of BS EN ISO 10204.

1.2 APPLICABLE CODES, STANDARDS AND SPECIFICATIONS In accordance with 0000-TS-L-0006 and 0000-TS-L0007.

Manufacturers shall have ISO 9000 accreditation confirming manufacture is in accordance with specified goods and material descriptions.

1.3	SPECIAL REQUIREMENTS FOR INSPECTION AND TESTING

In accordance with documents listed in Section 2 of this requisition, and the following additional requirements;

- Drawings and mechanical data sheets shall be submitted to the client for approval prior to commencement of manufacture or dispatch from Vendor’s Shop.

- Valve Castings: ASME Class 900, 1500 and 2500 valve bodies, including flanges, shall be inspected as per the requirements of Specifications 0000-TS-L006.

- In addition to the requirements of API-598/API-6D any valve bodies (cast or forged) manufactured in China or India shall be subject to an extended hydrostatic shell test duration of 10 minutes.

- Inspection level: Final inspection of goods and documentation at Supplier’s works prior to dispatch.

- No goods shall be dispatched from Supplier without an inspection release note.

Quality Assurance AS/NZS ISO 9001

Supplier shall apply a quality system that complies with the requirements of AS/NZS 9001 and is currently certified as complying with that standard by a recognised Third Party.

QA Documentation that the Supplier will be required to submit after award of purchase order is detailed in the Supplier Data Requirement Form.

Company, and or representative of Company, shall have all reasonable right of access to Supplier’s, and where applicable to Supplier’s sub-contractor’s, offices and works, for verification, inspection and expediting of any aspect of the manufacturing program.

Page 1 of 4

G:\360\2008\00479 - Technical Evaluation of LLI\13.0 Procurement\Valve Requisition.doc

|  |  |  | Engineering Requisition |  |
| --- | --- | --- | --- | --- |
|  |  |  | for Equipment / Services Form |  |
| SECTION 2 – SUPPLIER DATA REQUIREMENTS FORM |  |
| Part 1 – Information Required with Quotation |  |
| To be read in conjunction with instructions in Section 1 |  |
|  | Item |  | Description |  | Required |
| 1 |  | Compliance Statement (see below) |  |  |
| 2 |  | Supplier Drawing and Data Index |  |  |
| 3 |  | Manufacturing / Delivery Schedule |  |  |
| 4 |  | Uncontrolled Copy of Quality Assurance Manual Or current ISO 9001 Certification by |  |  |
|  |  | Third Party |  |  |
| 5 |  | Quality Plan |  |  |
| 6 |  | Safety Plan |  |  |
| 7 |  | Sample Inspection and Test Plan |  |  |
| 8 |  | General Arrangement Drawing(s) |  |  |
| 9 |  | Shop Detail Drawing(s) |  |  |
| 10 | Assembly Drawings(s) |  |  |
| 11 | Cross Section Drawing(s) |  |  |
| 12 | Dimensioned General Outline Drawings |  |  |
| 13 | Calculations |  |  |
| 14 | Sample Weld Procedures |  |  |
| 15 | Complete Parts List |  |  |
| 16 | Quotation for Special Tools |  |  |
| 17 | Priced Spare Parts for Start-up and Commissioning |  |  |
| 18 | Complete Data Sheets / Descriptive Literature |  |  |
| 19 | List of Previous Experience with Similar Work / Projects |  |  |
| 20 | Recommendation for Operating Spares (for 2 years) |  |  |
| 21 | Hazardous Area Certificates of Conformity |  |  |
| 22 | List of proposed Sub-Vendors, Manufacturing Locations and Country of Origin for all |  |  |
|  |  | key valve components including castings and forgings. Note: It must be made |  |  |
|  |  | explicitly clear at the tender stage if any components will be supplied from China |  |  |
|  |  | or India. |  |  |
| 23 | Additional information to be provided per Section 6.0 of Specification 0000-TS-L006 |  |  |
|  |  | and 0000-TS-L007 |  |  |
| 24 | Valve Type Test Fire Rating Certificate |  |  |
| 25 |  |  |  |  |
| 26 |  |  |  |  |
| 27 |  |  |  |  |
| 28 |  |  |  |  |

This Supplier / Sub-contractor shall supply a Compliance Statement that confirms complete compliance with the Requisition and referenced documents or lists specific deviations and exceptions.

Page 2 of 4

G:\360\2008\00479 - Technical Evaluation of LLI\13.0 Procurement\Valve Requisition.doc

Engineering Requisition

for Equipment / Services Form

SECTION 2 – SUPPLIER DATA REQUIREMENTS FORM

Part 2 – Information Required After Award of Purchase Order

To be read in conjunction with instructions in Section 1

The Supplier or his authorised representative shall sign and return this page with the tender to show compliance with the Supplier data requirements.

Name

Company

Date

Signature

|  |  |  |  |  |  | Required |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | Item | Description No |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  | Approval / Info |  |  |  |  | Certified |  |
|  |  |  | No | Type | A/I |  | Wks |  | No | Type |  | Wks |
|  |  | QA / Inspection & Testing |  |  |  |  |  |  |  |  |  |  |
| 1 | Supplier Drawing and Data Index | 1 | E | A |  | 1 |  | 1 | E & P |  | 2 |
| 2 | Manufacturing / Delivery Schedule | 1 | E | A |  | 1 |  |  |  |  |  |
| 3 | Quality Assurance / Safety Plan |  |  |  |  |  |  |  |  |  |  |
| 4 | Inspection & Test Plans | 1* | E | A |  | 1 |  | 1 | E & P |  | Note 4 |
|  |  | Engineering & Design Documents |  |  |  |  |  |  |  |  |  |  |
| 5 | Piping and Instrument Diagrams |  |  |  |  |  |  |  |  |  |  |
| 6 | General Arrangement Drawing(s) | 1* | E & P | A |  | 2 |  | 1 | E & P |  | In MDR |
| 7 | Shop Detail Drawing(s) |  |  |  |  |  |  |  |  |  |  |
| 8 | Assembly Drawing(s) | 1* | E & P | A |  | 2 |  | 1 | E & P |  | In MDR |
| 9 | Cross Section Drawing(s) | 1* | E & P | A |  | 2 |  | 1 | E & P |  | In MDR |
| 10 | Vessel Detail Drawing(s) |  |  |  |  |  |  |  |  |  |  |
| 11 | Tie-in Schedule |  |  |  |  |  |  |  |  |  |  |
| 12 | Vessel Calculations |  |  |  |  |  |  |  |  |  |  |
| 13 | Process Calculations |  |  |  |  |  |  |  |  |  |  |
| 14 | Mechanical Data Sheets | 1* | E & P | A |  | 2 |  | 1 | E & P |  | In MDR |
| 15 | Instrument Data Sheets |  |  |  |  |  |  |  |  |  |  |
| 16 | Electrical Single Line Diagram(s) |  |  |  |  |  |  |  |  |  |  |
| 17 | Electrical Schematic Diagram(s) |  |  |  |  |  |  |  |  |  |  |
| 18 | Electrical Wiring Diagram(s) |  |  |  |  |  |  |  |  |  |  |
| 19 | Electric Motor Details |  |  |  |  |  |  |  |  |  |  |
| 20 | Instrument Schematic Diagrams (inc. JBs & |  |  |  |  |  |  |  |  |  |  |
|  | Panels) |  |  |  |  |  |  |  |  |  |  |
| 21 | Instrument Layout Diagrams |  |  |  |  |  |  |  |  |  |  |

Page 3 of 4

G:\360\2008\00479 - Technical Evaluation of LLI\13.0 Procurement\Valve Requisition.doc

|  |  |  |  |  |  | Engineering Requisition |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | for Equipment / Services Form |  |
|  |  |  |  |  |  |  |  |  | Required |  |  |  |  |
|  | Item | Description No |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  | Approval / Info |  |  |  |  | Certified |  |
|  |  |  |  |  |  | No | Type | A/I |  | Wks |  | No | Type |  | Wks |
| 22 | Instrument Connection Diagrams (inc. JBs) |  |  |  |  |  |  |  |  |  |  |  |
| 23 | Hazardous Area Certificates |  |  |  |  |  |  |  |  |  |  |  |
| 24 | Weight Calculations |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  | Other Documents |  |  |  |  |  |  |  |  |  |  |  |
| 25 | Weld Procedures |  |  |  |  |  |  |  |  |  |  |  |
| 26 | Material Test Certificates (Mech & Inst) |  |  |  |  |  |  |  | 1 | E & P |  | In MDR |
| 27 | Certificate of Compliance – NACE, etc |  |  |  |  |  |  |  | 1 | E & P |  | In MDR |
| 28 | Complete Parts List |  |  |  |  |  |  |  | 1 | E & P |  | In MDR |
| 29 | List of Special Tools |  |  |  |  |  |  |  |  |  |  |  |
| 30 | Spare Parts List |  |  |  |  |  |  |  | 1 | E & P |  | 2 |
| 31 | Commissioning Spares |  |  |  |  |  |  |  | 1 | E & P |  | 2 |
| 32 | Installation, Operation and Maintenance |  |  |  |  |  |  |  | 1 | E & P |  | 2 |
|  | Manuals |  |  |  |  |  |  |  |  |  |  |  |
| 33 | Performance Test Reports / Hydrotest Reports |  |  |  |  |  |  | 1 | E & P |  | In MDR |
| 34 | Manufacturer’s Data Report (MDR) |  |  |  |  |  |  |  | 1 | E & P |  | Note 4 |
| 35 | Recommendation for Operating Spares |  |  |  |  |  |  |  | 1 | E & P |  | 2 |
| 36 | NDT Reports (Radiographic, Ultrasonic, etc) |  |  |  |  |  |  |  | 1 | E & P |  | In MDR |
| 37 | Heat Treatment Records |  |  |  |  |  |  |  | 1 | E & P |  | In MDR |
| 38 | Valve Type Test Fire Rating Certificates |  | 1* | E & P | A |  | 2 |  | 1 | E & P |  | In MDR |
| 39 | Painting / Coating Test Reports |  |  |  |  |  |  |  |  |  |  |  |
| 40 | Valve breakaway torque figures at maximum |  |  |  |  |  |  |  | 1 | E & P |  | In MDR |
|  | DP |  |  |  |  |  |  |  |  |  |  |  |
|  | Note: |  |  |  |  |  |  |  |  |  |  |  |  |  |

- Submittal of any of the above listed drawings on CAD diskettes will be acceptable ONLY with prior approval.

- These items to be submitted pre-delivery.

- These items may be submitted post delivery two (2) weeks.

- These items to be submitted at time of goods dispatch.

Legend:

* = Critical Data	P = Print

A = Approval	T = Transparency

I = Information	E = Electronic Copy

Wks = Working Weeks After Award of Purchase Order

Page 4 of 4

G:\360\2008\00479 - Technical Evaluation of LLI\13.0 Procurement\Valve Requisition.doc